## Slide 1
Broadcast Technology
From SDI to IP workflows;
and from DAB to DASH distribution
Jerry Foss
jeremy.foss2@bcu.ac.uk

## Slide 2
This Session …
Production
Distribution
(Analogue/historical)
Digital
SDI Workflows
(inc NDI)
IP Workflows
SMPTE 2022 SMPTE 2110
PTP
Analogue Terrestrial,
…. Cable TV,
…. CATV (community antenna (US))
…. Satellite
Digital
DVB –
Terrestrial – DVB-T / T2
Cable TV – DVB-C / C2
Satellite – DVB-S / S2
Telco Broadband
  – DVB-I (IPTV)
DAB Radio
Web
http (HLS, DASH)
  inc mobile 5G, 6G, etc
5G, 6G,
etc
(Web, downloads, etc)
This lecture will address the red topics as an introduction and in a context in this evolution of the broadcast industry.

## Slide 6
0.07B’
BT.601 standard
BT.709 standard
Luma encoding formula:

## Slide 7
The Luma signal (Y’)

## Slide 8
Chroma sub-sampled bandwidths
The Chroma signals (CR, CB)
Chroma sub-sampling - Revision

## Slide 10
Encoding additional data in the signal
Line 1
Line 2
Line 3
Line blanking, sync and HANC data
Line blanking, sync and HANC data
etc …
Vertical sync and VANC data

## Slide 11
Encoding additional data in the signal – HANC and VANC

## Slide 12
ITU-R BT.601 sampling rates at 13.5 MHz for 4:3 video gives 704 active pixels per line.
i.e. a raw capture at 720 samples / line cropped to 704 samples to fit the 4:3 aspect ratio
Video Line (10b words)
4 word SAV
ADF = Ancilliary Data Flag
SDI SMPTE Primer

## Slide 13
tri-level sync

## Slide 14
to reduce long strings of 1’s or 0’s
see next slide

## Slide 15
compare to RTZ

## Slide 16
Why IP is replacing SDI*
for example …
Universal connectivity (broadcast and other industries)
Lower budgets, higher quality requirements
Production companies scaling:
  IP allows production personnel to remain in a central location
  Receive feeds from remote locations
Democratise the industry
  single producer can have many camera inputs from anywhere in the world
  * although SDI is still in development
IP Workflows

## Slide 17
ST 2110 – Essence-Based Approach
Designed from the ground up - separates video, audio and ancillary data
Flexibility: route and process streams independently
allows SDI ⇨SMPTE 2022-6 when necessary
The Move to IP: SMPTE 2022, 2110
SMPTE ST 2022-6 - IP Packetisation of SDI Raster
mapping SDI onto IP
i.e. the early stages of the shift from SDI

## Slide 18
Bundled (Audio, Video, Metadata together)
Audio/Video/Metadata/Sync travel coherently
Requires extra work to “unpack” separate essences
SMPTE ST 2022-6
- IP Packetisation of SDI Raster
One IP Address
Video
+ Audio
+ ANC Metadata

## Slide 19
Essence Based (Audio, Video, Metadata separate)
Suited for Studio/Production workflows
Individual essence kept in sync using PTP timing
No blanking!
ST 2110
– Essence-Based Approach
IP Address #1
Video
IP Address #2
Audio
IP Address #3
Metadata
IP Packetisation of Active Video
IP Packetisation of Audio Channels
IP Packetisation of ANC Data
IETF RFC 4175
AES-67
IETF ANC291

## Slide 20
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
Traditional Broadcast and Media Routing

## Slide 21
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
IP World of Broadcast and Media Routing
Note – SDI and IP in path from 2022 - 2110

## Slide 22
SDI
Receiver requests multicast
Control System tells Receiver:
  Multicast Group & Port#
  Technical Metadata of the new stream
Receiver is responsible for how it switches/transitions to it
Receiver asks the network for the new signal
Network sends data via packet forwarding logic
IP
SDI vs IP Video Routing
Multicast source
Receiver host
All routing via SDI crosspoint frame
what to switch where
switches everything internally
receivers receive all data sent to them

## Slide 23
COTS and IP Video Routers
IP Video Routers
High bandwidth - > 130Tb/s, > 60B packets/s
Non Blocking – router internal bandwidth can handle all port traffic simultaneously at full capacity
IGMP to establish multicast groups
PIM-SSM (Protocol Independent Multicast, Source Specific Multicast) – allows a client receive multicast traffic direct from source

## Slide 24
SMPTE ST 2022-6 (Multiplexed Streams)
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017

## Slide 25
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
SMPTE ST 2110 – Essence Streams

## Slide 26
SMPTE ST 2022-6 and TR-03 / ST 2110
https://www.tvtechnology.com/opinions/new-standard-for-studio-video-over-ip-approved
Proven technology across multiple industries (IEEE 1588)
common clock distributed to every node on the network
Can replace Black Burst, or work alongside it
Enables time alignment of separately transported essences
Precision Time Protocol (PTP)
Issue -
propagation delays in the Ethernet
processor queuing, IP message creation and latency
PTP
protocol messages sent between PTP nodes
clock offsets; delays in the network

## Slide 27
OTT Coder
OTT Coder
OTT Coder
Internet
Tx Encoder
Off Air Rx
Decoder
PTP
Rx Decoder
WAN Codec
Telco
Multiviewer Monitoring
Timing Reference
Graphics System
Vision Mixer
Sound Mixer
Record replay
Publish/Playout
Master Control
VSF TR-01
2022-6
2022-6
2110-40
2110-30
(AES 67)
2110-30
(AES 67)
2110
MPEG DASH
2022-6
2022-2
2022-6
2022-2
Example IP Media Facility
Ancillary Data
2110-20
2110-20
2110-20
IEEE 1588

## Slide 28
DVB
Digital TV Distribution …

## Slide 29
DVB - Digital Video Broadcasting
Standards
Satellite DVB-S, DVB-S2, SH
Cable DVB-C, DVB-C2
DTT DVB-T, DVB-T2
DTT for handhelds DVB-H, DVB-H2
IPTV DVB-IPTV
DASH DVB-DASH
DVB-3DTV - Frame Compatible Plano-Stereoscopic 3DTV
DVB-C2 - 2nd Generation Cable Transmission
DVB-CID - Carrier Identification for Satellite Transmission
DVB-CPCM - Content Protection and Copy Management
DVB-FF - DVB File Format
DVB-GEM - Globally Executable MHP
DVB-GSE - Generic Stream Encapsulation
DVB-H - Broadcasting to Handheld Devices
DVB-IPDC - Internet Protocol Datacasting
DVB-IPTV - Internet Protocol Television
DVB-MHP - Open Middleware for Interactive TV
DVB-PCF - Portable Content Format
DVB-RCS2 - Return Channel Satellite
DVB-RCT - Return Channel Terrestrial (03/2001)
DVB-S2 - 2nd Generation Satellite Broadcasting
DVB-SH - Satellite Services to Handheld Devices
DVB-T - Digital Terrestrial Television
DVB-T2 - 2nd Generation Terrestrial Broadcasting
DVB - Emergency Warning System
DVB Project - An Introduction
Hierarchical Modulation in DVB-T (03/2000)
plus many others (inc addenda, etc) …
Industry Organisation
Standardisation Process –
Joint Technical Committee (JTC) of:
ETSI - European Telecommunications Standards Institute
CENELEC - European Committee for Electrotechnical Standardization CENELEC
EBU - European Broadcasting Union
Note standards refer to other standards and patents, e.g. MPEG
http://www.dvb.org/standards/factsheets

## Slide 30
Digital Terrestrial TV (DTT)
Advanced Television Systems Committee - ATSC-8VSB
Modulation: 8VSB: 8-level Vestigial Sideband
American Continent
MPEG2-TS
Digital Video Broadcast, Terrestrial Television - DVB-T
Europe; also DVB-S for Satellite, DVB-C for Cable; DVB-H for handhelds
MPEG2 format; also
Integrated Services Digital Broadcasting, Television - ISDB-T
Japan; also ISDB-S for Satellite, ISDB-C for CableTV
MPEG2 format
Modulation: PSK, COFDM/PSK/QAM

## Slide 31
DVB Specifies …
Specifies - essentially a layer one protocol for transport with Data Link (Transport Streams, GSE, etc)
Including -
Input Interface
usually Transport Streams - i.e. TV
Generic Stream Encapsulation – e.g. IP
Modes
Variable Coding and Modulation
Adaptive Coding and Modulation
FEC
e.g. DVB-T2: LDCP, BCH ½. 3/5. 2/3. ¾. 4/5. 5/6
Modulation
e.g. DVB-T2: OFDM
Modulation Schemes
Q/8/16/32PSK, QAM
e.g. DVB-C2: 16-4096QAM
Guard Interval
e.g. DVB-T2: 1/4, 19/256, 1/8, 19/128, 1/16, 1/32, 1/128 (fractions of a symbol)
Interleaving
Bit- Time- and Frequency-Interleaving

## Slide 32
Transport Stream Multiplex
Transmission:
Terrestrial
Cable
Satellite
Broadband
Program Streams

## Slide 33
Distribution Network Architectures
These are the SMPTE colour bars, used for monitor calibration
See this from Bruce Devlin about SMPTE standards
https://www.smpte.org/top-standards
… there are many standards bodies involved in the media industry …
MPEG, DVB, DTG, ITU, AMWA, DPP, ETSI …
… and many others

## Slide 34
Distribution Network Architectures
headend
End user premises
modem/router
distribution network
WWW
edge network
ingest or other content acquisition
e.g. -
Terrestrial
Cable
Satellite
IPTV

## Slide 35
Digital Terrestrial
TV
(DTTV,
e.g.
Freeview)

## Slide 36
Digital Terrestrial TV (DTTV, e.g. Freeview)
475MHz
850MHz
Ch21
Ch68
48 channels
UHF Band IV, V
7Mhz Channel
contains a number of DVB-T TV channels

## Slide 37
Freeview – Sutton Coldfield Transmissions (9 Multiplexes altogether)

## Slide 38
Digital Terrestrial TV (DTTV, e.g. Freeview)
475MHz
850MHz
    – a transport stream modulated on many carriers
Ch21
Ch68
48 channels
UHF Band IV, V
7Mhz Channel
contains a number of DVB-T TV channels

## Slide 39
Multiplexing the Channels
freq
Data is modulated on to each of several carriers
Total data to be transmitted
00100010010101011110010010001001010101110010011001010100010100000.........
Each of these is one carrier with data modulated on to it in Quadrature Amplitude Modulation
(QAM – a mix of amplitude and phase modulation)
All these carriers are separate signals
A
Ch1
V
Ch1
V
Ch3
V
Ch4
V
Ch3
D
Ch2
SI
Ch1
V
Ch1
V
Ch4

## Slide 40
Satellite Distribution
image from
http://upload.wikimedia.org/wikipedia/en/8/80/Sat_contribution_fig.jpg
Video Headend

## Slide 41
Satellite TV
DBS - Direct Broadcast Satellite; Broadcasting Satellite Service
One-way broadcast
From a communications satellite to an end user
Uplink: large dish 9-12m dia
Receiver - Small round or oval dish antenna < 20" diameter.
Compressed digital signal in the Ku band
  (11-15GHz)
http://www.supersatelliteselection.com/how-satellite-tv-works.html
Reception affected by
  rain
  solar activity

## Slide 42
Geostationary Orbit
appears as a fixed position to an earth-based observer
revolves around the earth at a constant speed once per day over the equator
ground based antennae - no need for expensive tracking equipment
36,000 km
= 22,250 miles
Some satellite data …
SES Astra satellites located at 28.2° east (Astra 2A/2B/2C/2D)
Eutelsat's Eurobird 1 satellite at 28.5°E
receiver dish parameters

## Slide 43
Satellite Transponders
24 x 36MHz channels in 6GHz band
24 x 36MHz transmission channels in 11GHz band
Each Transponder is a separate transceiver or repeater
Each transmission channel is a multiplex of several digital TV channels
(note – bigger transmission channels than DTT
∴ many more TV channels in each multiplex)
http://www.dream.com.ph/howdreamworks/hwd_schematic.asp

## Slide 44
Feeder Horn
LNB Unit
LNB - Low Noise Block
Superheterodyne principle next slide …
Receives wide band of relatively high frequencies ...
Amplify and convert them to much lower frequency - intermediate frequency, IF
  IF: 900 – 2100 MHz)
Lower frequencies - much less attenuation in cables on user end
Easier and cheaper circuit design for lower frequencies
Signal is polarised in horizontal or vertical plane
LNB: waveguide with H / V detector

## Slide 45
Cable TV

## Slide 46
Hybrid networks:
fibre's reliability and bandwidth benefits
lower cost than a pure fibre network
utilising existing copper plant
HFC network - hybrid fibre-coax network
Combine both optical-fibre and coaxial cable lines.
TAP
TAP
TAP
Fibre Trunk
Coax Trunk
Router
Drop
Branch
Headend
Cable TV
Coaxial cable
- from the optical-fibre feeders to each subscriber's home.
Optical fibre
- from the cable head-end to neighbourhoods of 500 to 2,000 subscribers.
Network Economics!!
Where to install fibre or coax?
When to replace coax with fibre?
  Cost of build (equpt and labour) ?
  What additional services/revenues ?
Notes: -----------------------------------------
>> CMTS

## Slide 47
DOCSIS - Data Over Cable Service Interface Specification
The Standard for the interface between the CMTS and the Cable Modem
Developed and licensed by CableLabs
Specifies modulation schemes and protocol
for exchanging signals over cable
to carry MPEG and IP
Interface
DOCSIS
Data
Cable TV – Data and TV to the user

## Slide 48
Telecomms Service Providers (Telco)
Broadband Access

## Slide 49
Telephony
UPSTREAM
DOWNSTREAM
Initially - ADSL, XDSL via twisted pair cable
sub-channels
freq
signal
Telco Broadband Access
… but (increasingly) Ethernet over fibre

## Slide 50
WWW
Middleware
VOD Server
Broadcast
Video Head-End
PSTN
Public Service Telephone Network
IP Router
Network
DSLAM
Digital Subscriber’s Line Access Module
Customer Premises
Telco Broadband (IPTV)
Router (+WiFi)
FTTC
Notes: IP services
>>>> - SSw
>>>> - www
>>>> - Walled Garden
>>>> - video headend
>>>> Network
- (MSAN)
IP Router
- ASX4000, BXR 48000
>>>> B-RAS
migrate to edge - to MSAN
[more later]
---------------------
Second Mile - Ethernet

## Slide 51
Walled Garden
WWW
Middleware
VOD Server
Broadcast
Video Head-End
PSTN access
IP Router
Network
DSLAM
Customer Premises
bRAS
Ethernet
Fibre
Street
Cabinet
Router (+WiFi)
Mobile N/W
FTTH
FTTP

## Slide 52
Streaming
HTTP, HLS
  MPEG-DASH
RTP/RTSP

## Slide 53
HTTP overtaken by RTP/RTSP systems for large IPTV deployments
  Real Time Protocol
    using Real Time Streaming Protocol requests
  this needs a fairly well engineered architecture including firewalls which pass RTP traffic
  HTTP more recently back in favour
uses generic HTTP servers (often based on Apache or Windows Server)
HTTP Streaming
Early days of HTTP media distribution
Limited bandwidth available
    “Download and play”
        no lookahead seeking or random access
      Multiple viewers – server bandwidth issues

## Slide 54
Streaming Media Protocols – HTTP addresses RTMP Issues
RTMP/RTSP/HTTP for distribution to viewers - state of the market
little impetus for RTMP/RTSP sites to change –still widely used
widely used in IP production workflows
But … for distribution to end users - overwhelming view – HTTP
  (in fact most video content is delivered via plain old HTTP progressive download)

## Slide 55
HTTP server/client – stateless
  HTTP-ABR streaming: retrieves consecutive short chunks on as-needed basis
      little waste (the video is delivered as it is watched)
          server efficiently serves more streams
      Random seeking
        (viewer selects – player retrieves the appropriate chunks)
    firewall friendly
    can utilise HTTP caching mechanisms
    less expensive to implement (no streaming server required)
      scale more cheaply and effectively to serve available users
How can we use HTTP for streaming? … Adaptive Bit Rate (ABR)

## Slide 56
Client
Server
http GET
http GET
Segment timing:
10 seconds = reasonable balance for most broadcast content
Shorter segments
= more frequent refreshes of the index file
.. unnecessary network overhead for the client
Longer segments
= latency and initial startup time
Media Formats
e.g. video: H.264/5
  audio: .aac / Opus, etc
  video + audio file segments unwrapped
  … but certain applications –
  can be wrapped in MPEG-TS (DVB)
Audio segment
Video segment
etc
HTTP Streaming – now Adaptive bit-rate (ABR)
index file

## Slide 57
HTTP Live Streaming - HLS (DASH is similar)
Apple (part of QuickTime and iOS)
HLS current version is 7.0

## Slide 58
MPEG-DASH
Dynamic Adaptive Streaming over HTTP
http://www.streamingmedia.com/Articles/ReadArticle.aspx?ArticleID=79041
Background
HTTP streaming is OK - provided that the increased latency is acceptable
Benefits:
Firewall and NAT traversal
  (c.f. services based on RTP/UDP)
Widely deployed network caches (CDNs)
  Deployment of CDN caches can be kept simple
Complexity (adaptation) moved to client
Servers are agnostic to delivered content
network resources / configuration may vary over time

## Slide 59
MPEG-DASH
Content exists on the server in two parts:
Media Presentation Description (MPD)
    content presentation types
    various alternatives
    URL addresses, etc
Streaming content
from HTTP server
to a DASH client
content stored on HTTP server; delivered using HTTP
Media Segments
  contain the content bitstreams
  chunks, single or multiple files

## Slide 60
MPEG-DASH
DASH client obtains the MPD …
Media
Presentation
Description
… an XML document
  The MPD:
  delivered using HTTP or other transport
describes media data available at the servers
allows clients to select the data
defines segments available
can either be
  initialization segments - initialization data for decoding
  the actual media segments
  Uses ISO base Media File Format (ISOBMFF - general structure for time-based media
    however, segments based on other formats can be specified

## Slide 61
MPEG-DASH
Then DASH client selects the appropriate encoded
… starts streaming content using HTTP GET requests to fetch segments
  media-component locations on the network
  other content characteristics
DASH client learns about -
  program timing
  media-content availability
  media types
  Resolutions
  minimum and maximum bandwidths
  the existence of various encoded alternatives of multimedia components
  accessibility features and required digital rights management (DRM)

## Slide 62
MPEG-DASH
Media transfer continues:
Buffering to allow for network throughput variations
Client continues fetching subsequent segments
  monitors network bandwidth fluctuations
  adapts to available bandwidth by fetching segments of appropriate bitrate to maintain an adequate buffer
MPEG-DASH specification only defines
  MPD
  segment formats
Outside of MPEG-DASH’s scope:
  how MPD is delivered
  media-encoding formats containing the segments
  client behaviour for fetching, adaptation heuristics, and playing content

## Slide 63
On-demand streaming (stored video)
Live streaming
On-Demand Vs Live Streaming
(already compressed)
result of n/w jitter
Live media needs live compression stage

## Slide 64
Container Format - a meta file format specification
how different multimedia data elements (streams) and metadata coexist in files
A container format provides the following:
Stream Encapsulation
One or more media streams can exist in one single file.
Timing/Synchronization
The container adds data on how the different streams in the file can be used together. E.g. The correct timestamps for synchronizing lip-movement in a video stream with speech found in the audio stream.
Seeking
The container provides information to which point in time a movie can be jumped to. E.g. The viewer wants to watch only a part of a whole movie.
Metadata
There are many flavours of metadata. It is possible to add them to a movie using a container format. E.g. the language of an audio stream.
(also subtitles considered as metadata)
Media Containers
https://bitmovin.com/container-formats-fun-1/

## Slide 65
Common Media Application Format - CMAF
(See previous notes on HTTP Live Streaming …)
A Transport Stream (TS) is ill-suited to segmented media delivery and switching
HLS uses TS
DASH - allows TS but mostly ISO Base Media File Format (ISOBMFF)
First – some background on container formats ⇨⇨⇨
https://agama.tv/what-is-cmaf-and-why-does-it-matter/

## Slide 66
Container Format - a meta file format specification
how different multimedia data elements (streams) and metadata coexist in files
A container format provides the following:
Stream Encapsulation
One or more media streams can exist in one single file.
Timing/Synchronization
The container adds data on how the different streams in the file can be used together.
E.g. timestamps for synchronization
Seeking
The container provides information to a specific point in a video
Metadata
There are many flavours of metadata. It is possible to add them to a movie using a container format.
  E.g. the language of an audio stream.
  subtitles also considered as metadata
  … now back to CMAF ⇨⇨⇨
Media Containers
https://bitmovin.com/container-formats-fun-1/

## Slide 67
Common Media Application Format - CMAF
2016: MPEG cross industry proposal:
  “Common Media Format for Segmented Media”
⇒ Media Application Format (MAF)
MAF - “selecting tested and verified tools from MPEG standards
... appropriate selection for the envisioned application.
based on ISO Base Media File Format (ISOBMFF) + other MPEG standards
Became Common Media Application Format
  CMAF - MPEG-A Part 19 or ISO/IEC 23000-19
CMAF Aim:
To allow a single media encoding format to be used
across many applications and devices

## Slide 68
Common Media Application Format - CMAF
CMAF defines
  encoding
  storage
  identification
  subtitles/captions
  packaging of segmented media objects
  for delivery and decoding on end user devices in adaptive multimedia presentations
    segment format based on ISOBMFF
not the manifest
c.f. MPEG-DASH Interoperability Guidelines mainly aligned with Apple aim to support fragmented MP4 (fMP4)
Ultimate aim: a single segment format for OTT - Currently the two formats are:
    Transport Stream (TS)
    ISOBMFF

## Slide 69
DASH Manifest vs CMAP media object model
MPD periods, contain multiple adaptation sets / representations
CMAF does not define a manifest
… but any manifest can be used to instantiate the CMAF media object model
Periods in DASH are presentations in CMAF
DASH / CMAF
More information here

## Slide 70
ISO BMFF – ISO Base Media File Format
ISO base media file format ISO/IEC 14496-12 – MPEG-4 Part 12
Defines time-based multimedia files
It is the basis for other media file formats, e.g. container formats MP4 and 3GP
a general structure for time-based video and audio files
flexible, extensible; facilitates interchange, management, editing and presentation of the media
Base components of ISOBMFF are boxes - also called atoms
boxes - classes and an object oriented approach
The base class:
  Example FileTypeBox:
    to identify the purpose and usage of an ISOBMFF file
    often at the beginning of a file.
    box can also have children and form a tree of boxes
      e.g. MovieBox (moov) can have multiple TrackBoxes (trak)
      track is a single media stream

## Slide 72
Chroma Subsampling

## Slide 73
RGB to Y,Cb,Cr
RGB pixel format … … … is converted to … … … Y,Cb,Cr
where
Y = luminance (light intensity)
Cb, Cr = colour information
Weighted RGB converted to Y Cb, Cr
0.2989*R + 0.5870*G + 0.1140*B
Cr
Cb
Y
During the encoding stage ...

## Slide 74
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma

## Slide 75
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
similarly,
Cr = R – Y
= -
Cb = B – Y
i.e. 8 bits of Cb (0-255)
value of Cb:
value of original Blue
minus
value of luma
= -
e.g.
= 210 - 90
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma
1111000
11010010
01011010

## Slide 76
Y,Cb,Cr – for image of x x y pixels in “4:4:4”
x pixels
y pixels

## Slide 77
Y,Cb,Cr – Chroma Sub-sampled to “4:1:1”
x pixels
y pixels
Reason: To greatly reduce the amount of data
Rationale: The eye’s resolution of luminance is greater than for colour

## Slide 78
YCbCr
Colour Space: Y = Luminence Information; Cr, Cb = Chrominance Information
Derived from RGB (gamma corrected)
Y is dominant information; RGB colour info derived from Y, Cr, Cb relationships
  (simplified): Cb = B-Y ; Cr = R-Y
Cr
Cb
Y
Original image
Y,Cb,Cr

## Slide 79
Cr
Cb
Y
Cr
Cb
Y
RGB to Y,Cr,Cb
i.e. there are now three mappings of the original RGB image:
Y: Luminance intensity
Cb: Intensity of the values of
[B minus Y]
Cr: Intensity of the values of
[R minus Y]

## Slide 80
Chroma Subsampling
Left – original RGB image:
12 x 8 pixels = 96 pixels
bits for each pixel = 8 red + 8 green + 8 blue
∴ 24b each pixel, total bits = 24 x 96 b
= 2304b (= 288 Bytes)
Bottom left, YCbCr, 4:4:4 : (is also 2304b)
Below, Chroma sub-sampled, 4:1:1:
Luma = 96 x 8 = 768
Chroma = 3 columns of Cr and Cb,
  2 x 8b each C = 8 x 2 x 3 x 8 = 384 b
Total = 768+384 = 1152b (=144 B)
i.e. 50% saving

## Slide 81
Reception / Decoding
Decoding, reverse process ...
  from Chroma sub-sampled to full RGB
note – interpolating lost information
∴ detail is lost in the process
Perceptual (e.g. MPEG, etc ) encoding + decoding is also part of this process and loses a lot more detail
... more later in the module
encoding process
decoding process

## Slide 82
Chroma Subsampling
Luma and chroma components
Weighted sum of gamma-corrected R'G'B‘ tristimulus components
  instead of linear (tristimulus) RGB components
Luminance and colour detail are not completely independent of each another
  "bleeding" of luminance and colour information between the luma and chroma components
    i.e. because of the colour not represented in each pixel, and is interpolated for the final viewed image
    greatest for highly-saturated colours
    noticeable in between the magenta and green (when chroma subsampled)
without colour subsampling
with colour subsampling

## Slide 83
Chroma Subsampling
commonly expressed as a three part ratio J:a:b (e.g. 4:2:2)
number of luminance and chrominance samples in a conceptual region
  J pixels wide
  2 pixels high
Parts
J = horizontal sampling reference (width of the conceptual region)
  usually = 4
a = number of chrominance samples (Cr, Cb) in the first row of J pixels
b = number of changes of chrominance samples (Cr, Cb) between first and second row of J pixels
Alpha - horizontal factor (relative to first digit)
  omitted if alpha component is not present
  equal to J when present

## Slide 84
Chroma Subsampling
Y = Luminance Cb = Blue - Luma
Cr = Red - Luma
4:1:1 - Widely used in JPEG and MPEG
4:2:0 - Used in DVD, JPEG, MPEG
4:2:2 - Used in Studio recordings
4:4:4 - High end applications
(Note - Cb and Cr is colour difference information for the related pixel; not the red/blue value itself!)
full horizontal resolution, full vertical resolution
¼ horizontal resolution, full vertical resolution
½ horizontal resolution, full vertical resolution
½ horizontal resolution, ½ vertical resolution