## Slide 1
Broadcast Technology UG1
Review
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
Learning Outcomes
1. Differentiate between TV audio and video standards and apply for studio applications
2. Evaluate and select data interconnects for audio and video
3. Select and apply test procedures for audio and video signals
4. Compare and contrast network transmission standards worldwide, current and legacy, and evaluate for application to broadcast developments

## Slide 3
SCHEDULE (Planned)

## Slide 4
ASSESSMENT
The assessment for this module will be one exam
(i.e. an exam which accounts for 100% of the final module mark)
Exam date: Wednesday 14th June (morning)
.. online (exam monitoring software)
You are required to answer FOUR of the SIX questions
  Questions will have a number of parts (typically 3, 4 or 5)
  Marks breakdown is shown in brackets
Each question carries 25 marks; total marks for the paper = 100
Pass Mark: 40%
Note that marks are allocated for method, in addition to the final answer.
Therefore method and full calculations should be shown in your solutions to analytical questions
Calculators may be used provided they are in accordance with Faculty guidelines
Reassessment
Date - tbc
(same format as the original assessment)

## Slide 5
Information Transmission, Signal Encoding
Information
Source Coding
Channel Coding
Modulation
Interference
Phase Distortion
Attenuation
Demodulation
Channel Decoding
Information
Source Decoding
bit errors
Transmission Link
Source Information
coded data in as small space as possible (compressed, etc)
signal received – reverse processes
transmission is subject to noise interference
aim – to approach the Shannon Limit
Channel coding
appropriate error protection method
... depends on channel characteristics
modulation on to carrier
jeremy.foss@bcu.ac.uk
Crosstalk
Crosstalk
jitter
NOISE
NOISE
NOISE

## Slide 6
Transmission
Media

## Slide 7
Types of Transmission Media
Multiplexing - FDM, TDM, Statistical
  * introduction only – will be covered in depth later on
Cables
  Twisted Pair
  Coaxial
Fibre Optic
  Wave Division Multiplexing
Radio
  Spectrum
  Transmitter
  EM Wave, Radio Waves
  Propagation through lower and upper atmosphere
  Broadcast Transmitter Technologies (valves)
Transmission Media

## Slide 8
Twisted Pair Cable
Two insulated copper wires that are twisted together (which results in cancellation of induced interference; cancellation of radiated interference, hence reduces radiation)
The individual pairs can be shielded (STP) or unshielded (UTP)
The cable can also be shielded (S/STP)
Categories (CAT ...)
  1 - primarily for voice
  2 - 4Mbps
  3 - 16MHz bandwidth; 10Mb/s
  4 - 20MHz bandwidth; 16Mb/s
  5 - 100MHz bandwidth; 100Mb/s (4 pairs/cable)
  - 400MHz bandwidth; 1Gb/s (4 pairs/cable)
  - 600MHz bandwidth (1GHz for Augmented); 10Gb/s
  - 1.2GHz bandwidth
Common Uses:
  Voice Telephony, various Digital Subscriber Line (xDSL), LANs
CAT 7 – Screen Shielded Twisted Pair (SSTP)

## Slide 9
Twisted Pair Cable
Advantages:
  High availability
  Low installation cost
Disadvantages:
  Usable frequency spectrum is small
  Limited data rates
  Limited range
  High suceptibility to electromagnetic and radio frequency interference
ref – Prof. David Bernstein, James Madison University

## Slide 10
In balanced pair operation -
Differential mode transmission -
differential signals; receiver detects the difference between the two
noise signals tend to couple to both wires equally
∴ noise produces a common signal in each conductor
- which is cancelled at the receiver
(not effective when the noise source is close to the signal wires; closer wire will couple with the noise more strongly)
Twisted Pair Cable
Twist rate
more twists the better (usually)
http://www.extron.com/company/article.aspx?id=utptechnology

## Slide 11
Frequency dependent attenuation and dispersion
… Intersymbol Interference (ISI)
Coupling between wires in same and adjacent binders
… crosstalk - near-end cross-talk = NEXT
- far-end cross-talk = FEXT
Bridged taps and gauge transitions
… reflections : pulse distortion (ISI)
Impulsive noise : high bursts of short duration (10 ms - 1 ms)
Signal Issues on Twisted Pairs at High Frequencies
Impedance mismatch between hybrid and line impedance
… reflections (echo)
RFI interference: AM broadcast & amateur radio
… ingress & egress
All these require a highly adaptive transceiver (at each end)

## Slide 12
Coaxial Cable
A (thick) copper wire surrounded by an insulator and an outer conductor
Common Types:
  RG-6 - 1.00mm core, 75 Ω
  RG-59 - 0.81mm core, 75 Ω
  RG-58 - 0.90mm core, 50 Ω
  RG-8 - 2.17mm core, 50 Ω
Common Uses:
  Applications for RF signals
  Cable TV (Old: RG-59; New: RG-6)
  Ethernet (RG-58: 10Base2; RG-8: 10Base5)
  connecting radio transmitter feeds
Advantages:
  High capacity (370-1000 times more than twisted pair)
  Low susceptibility to noise and crosstalk (because of shielding)
Disadvantages:
  Noise on the return path
  High installation cost

## Slide 13
Coaxial Cable
All cables have electrical properties - they are not just short-circuits between equipment
Electrical properties of any cable pair:
R: resistance along the cable
L: signals cause inductance along the length of the cable
G: conductance - a certain amount of leakage, similar to a high resistance between the conductors
C: capacitance between the two conductors
Coax cable is designed to control these parameters

## Slide 14
Coaxial Cable
All cables have electrical properties - they are not just short-circuits between equipment
All cables are effectively a (mathematically) complex circuit of distributed impedance sections

## Slide 15
Total Internal Reflection
Light passing from one medium (m1) to another (m2) with lower index of refraction (ri) bends away from the normal line
At the critical angle, defined by sin ( θ ) = n1 . n2, the refracted light will not go into the second medium but will travel along the border
Fibre Optic Cable

## Slide 16
Three types of fibre optic cable commonly used:
Multimode - MMF
many rays (modes)
core = 62.5 microns
  (some 50 microns)
LED and laser sources 850, 1300nm
LANs
graded index ~2GHz b/w
step index is rare
Single mode - SMF
single ray (mode)
core = 9 microns
telephony, CATV
laser @ 1300, 1550 nm
b/w ~ 100THz
Fibre Optic Cable

## Slide 17
Summary of Modes and dispersion
Fibre Optics
Most fibres 125um outside diameter
MMF
larger core: 50 or 62.5um
wavelengths: 850 and 1300 nm
SMF
smaller core ~9um
Plastic Optical Fibre (POF)
large core ~1mm
usually step index
short, low speed
PCS, HCS
PCS plastic clad silica
HCS hard clad silica
smaller glass core ~200um
thin plastic cladding

## Slide 18
Fibre Networks

## Slide 19
(left) http://learn.uci.edu/oo/getOCWPage.php?course=OC0811004&lesson=005&topic=002&page=21
Electromagnetic Wave
alternating electrical current produces an electric and magnetic field that are also alternating
the wave of the electric field and the wave of the magnetic field are propagated perpendicularly to the direction of propagation and to each other

## Slide 20
Electromagnetic Wave

## Slide 21
Radio Wave Propagation
Reflection
similar to light
for long wavelengths (80m+)
small obstacles (cars, trees) have little effect
  objects small compared to the wavelength, can't reflect the energy
  long waves are reflected by the ground ... but also penetrate
short wavelengths - V/UHF waves (2m - 70cm)
very sensitive to small obstacles
metal objects can be used as reflectors
Reflections
e.g. wi-fi in metal framed buildings
radio waves reflect and interact
could cause stronger or weaker reception

## Slide 23
Pulse Transmission,
Interference (ISI)
Eye Diagrams
Original generated signal → transmission system → received signal

## Slide 24
Theoretically perfect random pulse train
Pulse train: two or three pulse periods successively sampled, overlayed on each other
Random pulse train affected by imperfect transmission medias
Practical pulse train: successively sampled, overlayed
Quality of the Transmission

## Slide 25
Jitter
theroretical clock pulses
actual clock pulses
Distribution of clocking arising through various issues, e.g. arising through the nodes transmission
pulse train cleaned up at receiver
degraded pulse train received
smearing and delay
overshoot (“ringing” at filters)

## Slide 26
DATA GENERATOR
CHANNEL
OSCILLOSCOPE
Y-INPUT Ext Trigger
Clock In
Clock Out
Eye Diagram - test set-up
Sampling Instant
one pulse interval

## Slide 27
a run of pulses are fed into a scope –
locked on to one or two pulse widths
superimposed 1’s and 0’s
ISI – Eye Diagram
Demonstrated by “eye pattern” analysis of impulse response
It indicates the performance of a transmission system
original generated signal → transmission system → received signal

## Slide 28
Different Eye Patterns
Signal + timing errors - eye closing
Signal only - various small individual random distortions (but likely OK)
- eye is “open”
Signal + noise - eye closing (amount depends on noise)

## Slide 29
Can reveal important information
best point for sampling
SNR at the sampling point
amount of jitter and distortion
time variation at zero crossing - jitter
ISI – Eye Diagram
http://www.edn.com/design/test-and-measurement/4389368/Eye-Diagram-Basics-Reading-and-applying-eye-diagrams

## Slide 30
Multipath ISI
an undesirable effect – reflections of radio waves hitting various objects in the environment
unavoidable
http://www.st-andrews.ac.uk/~www_pa/Scots_Guide/RadCom/part19/page3.html
i.e. interference between a symbol and its own reflection … another form of ISI

## Slide 31
Noise

## Slide 32
Noise
IMPORTANCE:
for audio or video:
  … noise is an obvious disturbance to the original noiseless signal
for data transfer
  … noise can obliterate data; can reduce data rates; require retransmissions, etc

## Slide 33
Noise
Nature of noise
typically random – a stochastic process
Noise is manifested as a voltage
… alongside the voltage of the original signal
Various causes of noise
(coming next …)
Need ways to measure and represent noise
signal / noise ratio
Useful noise (sometimes)
white and pink noise

## Slide 34
Noise
signal
noise
signal + noise

## Slide 35
Sensor Noise
any active circuit (and many passive circuits) including camera sensors will produce noise ...
+ =
+ =
photocell charge plus positive noise spike = brighter pixel
photocell charge plus negative noise spike = darker pixel
original image = pure grey tone
recorded image = noisy grey tone
At the instant of image capture:

## Slide 36
Dynamic Range – Camera Sensor, Signal to Noise
signal: the light which hits the camera sensor
noise is unavoidable
can be small relative to the signal
  appears to be nonexistent
noise low ratio = much noise high ratios = very little visible noise
signal strength
constant noise level
image signal
Signal to noise ratio (SNR)
compare relative amounts of signal and noise
used for any electronic system
http://www.cambridgeincolour.com/
light level

## Slide 37
Noise Factor, Fn
The noise factor of a system is
the ratio of output noise power (Pno)
to input noise power (Pni):
Ideally Fn = 1
(because noise out would = noise in)
Noise sources are subject to temperature (thermal noise)
∴ needs to be measured at a standard temperature = T0 = 20ºC; = 293K
Fn
specifies how much additional noise the device will contribute to the noise already from the source.
Fn =
Fn =
Noise Figure, NF
Noise Figure NF is the Noise Factor in dB
NF = 10 Log10 Fn

## Slide 38
Signal Distortion
Frequency Distortion
certain frequencies are boost or cut unevenly across the audio spectrum
stated in equipment specifications as the components frequency response
Phase Distortion
given frequency from a complex waveform takes longer to pass through a signal chain than others: i.e. a phase shift in the individual frequencies
(amplitudes may be amplified equally over the entire frequency band, but the composite waveform has been varied)
Total Harmonic Distortion (THD)
most commonly known form of distortion
directly related to the percentage of harmonics generated by the components in the signal chain
Measured using Fourier Analysis
Intermodulation (IM) Distortion
modulation of combinations of spurious frequencies
the combination of resulting frequencies are equivalent to the sum and/or difference of integral multiples of the individual frequencies of a complex waveform
Transient Intermodulation (TIM)
solid-state amplifiers use negative feedback in order to improve frequency response and reduction of harmonic distortion
occurs during high-frequency music passages

## Slide 40
Video Packets
Audio Packets
Data Packets
PS
Mux
TS Mux
Mux adaptation, scrambling
Error Correction
Block Code
Interleaving
(against long errors)
FEC
Convolutional
coding
Interleaving
(against burst errors)
Mapper
(IQ symbols)
Frame adaptation
symbols
Pilot, TPS signals
OFDM
Modulation
Guard interval insertion
DAC for Tx
DVB Transmission Playout System
Antenna,
Cable,
Sat uplink
(Based on DVB-T, but –C, -S and –H are similar)
QPSK, QAM, etc
Blocks (1512 – 6048 sy/block)
of symbols →
frames (68 blocks)
(4frames =superframe)
Transmission parameters
carriers, 2k – 32k (for T2
channel b/w =
1.7 to 10MHz
includes cyclic prefix
FEC – Outer …….
FEC – Inner

## Slide 41
Inter-Symbol Interference for Modulated Data
Causes
In radio:
multipath interference, including atmospherics
On cables:
transmission line propagation, phase delays, electrical characteristics
Implications on radio and cable:
channel gain variations
signal spreading over a transmission line/path
jitter and other timing issues

## Slide 42
Multipath Interference in Radio
+ =
+ =
Path difference – results in phase difference

## Slide 43
Modulation,
AM, FM, Phase,
(QAM ... later on …)

## Slide 44
AM Frequency Spectrum - Sidebands
AM process produces a spectrum containing the carrier and two sidebands of frequencies related to the modulating signal
e.g.:
e.g. modulating signal is between 100Hz and 8KHz,
and carrier freq = 600KHz (=600,000Hz)
Then - USB extends up from [600,000 + 100]Hz to [600,000 + 8,000]Hz
= 600.1KHz up to 608KHz
LSB extends down from [600,000 – 100]Hz to [600,000 – 8,000]Hz
= 599.9KHz down to 592KHz
fc
fc + freq range of signal
fc - freq range of signal
Power
LSB =
Lower Side Band
USB =
Upper Side Band

## Slide 45
Subcarriers
An example of subcarrier – consider an AM transmission:
fc
freq range of signal
Power
Side Band
A frequency (i.e. a tone) modulated on to the main carrier
… becomes a subcarrier
fc
freq range of signal
Power
Side Band
Data (in sidebands) modulated onto the subcarrier
This example shows AM modulation on the subcarrier …
but could be other forms of modulation
phase (PM)
frequency (FM)
etc
so, in effect we have two levels of modulation (at least)

## Slide 46
Subcarriers …??
Total data to be transmitted
Intersymbol interference due to multipath reflections
Solution: multiple carriers
But these are separate carriers – not subcarriers modulated onto one carrier
… but they are often referred to as “subcarriers”
freq

## Slide 47
Vision Carrier
1.25MHz
(AM / VSB)
Colour Sub-Carrier
(suppressed)
5.68MHz
Chroma coding (QAM)
Sound Centre Freq
6.75MHz
(FM)
7.0MHz
PAL Signal Spectrum
freq
Full Sideband
Vestigial Sideband

## Slide 48
Multiplexing:
FDM, TDM
Statistical
Multiplexing: combination of signals to transmit on a common bearer / channel

## Slide 49
  Each signal is modulated onto a different frequency (subcarrier )
  Multiplexing - Frequency Division Multiplexing (FDM)
“baseband”
signals
i.e. unmodulated original signal
f1 f2

## Slide 50
  Multiple signals are interleaved (in bits or blocks) over time
  Multiplexing - Time Division Multiplexing (TDM)
Data streams divided into frames
Frames divided into time slots
Each user is allocated one time slot
Time slots contain data with guard period if needed for synchronisation
1
3
4
2

## Slide 51
10110011
01001001
10010001
010100101
010100101
10010001
01001001
010100101
010100101
01001001
010100101
Time Division Multiplex
4kHz voice sampled at 8kHz (fs) into 8 bits binary
e.g. for UK / European E1 Multiplexes:
30 channels of speech into 32 channel frame “Multiplex”
32 channels x 8b x 8kHz = 2.048Mbs-1
  (includes 1 channel signalling and 1 channel synchronisation)
TS1 TS2 TS3 TS4 TS5 TS6 TS7 TS8 ………………………………………………………………….
Analogue – Digital: Samples are dropped into allocated timeslot for each frame
TS6 previous frame
TS6 this frame
TS6 next frame

## Slide 52
Statistical Multiplexer
Input buffer
Multiplexing - Statistical Multiplexing
Input buffer
Input buffer
Input buffer
Output buffer
Input buffer
Source A
Source B
Source C
Source D
Source E
Incoming ports: Data blocks arrive asynchronously from variable-rate sources
Input buffers smooth fluctuation in input data rates
Headers containing addresses and other information are added to the data blocks – to form packets
Packets are then fed to the output buffer
Outgoing Port:
Packets are placed on the outgoing channel

## Slide 53
Multiplexing - Statistical Multiplexing
e.g. DVB multiplex:
End
Flag
Address
Field
Control
Field
Information
Payload
Error
Control
Start
Flag
Packet format: Control, management and content assigned into fields

## Slide 54
Dynamic capacity allocation
Variable Bit Rate – VBR
one channel capacity reallocated to meet immediate service needs of other channels
Statistical Multiplexing
http://igorfuna.com/dvb-t/slovenia/multiplex-a-usage-chart
allow additional elementary bit streams to be added at the input of the multiplexer
... or allow elementary bit streams to be multiplexed at a second stage

## Slide 55
Correction to a Power-Based Curve
Exposure of scene
Brightness / Intensity of image/Display
(Simplistic explanation):
Input is raised to a power ɣ
Vfile = Vin1/ɣ
And output (display must be inverse of this, ɣ:
Vdisplay = Vinɣ
Actually, the equations may include a system constant A:
Vfile = AVin1/ɣ
(where A = a constant)
Vdisplay = AVinɣ
Result:
The eye needs to see the result of the
input ⇨ output transfer
… and should be a straight line
i.e. the viewer sees the original scene

## Slide 56
http://www.cambridgeincolour.com/tutorials/gamma-correction.htm
Camera detects this as 50% as bright
Eyes detect this as 50% as bright
Eye Response Compared to Camera ... Gamma (ɣ)
Camera response is linear ...
Eyes are much more sensitive to changes in dark tones than we are to similar changes in bright tones
  … this enables our vision to operate over a broader range of luminance
  (otherwise - outdoors brightness ranges would be too overwhelming)
Reference Tone
(full brightness)

## Slide 57
Eye Response Compared to Camera ... Gamma (ɣ)
Gamma translates between our eye's light sensitivity and that of the camera
when a digital image is saved, it's gamma encoded
the file more closely corresponds to what we would perceive in brightness increases
http://www.cambridgeincolour.com/tutorials/gamma-correction.htm
Camera detects this as 50% as bright
Eyes detect this as 50% as bright
Reference Tone
(full brightness)

## Slide 58
Display Gamma 1.0 1.8 2.2 4.0
Display Gamma
display gamma exactly corrects the image gamma
overall linear system gamma
display gamma over-compensates for the image gamma
overall system gamma that curves downward
(darkens the image)
x
x
x
✓

## Slide 59
Ideally EOTF should be defined by the human visual response
The current gamma worked well enough for the CRT era
… is a sort of perceptual EOTF
… But only at relatively low luminance levels
  and small dynamic ranges
But next generation systems
are much brighter
have much higher dynamic range
… so need to stretch or modify gamma to allow a little more brightness and dynamic range out the current system
… and adapt to scenes
HDR Transfer Functions

## Slide 60
Colour/luminance volume:
BT.2020 (10,000 nits for new LCDs and OLED displays)
vs
BT.709 (100 nits); Yxy
(Sony)
Nit: Unit of luminance, the intensity of visible light.
To describe the brightness of TV displays.
One nit = one candela/m2
https://www.flatpanelshd.com/focus.php?subaction=showfull&id=1505390780
Colour in BT.709 vs BT.2020

## Slide 61
Traditional display devices
used BT.709 Gamma transfer function
brightness range of up to 100 Nits (cd/m2).
For HDR
Perceptual Quantizer (PQ)
  an absolute, display-referred signal
    (i.e. image data is referred to each display’s capabilities)
  implement tone mapping to adapt the light levels
  use content metadata to display PQ coded images
    could be for entire video stream (static)
  or for each individual shot (dynamic)
  but dynamic PQ not compatible with existing display systems
Hybrid Log-Gamma (HLG) - a relative, scene-referred signal
  compatible with existing display systems
The Need for HDR Transfer Functions – HLG and PQ

## Slide 62
HDR – Signal To Light Mapping
Brightest
Image
Darkest
Image
HLG
BT.709 Gamma
PQ SMPTE ST2048
light level range in darker region is represented by a larger signal value range compared to the brighter regions: so more granular representation in darker regions
  this is more evenly distributed for the BT.709 based displays
  become less granular for HDR displays in the brighter regions

## Slide 63
Requirement:
To transmit Audio and Video compressed data in:
(i) reliable channels – studio, DVD, reliable media (PS)
(ii) transmission in hostile environments (TS)
Allow interchange between these two formats
Video
Audio
Video
Audio
Data
MPEG-2 Transport Mux
Transport Stream, TS
Program Stream, PS
MPEG-2
Systems Processor
MPEG-2
Systems Processor
MPEG-2
Compressors
MPEG Systems
Decoder
Decoder
Decoder

## Slide 64
Video Presentation Units: Raw video coding at discrete time intervals
MPEG-2 Packets and Multiplexes
audio and video data can be exchanged between TS and PS at PES level
Audio
Encoder
Video
Encoder
Packetiser
Packetiser
TS Multiplexer
PS Multiplexer
Transport Stream
(TS)
Program Stream
(PS)
Access Units (AU)
Audio Elementary Stream
Access Units (AU)
Video Elementary Stream
Audio PES
Video PES
Scope of MPEG-2 Systems Standard
Clock
Audio Presentation Units: 24mS of Raw uncompressed audio

## Slide 65
MPEG-2 – PES ⇒ PS Packs and TS Packets
PS
Pack
Pack
Pack
Program end code
........................
Pack
Header
PES
Pack
PES
PES
PES
...................
PES
PES
Header
PES payload
TS
Header
TS payload
TS
Header
TS payload
TS Packet
PID =m
TS Packet
PID = k
TS Packet
PID = m
TS Packet
PID = h
TS Packet
PID = k
.................................
188 bytes
188 bytes
188 bytes
188 bytes
188 bytes
TS
Packet
TS
Pack

## Slide 66
MPEG-2 – PES ⇒ PS Packs and TS Packets
PS
Pack
Pack
Pack
Program end code
........................
Pack
Header
PES
Pack
PES
PES
PES
...................
PES
PES
Header
PES payload
TS
Packet
TS
Pack
Program Steam - PS
for transmission and storage in error-free channels
PES - long variable-length packets
... into variable length packs
    multiple PES packets
... of nearly equal length
(video and audio)

## Slide 67
MPEG-2 – PES ⇒ PS Packs and TS Packets
PS
Pack
PES
PES
Header
PES payload
TS
Header
TS payload
TS
Header
TS payload
TS Packet
PID =m
TS Packet
PID = k
TS Packet
PID = m
TS Packet
PID = h
TS Packet
PID = k
.................................
188 bytes
188 bytes
188 bytes
188 bytes
188 bytes
TS
Packet
TS
Transport Stream – TS
for channels with likely errors
short fixed-length: 188B
PES packets – long variable length
  Sub-divided
  carried as payload of TS packets

## Slide 68
Video Compression (Introduction)

## Slide 69
The Eye
The Eye
The Eye

## Slide 70
Psychovisual – how we perceive images
Light sensitivity in the eye
Rods - light intensity - not colour
~125 million across the retina
characteristics of high speed black & white film
Cones - colour - responsive in three wavebands
6 or 7 million cones
characteristics of low-speed colour film
RODS and CONES
(retina)
... Chroma Sub-sampling

## Slide 71
Images Captured on a Camera
Image captured on red blue and green – responsive photo-sites
each pixel is represented by R, B, G
each pixel has its own value of light intensity
Original captured image at camera sensor:

## Slide 72
RGB to Y,Cb,Cr
RGB pixel format … … … is converted to … … … Y,Cb,Cr
where
Y = luminance (light intensity)
Cb, Cr = colour information
Weighted RGB converted to Y Cb, Cr
0.2989*R + 0.5870*G + 0.1140*B
Cr
Cb
Y
During the encoding stage ...

## Slide 73
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma

## Slide 74
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
similarly,
Cr = R – Y
= -
Cb = B – Y
i.e. 8 bits of Cb (0-255)
value of Cb:
value of original Blue
minus
value of luma
= -
e.g.
= 210 - 90
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma
1111000
11010010
01011010

## Slide 75
Y,Cb,Cr – for image of x x y pixels in “4:4:4”
x pixels
y pixels

## Slide 76
Y,Cb,Cr – Chroma Sub-sampled to “4:1:1”
x pixels
y pixels
Reason: To greatly reduce the amount of data
Rationale: The eye’s resolution of luminance is greater than for colour

## Slide 77
YCbCr
Colour Space: Y = Luminence Information; Cr, Cb = Chrominance Information
Derived from RGB (gamma corrected)
Y is dominant information; RGB colour info derived from Y, Cr, Cb relationships
  (simplified): Cb = B-Y ; Cr = R-Y
Cr
Cb
Y
Original image
Y,Cb,Cr

## Slide 78
Cr
Cb
Y
Cr
Cb
Y
RGB to Y,Cr,Cb
i.e. there are now three mappings of the original RGB image:
Y: Luminance intensity
Cb: Intensity of the values of
[B minus Y]
Cr: Intensity of the values of
[R minus Y]

## Slide 79
Reception / Decoding
Decoding, reverse process ...
  from Chroma sub-sampled to full RGB
note – interpolating lost information
∴ detail is lost in the process
Perceptual (e.g. MPEG, etc ) encoding + decoding is also part of this process and loses a lot more detail
... more later in the module
encoding process
decoding process

## Slide 80
Contribution and
Distribution

## Slide 81
http://www.cisco.com/c/en/us/solutions/service-provider/distribution/index.html#
Production Contribution Distribution Consumption
Contribution and Distribution

## Slide 82
ACQUISITION
LOGGING
INGEST
MEDIA
STORE
DELIVERY
PRODUCTION
SCHEDULE
CREATION
ARCHIVE
AUTOMATION
& PLAYOUT
EPG
CREATION
CODING
&
MULTIPLEX
INTERNET
Streaming
Encoding
iPlayer
Website
CDN
Live Feeds
Studios
OBs
Low end /
Domestic
Camcorders /
DSLRs
News
Camcorders
Hi-End
Camcorders
Digital
Cinema
Cameras +
Recorders
Multi-
Camera
Studio / OB
Other
Material
Data
Input
Data
Input
Data Store
Database
Edit
Grading
Graphics
Effects
Audio
Dubbing
Broadcast and Production Workflow (BBC Schematic)
Media
Metadata
Both
Transmission

## Slide 83
http://www.snellgroup.com/documents/brochures/automation-and-media-management/Momentum.pdf
Workflow Processes
Typical – there are many variations ...
... and automated:

## Slide 84
MEDIA ASSET MANAGEMENT
BPM: Business Process Management (“Workflow Engine”)
Database

## Slide 85
Preferred approach - file-folder structure
accessible via a standard network protocol (rather than a proprietary interface between the storage and the asset management system)
Typical MAM File System Approach
File 1: DISK H1 … written today
File 2: LTO L3
File 3: DISK H4 … being copied to LTO L2
File 4: LTO L2
File 5: DISK H3 … written last hour
File 1: LTO L7
File 2: LTO L5
File 3: DISK H2
File 4: LTO L1 being copied back to disk (due to recent read attempt)
+ access to other cloud storages (own, third party)

## Slide 86
General specifications |  |  |  | 
Tape type | Raw capacity (compressed capacity @ 2.5:1) | Max Uncompressed Speed MB/s (note bytes) | WORM | Released
LTO-1 | 100 GB | 20 | No | 2000
LTO-2 | 200 GB | 40 | No | 2003
LTO-3 | 400 GB | 80 | Yes | 2005
LTO-4 | 800 GB | 120 | Yes | 2007
LTO-5 | 1.5 TB | 140 | Yes | 2010
LTO-6 | 2.5 TB 6.25 TB | 160 | Yes | 2012
LTO-7 | 6.4 TB 16 TB | 315 | Yes | 2015
LTO-8 | 12.0 TB 30 TB | 472 (upto 900Mb/s) | Yes | Now
LTO-9 | 26 TB 65.2 TB | 708 | Planned | TBA
LTO-10 | 48 TB 120 TB | 1100 | Planned | TBA
Linear Tape Open – to LTO 10
Note comparative native / compressed capacities
(2014 … )
Sony Tape @ 148Gb/in2
… 185TB per cartridge

## Slide 87
IP Workflows
SMPTE 2022, 2110

## Slide 88
Why IP is replacing SDI*
Universal connectivity (broadcast and other industries)
Lower budgets, higher quality requirements
Production companies scaling:
  IP allows best production talent remains in a central location
  Receive camera feeds from remote locations
Democratise the industry
  single producer can have many camera inputs from anywhere in the world
  * although SDI is still in development
IP Workflows

## Slide 89
https://www.smpte.org/sites/default/files/section-files/GVExpo2018%20SMPTE%2004%20-%20Scalable%20Facilities%20with%20ST%202110%20-%20Mailhot.pdf
In SDI Routing, all routing in the SDI crosspoint frame
The Control System tells the crosspointwhat to switch where
The Crosspoint Router switches everything internally
Receivers just receive all data sent to them
In IP Routing, the Receiver is involved …
Control System tells the Receiver:
  What Multicast Group & Port# to switch to (Main and Protect)
  Technical Metadata of the new stream
  The Receiver is responsible for how it switches/transitions to it
  The Receiver asks the network for the new signal
  The network provides the new signal through packet forwarding logic
How is IP Television Routing Different from SDI ?

## Slide 90
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
Traditional Broadcast and Media Routing

## Slide 91
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
IP World of Broadcast and Media Routing

## Slide 92
SMPTE ST 2022-6 (Multiplexed Streams)
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017

## Slide 93
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
SMPTE ST 2110 – Essence Streams

## Slide 94
Content Delivery Networks

## Slide 95
CDN - to optimize content delivery
infrastructure solutions to network service providers who deploy their own dedicated digital media delivery
asset tracking
network performance
  real-time load
  statistics reporting
Internet - end-to-end
  core network is simple - only forwards data packets
  intelligence is at edges
Content Networking
1 – central server
2 – cache (edge server/cache)
3 – end users

## Slide 96
system of caches containing copies of data
data is distributed at various points in a network
maximizes the bandwidth required to access the data from clients throughout the network
Content Networking
1 – central server
2 – cache (edge server/cache)
3 – end users

## Slide 97
The Cloud
Storage
Processing
Software as a Service (SaaS)
Platform as a Service (PaaS)
Not really a cloud (!)
a facility of servers and processors
may be private owned
may be third party owned
resources rented out
  service level agreements
e.g.
media workflow facilities
video headends
etc …

## Slide 98
Media Distribution
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End
Distribution Network
Satellite
Cable
Telco Broadband
Terrestrial TV
Web (OTT)
Mobile

## Slide 99
Media Distribution ... ... Satellite
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End

## Slide 100
Media Distribution - Digital Terrestrial (DTTV)
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
STB, etc
End Users
Video Head-End

## Slide 101
Media Distribution – Cable
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Cable Network
Video Head-End
Access Network

## Slide 102
Media Distribution – IPTV - Telco Broadband, OTT/Web
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
VOD and
Various
Functions
(Servers, etc)
Video Head-End
Access Network
Telco Broadband

## Slide 103
Media Distribution – IPTV - Telco Broadband, OTT/Web
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
Video Head-End
Access Network
Telco Broadband
OTT
OTT
WEB-BASED VIDEO PROVIDER

## Slide 104
Media Distribution
Broadcast
  but what is “broadcast?”
  … vs On Demand
  (what are “video servers”? – or any other server)
  digital cinema distribution
Streaming:
  DVB – Cable, Satellite, DTTV
  IP-based – IPTV (Telco broadband, OTT)
    http
      MPEG → DASH (dynamic adaptive streaming on http)
      HLS (http live streaming, Apple implemented)
    rtp protocol

## Slide 105
VOD and
Various
Functions
(Servers, etc)
Network Access Equipment
STB, etc
End Users
Video Head-End
Off air
Content
Local
Content
Encoding /
Transcoding
Conditional
Access
EPG
Additional Services
Prepare for
Transmission
modulation, etc
Transmission
Network
cable
satellite
Telco IPTV
Web
Customer
Home
Modem
Set Top Box
  inc CA
TV
Multiplexing
Middleware
Advertisment Inserts
Authentication
DHCP
The Headend (Cable, Satellite, Web, Telco ... )

## Slide 106
Streaming
HTTP, HLS
  MPEG-DASH
RTP/RTSP

## Slide 107
The original solution for streaming
  ... overtaken by RTP/RTSP based for large IPTV deployments
  ... more recently back in favour
used generic HTTP servers (often based on Apache or Windows Server)
HTTP Streaming
Early days
Limited bandwidth available
    “Download and play”
        no lookahead seeking or random access
      Multiple viewers – server bandwidth issues
Apple introduce progressive download

## Slide 108
HTTP server/client – stateless
  HTTP-streaming: retrieves consecutive short chunks on as-needed basis
      little waste (the video is delivered as it is watched)
          server efficiently serves more streams
      Random seeking
        (viewer selects – player retrieves the appropriate chunks)
    firewall friendly
    can utilise HTTP caching mechanisms
    less expensive to implement (no streaming server required)
      scale more cheaply and effectively to serve available users
Streaming Media Protocols – HTTP addresses RTMP Issues
RTMP/RTSP/HTTP – state of the market
little impetus for RTMP/RTSP sites to change –still widely used
new installations - overwhelming view – HTTP
in fact most video content is delivered via plain old HTTP progressive download

## Slide 109
Client
Server
http GET
http GET
Segment timing:
10 seconds = reasonable balance for most broadcast content
Shorter segments
= more frequent refreshes of the index file
.. unnecessary network overhead for the client
Longer segments
= latency and initial startup time
Media Formats
e.g. video: H.264 / VP9,
  audio: .aac / Opus, etc
  video + audio file segments unwrapped
  … but certain applications –
  can be wrapped in MPEG-TS (DVB)
Audio segment
Video segment
etc
HTTP Streaming

## Slide 110
HTTP Live Streaming - HLS
Apple (part of QuickTime and iOS)
HLS v5 announced in Sept16
support for Fragmented MP4

## Slide 111
MPEG-DASH
Dynamic Adaptive Streaming over HTTP
http://www.streamingmedia.com/Articles/ReadArticle.aspx?ArticleID=79041
Background
(commercial) audio/video was typically transported over RTP/UDP
  (but streaming proprietary solutions based HTTP/TCP)
HTTP streaming - good - provided that the increased latency is acceptable
Benefits:
Firewall and NAT traversal (c.f. services based on RTP/UDP)
Widely deployed network caches (CDNs)
  Deployment of CDN caches can be kept simple
Complexity (adaptation) moved to client
Servers are agnostic to delivered content
network resources / configuration may vary over time

## Slide 112
MPEG-DASH
DASH client obtains the MPD …
MPD (Media Presentation Description) –
XML document
  delivered using HTTP or other transport
describes media data available at the servers
allows clients to select the data
defines segments available
can either be
  initialization segments - initialization data for decoding
  media segments
segment format based on MPEG2-TS
  Using ISO base Media File Format (ISOBMFF - general structure for time-based media
  (however, segments based on other formats can be specified)