## Slide 1
Broadcast Technology UG1
DVB, Compression
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
DVB

## Slide 3
DVB - Digital Video Broadcasting
Standards
Satellite DVB-S, DVB-S2, SH
Cable DVB-C, DVB-C2
DTT DVB-T, DVB-T2
DTT for handhelds DVB-H, DVB-H2
IPTV DVB-IPTV
DASH DVB-DASH
DVB-3DTV - Frame Compatible Plano-Stereoscopic 3DTV
DVB-C2 - 2nd Generation Cable Transmission
DVB-CID - Carrier Identification for Satellite Transmission
DVB-CPCM - Content Protection and Copy Management
DVB-FF - DVB File Format
DVB-GEM - Globally Executable MHP
DVB-GSE - Generic Stream Encapsulation
DVB-H - Broadcasting to Handheld Devices
DVB-IPDC - Internet Protocol Datacasting
DVB-IPTV - Internet Protocol Television
DVB-MHP - Open Middleware for Interactive TV
DVB-PCF - Portable Content Format
DVB-RCS2 - Return Channel Satellite
DVB-RCT - Return Channel Terrestrial (03/2001)
DVB-S2 - 2nd Generation Satellite Broadcasting
DVB-SH - Satellite Services to Handheld Devices
DVB-T - Digital Terrestrial Television
DVB-T2 - 2nd Generation Terrestrial Broadcasting
DVB - Emergency Warning System
DVB Project - An Introduction
Hierarchical Modulation in DVB-T (03/2000)
plus many others (inc addenda, etc) …
Industry Organisation
Standardisation Process –
Joint Technical Committee (JTC) of:
ETSI - European Telecommunications Standards Institute
CENELEC - European Committee for Electrotechnical Standardization CENELEC
EBU - European Broadcasting Union
Note standards refer to other standards and patents, e.g. MPEG
http://www.dvb.org/standards/factsheets

## Slide 4
Digital Terrestrial TV (DTT)
Advanced Television Systems Committee - ATSC-8VSB
Modulation: 8VSB: 8-level Vestigial Sideband
American Continent
MPEG2-TS
Digital Video Broadcast, Terrestrial Television - DVB-T
Europe; also DVB-S for Satellite, DVB-C for Cable; DVB-H for handhelds
MPEG2 format; also
Integrated Services Digital Broadcasting, Television - ISDB-T
Japan; also ISDB-S for Satellite, ISDB-C for CableTV
MPEG2 format
Modulation: PSK, COFDM/PSK/QAM

## Slide 5
DVB Specifies …
Specifies - essentially a layer one protocol for transport with Data Link (Transport Streams, GSE, etc)
Including -
Input Interface
usually Transport Streams - i.e. TV
Generic Stream Encapsulation – e.g. IP
Modes
Variable Coding and Modulation
Adaptive Coding and Modulation
FEC
e.g. DVB-T2: LDCP, BCH ½. 3/5. 2/3. ¾. 4/5. 5/6
Modulation
e.g. DVB-T2: OFDM
Modulation Schemes
Q/8/16/32PSK, QAM
e.g. DVB-C2: 16-4096QAM
Guard Interval
e.g. DVB-T2: 1/4, 19/256, 1/8, 19/128, 1/16, 1/32, 1/128 (fractions of a symbol)
Interleaving
Bit- Time- and Frequency-Interleaving

## Slide 6
Transport Stream Multiplex
Transmission:
Terrestrial
Cable
Satellite
Broadband
Program Streams

## Slide 7
MPEG
Motion Picture Experts Group
MPEG 1
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), 4, 5,
MPEG 2
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), …
MPEG 3 - originally for HDTV - abandoned
MPEG 4
audio and video coding - parts 1 - 22
MPEG 7
metadata, description
MPEG 21
framework for multimedia content delivery
XML-based; to communicate machine-readable license information
open framework for multimedia applications
"Rights Expression Language"

## Slide 8
Audio and video coding
Parts
1 - Synchronization and multiplexing of video and audio
- transport stream
2 - Compression codec for non-interlaced video signals
3 - Compression codec for perceptual coding of audio signals
- three layers of audio coding options (mp, mp2, mp3)
4 - Procedures for testing conformance
5 - Reference software
video CD format - quality ~ VCR
originally 1.5M bit/second data rates and 352x240 resolution
later up to 4M bit/second
the most compatible format in the MPEG family
only progressive scan video (... so need for MPEG-2)
MPEG-1

## Slide 9
(1994) Audio and video coding
for broadcast - DVB (satellite, cable, DTT, etc), also DVD (with mofifications)
9 Parts, including -
1 - Transport Streams - TS
  to carry digital video and audio in (unreliable) broadcast applications
  Program streams carry audio and/or video data + time stamp data
2 - Video
  similar to MPEG-1
  support for interlaced video
  optimised > 3 Mbit/s; not for low bit-rates (less than 1 Mbit/s)
  backwards compatible to MPEG1
  enhancements - used (to date) in most HDTV transmission systems
3 - Audio
  layers 1, 2, 3
4, 5 - as MPEG-1
7 - Enhanced audio
MPEG-2

## Slide 10
Part 3
new audio encoding (see later...)
low bitrate encoding with halved sampling rate
  MPEG-1 Layer 1/2/3 LSF - low sampling frequency
multichannel encoding with up to 5.1 channels
... backwards compatible -
MPEG-1 audio decoders can decode stereo from MPEG-2 multi-chan audio
MPEG-2 AAC - Part 7
make better use of available bandwidth
  non-backwards-compatible
MPEG-2 Audio

## Slide 11
Compression - Introduction

## Slide 12: Why Compress Audio?
CD quality = 2* 44.1 *16 Kbps ≈ 1.4 Mbps
About 1/850 of HDTV video
1 hour of audio needs 3600* 1.4 /8 = 630 MB
100 songs take about 360 minutes ≈ 4 GB
Will we continue to compress audio –
Mobile devices may prefer to save battery power by not decompressing??

## Slide 13: Why Compress Video
Size of uncompressed 1080p HDTV
1920 * 1080 ≈ 2 Mpixels per frame
For RGB this is 6MB per frame
Thus 1 s of video needs 25 *6MB = 150MB
Data rate of 150 *8 = 1200 Mbps = 1.2 Gbps
One hour of video needs 3600*150 MB
= 540,000 MB = 540 GB

## Slide 14: Compressed and Uncompressed Images
raster
image
display
processing
time
display
compressed
image
processing
time

## Slide 15: Compression Techniques: Lossless
uses techniques (tricks) to reduce data storage requirements whilst maintaining ability to reproduce original file exactly
possible because image is generally stored in a format that is logical and also compatible with the capture or display medium
lossless compression will generally compact data by processing it from the most logical or compatible structure to a format that requires minimal storage space
trades storage space for additional processing time

## Slide 16: Compression – Information Theory
IF …
image is all the same colour
  very easy to compress - just replace with colour value and codeword to indicate
every pixel is a random number between 0 & 255 and not correlated in any way with other pixels
  it is impossible to compress
In between -
look for patterns only for lossless compression
additionally psychovisual characteristics for lossy compression

## Slide 17: Lossless Compression
RLE replaces repeating bytes with number and kind:
  e.g.777555555 becomes 3765
  compression ratio 9:4 =2.25
In most applications RLE files are further compressed using Huffman which scans the whole file to discover the most frequently occurring bytes. These bytes are then translated to bit form, for example using only 1 bit for the most frequently occurring byte , 2 bits for the next most frequently occurring and so on

## Slide 18
Bit Rate Reduction Principles
Main process of bit-rate reduction:
Remove lower priority information from the signal at encoder
  ... according to what we perceive in the image
Coding - including information about the bit-rate reduction
  ... codec at time of image capture
Decode - to assemble and play the compressed file
  ... codec at time of viewing image

## Slide 19
Audio Compression (Introduction)

## Slide 20
Audio Compression
Audio Compression
Compression Usability, Latency
Encoding Architecture
Perceptual Coding: Psychoacoustic Models
Transform Domain Methods, Decoding
Coding, Bit Allocation, Frames
AAC - Advanced Audio Coding
MPEG-4 AAC, Low Delay Coder, Error Resilience,
Variable Bit Rate

## Slide 21
The Physiology of Hearing
Ossicles
Auditory Nerve
Cochlea
Tympanic Membrane
Auditory Canal
acts as a closed tube resonator
enhances sounds in the range 2-5 KHz
Pinna
presents larger area to received sound energy
“collects” sound – like a preamplifier
Stirrup
low + high frequencies

## Slide 22
High frequency sounds
The Physiology of Hearing – The Cochlea
schematic view - unroll the cochlea - distribution of sensitive hair cells
nerve endings
hair cells
incoming sounds
Lower frequencies

## Slide 23
http://www.hitl.washington.edu/publications/hollander/2.html
low + high frequencies
The Physiology of Hearing – The Cochlea

## Slide 24
Two signals within a critical band - closely related in frequency
stimulate the same area of the membrane in the cochlea
these two sounds added together don’t give twice the loudness
Two signals - frequencies separated
stimulate the different areas of the membrane in the cochlea
not competing for the same nerve endings
give an appreciable increase of perceived intensity
The Physiology of Hearing
freq
freq
freq
critical band
critical band
critical bands

## Slide 25
Psychoacoustics
Frequency dependent resolution:
  Human inability to discern minute differences in frequency
  within the critical bands
Auditory masking:
  Two signals in a critical band: the louder will mask the softer
    (either completely or to a certain extent)
  A masked signal must be louder than some threshold for it to be heard
User selection of bit rates: file size vs quality

## Slide 26
Model - To determine perceptually irrelevant information in the signal
an assimilation of human perception of (coincident) sounds
component frequencies allocated bits according (perceived) audibility
Psychoacoustic Models
http://www.head-fi.org/t/610161/lightbox/post/8384518/id/604385
Auditory Masking

## Slide 27
Threshold of Hearing, Masking Threshold

## Slide 28
MPEG Psychoacoustic Models
MPEG standard defines two models:
Psychoacoustic Model 1:
  simpler, less computationally expensive
  serious compromises in what it assumes a listener cannot hear
Psychoacoustic Model 2:
  More features
    more complex coding (assuming increased processor bandwidth)
  Layer III (.mp3)

## Slide 29
Temporal Masking
Temporal
  - faint sounds not heard following loud sounds
  Layer 1 - smaller frames - no temporal knowledge
  Layers II, III - do support temporal masking

## Slide 30
Video Compression (Introduction)

## Slide 31
Image Compression – A Number of Stages are used:
Lossy
Chroma Subsampling
DCT-based (harmonics/synthesis) compression
Lossless
iii. Huffman (statistical) coding

## Slide 32
The Eye
The Eye
The Eye

## Slide 33
Receptors
… Rods and Cones
http://www.cellsignallingbiology.org/csb/010/csb010fig10_rod_and_cone_structure.htm

## Slide 34
Psychovisual – how we perceive images
Light sensitivity in the eye
Rods - light intensity - not colour
~125 million across the retina
characteristics of high speed black & white film
Cones - colour - responsive in three wavebands
6 or 7 million cones
characteristics of low-speed colour film
RODS and CONES
(retina)
... Chroma Sub-sampling

## Slide 35
Images Captured on a Camera
Image captured on red blue and green – responsive photo-sites
each pixel is represented by R, B, G
each pixel has its own value of light intensity
Original captured image at camera sensor:

## Slide 36
RGB to Y,Cb,Cr
RGB pixel format … … … is converted to … … … Y,Cb,Cr
where
Y = luminance (light intensity)
Cb, Cr = colour information
Weighted RGB converted to Y Cb, Cr
0.2989*R + 0.5870*G + 0.1140*B
Cr
Cb
Y
During the encoding stage ...

## Slide 37
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma

## Slide 38
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
similarly,
Cr = R – Y
= -
Cb = B – Y
i.e. 8 bits of Cb (0-255)
value of Cb:
value of original Blue
minus
value of luma
= -
e.g.
= 210 - 90
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma
1111000
11010010
01011010

## Slide 39
Y,Cb,Cr – for image of x x y pixels in “4:4:4”
x pixels
y pixels

## Slide 40
Y,Cb,Cr – Chroma Sub-sampled to “4:1:1”
x pixels
y pixels
Reason: To greatly reduce the amount of data
Rationale: The eye’s resolution of luminance is greater than for colour

## Slide 41
YCbCr
Colour Space: Y = Luminence Information; Cr, Cb = Chrominance Information
Derived from RGB (gamma corrected)
Y is dominant information; RGB colour info derived from Y, Cr, Cb relationships
  (simplified): Cb = B-Y ; Cr = R-Y
Cr
Cb
Y
Original image
Y,Cb,Cr

## Slide 42
Cr
Cb
Y
Cr
Cb
Y
RGB to Y,Cr,Cb
i.e. there are now three mappings of the original RGB image:
Y: Luminance intensity
Cb: Intensity of the values of
[B minus Y]
Cr: Intensity of the values of
[R minus Y]

## Slide 43
Chroma Subsampling
Left – original RGB image:
12 x 8 pixels = 96 pixels
bits for each pixel = 8 red + 8 green + 8 blue
∴ 24b each pixel, total bits = 24 x 96 b
= 2304b (= 288 Bytes)
Bottom left, YCbCr, 4:4:4 : (is also 2304b)
Below, Chroma sub-sampled, 4:1:1:
Luma = 96 x 8 = 768
Chroma = 3 columns of Cr and Cb,
  2 x 8b each C = 8 x 2 x 3 x 8 = 384 b
Total = 768+384 = 1152b (=144 B)
i.e. 50% saving

## Slide 44
Reception / Decoding
Decoding, reverse process ...
  from Chroma sub-sampled to full RGB
note – interpolating lost information
∴ detail is lost in the process
Perceptual (e.g. MPEG, etc ) encoding + decoding is also part of this process and loses a lot more detail
... more later in the module
encoding process
decoding process

## Slide 45
Chroma Subsampling
Luma and chroma components
Weighted sum of gamma-corrected R'G'B‘ tristimulus components
  instead of linear (tristimulus) RGB components
Luminance and colour detail are not completely independent of each another
  "bleeding" of luminance and colour information between the luma and chroma components
    i.e. because of the colour not represented in each pixel, and is interpolated for the final viewed image
    greatest for highly-saturated colours
    noticeable in between the magenta and green (when chroma subsampled)
without colour subsampling
with colour subsampling

## Slide 46
Chroma Subsampling
commonly expressed as a three part ratio J:a:b (e.g. 4:2:2)
number of luminance and chrominance samples in a conceptual region
  J pixels wide
  2 pixels high
Parts
J = horizontal sampling reference (width of the conceptual region)
  usually = 4
a = number of chrominance samples (Cr, Cb) in the first row of J pixels
b = number of changes of chrominance samples (Cr, Cb) between first and second row of J pixels
Alpha - horizontal factor (relative to first digit)
  omitted if alpha component is not present
  equal to J when present

## Slide 47
Chroma Subsampling
Y = Luminance Cb = Blue - Luma
Cr = Red - Luma
4:1:1 - Widely used in JPEG and MPEG
4:2:0 - Used in DVD, JPEG, MPEG
4:2:2 - Used in Studio recordings
4:4:4 - High end applications
(Note - Cb and Cr is colour difference information for the related pixel; not the red/blue value itself!)
full horizontal resolution, full vertical resolution
¼ horizontal resolution, full vertical resolution
½ horizontal resolution, full vertical resolution
½ horizontal resolution, ½ vertical resolution

## Slide 48
MPEG –
Coding For
Moving Images
Intraframe and Interframe Compression

## Slide 49
Video Sequence
Group Of Pictures (GOP)
GOPs – Groups Of Pictures
Group of Pictures (GOP)
Header + series of one of more pictures
3 types of pictures: I, P, B
Provides a regular structure of video content
  recurring pattern of pictures
  allow easy access to the video stream
For TV the GOP is 12 pictures ( 0.5 s of a projected at 24 frames / s movie
For NTSC 30 fps, uses 15 pictures

## Slide 50
Basic Principles for Moving Elements in Images
Blocks Identical or nearly-identical in following frames
Blocks with nearly* identical characteristics are replicated; spatial displacement is coded with a motion vector
*we’ll deal with the “nearly” part shortly …

## Slide 51
Difference Coding
Amount of information in the difference between the two frames is a lot less than in Frame 2
motion in the scene will increase the differences
analyse motion
  … where each block moved since previous frame
  encode motion as vector -
    x- and y- direction vectors
  encode differences for the moved block like a jpg,
  i.e. DCT, quantization, RLE (zig-zag), Huffman
  (… but this jpeg is very simple to encode due to little changed information in the image)
see - http://www.cs.ucl.ac.uk/teaching/GZ05/08-h261.pdf

## Slide 52
Streaming
HTTP, HLS
  MPEG-DASH
RTP/RTSP

## Slide 53
The original solution for streaming
  ... overtaken by RTP/RTSP based for large IPTV deployments
  ... more recently back in favour
used generic HTTP servers (often based on Apache or Windows Server)
HTTP Streaming
Early days
Limited bandwidth available
    “Download and play”
        no lookahead seeking or random access
      Multiple viewers – server bandwidth issues
Apple introduce progressive download

## Slide 54
HTTP server/client – stateless
  HTTP-streaming: retrieves consecutive short chunks on as-needed basis
      little waste (the video is delivered as it is watched)
          server efficiently serves more streams
      Random seeking
        (viewer selects – player retrieves the appropriate chunks)
    firewall friendly
    can utilise HTTP caching mechanisms
    less expensive to implement (no streaming server required)
      scale more cheaply and effectively to serve available users
Streaming Media Protocols – HTTP addresses RTMP Issues
RTMP/RTSP/HTTP – state of the market
little impetus for RTMP/RTSP sites to change –still widely used
new installations - overwhelming view – HTTP
in fact most video content is delivered via plain old HTTP progressive download

## Slide 55
Client
Server
http GET
http GET
Segment timing:
10 seconds = reasonable balance for most broadcast content
Shorter segments
= more frequent refreshes of the index file
.. unnecessary network overhead for the client
Longer segments
= latency and initial startup time
Media Formats
e.g. video: H.264 / VP9,
  audio: .aac / Opus, etc
  video + audio file segments unwrapped
  … but certain applications –
  can be wrapped in MPEG-TS (DVB)
Audio segment
Video segment
etc
HTTP Streaming

## Slide 56
HTTP Live Streaming - HLS (DASH is similar)
Apple (part of QuickTime and iOS)
HLS v5 announced in Sept16
support for Fragmented MP4

## Slide 57
Production and Distribution Technology UG2
T3: Harmonic Analysis
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 58
Time and Frequency Domains
represents a signal as a mathematical function a computer* can handle
*computer = PC, Set Top Box, Console, player …
converts a time-based signal into a frequency-based signal for processing
  … and back again for playout
Time Domain
Frequency Domain
From the Goldwave Audio editing program
signal amplitude
time
frequency
signal amplitude

## Slide 59
Time and Frequency Domains

## Slide 60
Series
Mathematical Series, example:
sum
limits

## Slide 61
Fundamental
(1st Harmonic)
2nd Harmonic
3rd Harmonic
4th Harmonic
5th Harmonic
6th Harmonic
:
:
12th Harmonic
Harmonics

## Slide 62
Waveform Synthesis
f = sin(x)

## Slide 63
f = sin(x)
f = 1sin(3x)
3
Waveform Synthesis

## Slide 64
f = sin(x)
summation of amplitudes
f = 1sin(3x)
3
Waveform Synthesis

## Slide 65
f = sin(x)
summation of amplitudes
f = 1sin(3x)
3
f = sin(x) + 1sin(3x) 3
Waveform Synthesis

## Slide 66
f = sin(x)
summation of amplitudes
f = 1sin(5x)
5
f = 1sin(3x)
3
f = sin(x) + 1sin(3x) 3
Waveform Synthesis

## Slide 67
f = sin(x)
summation of amplitudes
summation of amplitudes
f = 1sin(5x)
5
f = 1sin(3x)
3
f = sin(x) + 1sin(3x) 3
Waveform Synthesis

## Slide 68
f = sin(x)
summation of amplitudes
summation of amplitudes
f = 1sin(5x)
5
f = 1sin(3x)
3
f = sin(x) + 1sin(3x) 3
f = sin(x) + 1sin(3x) + 1sin(5x) 3 5
Waveform Synthesis

## Slide 69
Fourier Series – (here just the sine)
where:
= the fundamental frequency
= amplitudes of successive terms
n = the series
t = 2f (f= frequency)
i.e. the
coefficients
increasingly high frequency components … (usually) lower amplitudes
…...
… Discrete Cosine Transform is similar

## Slide 70
sin and cos
cos 
sin 
0 90 180 270 360 450 540 630 720 810 900
Compare sin and cos:
note that for any value of sin, cos got there 90° earlier
i.e. cos leads sin by 90 °
... or sin lags cos by 90 °

## Slide 71
An expansion of a periodic function f(x) (or f(t))
  in terms of an infinite sum of sines and cosines
makes use of the orthogonality relationships of the sine and cosine functions (odd / even functions)
Fourier Series

## Slide 72
Fourier Series
where:
= the fundamental frequency
= amplitudes of successive terms
n = the series
t = 2f (f= frequency)
i.e. the
coefficients
increasingly high frequency components … (usually) lower amplitudes
…...
Series contains sin and cos to accommodate for odd and even functions of f(t)

## Slide 73
Waveform Synthesis - Fourier Transforms
increasingly high frequency components … (usually) lower amplitudes
…...
f = sin(x) + 1sin(3x) + 1sin(5x) 3 5
(1)
e.g. in this waveform (comprising only sine functions):
Note – the highest frequency in the series is the Nyquist frequency (i.e. below half the sampling frequency)

## Slide 74
Example – the square wave and its sine-wave components
freq
Time Domain – to Frequency Domain
Harmonics
Coefficients (i.e. amplitudes)

## Slide 75
Perceptual Coding
for JPEG Image Compression

## Slide 76
Frequency: amplitude with time
sin 
sin 
0 90 180 270 360 450 … etc
angle 

## Slide 77
“Spatial” Frequency (horizontal)
sin 
0 90 180 270 360 450 … etc
angle 
sin 

## Slide 78
“Spatial” Frequency (vertical)

## Slide 79
“DC Conditions”
sin 
0 90 180 270 360 450 … etc
angle 
sin 
0 90 180 270 360 450 … etc
angle 
1
0
i.e. the whole sin  waveform has been lifted by a constant 1 volt
1 volt

## Slide 80
DC Conditions … in an image ???
+
0
-

## Slide 81
The image is the correlation of …
… this harmonic content
+ this harmonic content
+ this DC
Image broken in to 8 x 8 pixel blocks
The codec decides how to describe each block as a correlation of ...