## Slide 1
Broadcast Technology UG1
Signals
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
The Signal
The Channel
From Analogue to Digital
Bandwidth
Why Sine Waves ?
Pulse Transmission, Interference (ISI)
Noise
Signal Distortion
IRE Levels

## Slide 3
Why
Sine
Waves ???

## Slide 4
sine (sin):
a
(opposite)
b
(adjacent)
c
(hypotenuse)

sin  =
i.e. a ratio of the opposite side and hypotenuse of a right-angled triangle
for  = 0° ⇨ 90 °
sin  = 0 ⇨ 1.00
notable value:
sin 30 ° = 0.500
Why sine (sin) Waves?

## Slide 5
sine (sin)
a
b
c

0° 30° 90°
1.0
0.5
0
sin  =
Plotting values of sin  between 0° and 90° gives a graph ....
sin


## Slide 6
sine (sin)
sin 
0° 30 ° 90° 150° 180°
1.0
0.5
0
as  continues past 90° and towards 180°, the value sin falls back to 0
a
b
c



## Slide 7
sine (sin)
a
b
c

as  continues past 180°, sin  goes negative
... then falls from 0 (at 180°) through -1 (at 270°)
... and back up to 0 at 360°
360° = 0°
... and the cycle starts over ...
0 90 180 270 360 = 0 450 = 90
1
0
-1

sin 

## Slide 8
sin 
sine (sin)
As  continues, the curve of sin  forms a sin wave
0 90 180 270 0 90 180 270 0 90
360 450 540 630 720 810 ………

## Slide 9
Waveforms: Wavelength, Frequency and Period
Wave “travelling”, imagine an observer counting the wavelengths:
frequency = number of wavelengths / unit of time
i.e.
velocity = frequency x wavelength
One wavelength “”
v
f 
unit of wavelength
= any length unit
mm, cm, m ...

## Slide 10
The period of the wave = T = the length of time for one wavelength
One wavelength “”
unit of wavelength
= any length unit
mm, cm, m ...
f T= 1 second
Period of the wave, time in seconds
(more likely mS or S)
Waveforms: Wavelength, Frequency and Period

## Slide 11
Radian
= the angle where the arc swept = the radius of the circle
i.e. 1 Rad = 180/π° ≈ 57.3 °
i.e. 2π Rad = 360 °
So if we take an arc around the circle the same length as the radius (r)
It will trace an angle of 57.3°
… call this an angle = 1radian
But consider - how many radius lengths are there around the circmference?
= 2πr ÷ r
= 2π
r
D
360°
Circumference
= πD
= 2πr
Radians

## Slide 12
The Signal

## Slide 13
Shure SM58 Specifications
Output voltage ~ 0.19mV =
http://www.shure.com/idc/groups/public/documents/webcontent/us_pro_sm58_specsheet.pdf

## Slide 14
AC Power supply in UK (and the rest of Europe) is 230V AC
AC = “alternating current”
… alternating at a rate of 50 Hz (cycles per second)
North America = 120V @ 60Hz
Varies quite a bit around the world
RMS Voltage, e.g. Mains Supply
0V
Peak = ~340V
RMS = 230V
f-= 50Hz
t
Problem: What is the “average” value of the sinusoidal waveform?
Answer: Zero … but obviously this is misleading
Mathematically this is expressed as RMS … Root Mean Square
Practically, could consider the RMS voltage as the voltage required to produce the equivalent power (e.g. heating effect ) as a DC voltage

## Slide 15
Values 0 7 10 7 0 -7 -10 -7
Squares 0 49 100 49 0 49 100 49
Sum of squares = 396
Average of squares = 396/8 = almost 50
Square root = approx 7
With more intervals the rms average turns out to be
= (peak value) / √2
= peak value/1.41
= 0.707peak value
http://www.practicalphysics.org/go/Guidance_107.html
Root Mean Square
For example: suppose the time samples are as shown in the diagram:
(note: eight samples)

## Slide 16
0V
Peak = ~340V
RMS = 230V
one cycle = 1/50th second
Vpeak = √2 x Vrms
√2 = 1.414
240V RMS, 50Hz:
tolerance of +10%, -15%
t
Root Mean Square – the Power Supply

## Slide 17
time
amplitude
Analogue Signal - for example …
time
= zero?
= zero?
volts?
DC Bias

## Slide 18
time
amplitude
= zero?
Analogue Signal - for example …

## Slide 19
The Channel

## Slide 21
Transmitted Signal
Received Signal
Channel
Signal and Channel
External Influences
(interference)

## Slide 22
Analogue Signal Problems In The Reproduction Process
Original signal
Reproduced signal
phase effects
interference
other signals crosstalk
various intermodulation products
mechanical transducer ineffective / inefficient

## Slide 23
Information Transmission, Signal Encoding
Information
Source Coding
Channel Coding
Modulation
Interference
Distortion
Attenuation
Demodulation
Channel Decoding
Information
Source Decoding
bit errors
Transmission Link
Source Information
coded data in as small space as possible (compressed, etc)
signal received – reverse processes
transmission is subject to noise interference
aim – to approach the Shannon Limit
Channel coding
appropriate error protection method
... depends on channel characteristics
Modulation
… on to carrier
jeremy.foss@bcu.ac.uk
MSc Digital Broadcast Technology: Signal Compression and Encoding

## Slide 24
Pulse Transmission,
Interference (ISI)
Eye Diagrams
Original generated signal → transmission system → received signal

## Slide 25
Theoretically perfect random pulse train
Pulse train: two or three pulse periods successively sampled, overlayed on each other
Random pulse train affected by imperfect transmission medias
Practical pulse train: successively sampled, overlayed
Quality of the Transmission

## Slide 26
Jitter
theroretical clock pulses
actual clock pulses
Distribution of clocking arising through various issues, e.g. arising through the nodes transmission
pulse train cleaned up at receiver
degraded pulse train received
smearing and delay
overshoot (“ringing” at filters)

## Slide 27
DATA GENERATOR
CHANNEL
OSCILLOSCOPE
Y-INPUT Ext Trigger
Clock In
Clock Out
Eye Diagram - test set-up
Sampling Instant
one pulse interval

## Slide 28
a run of pulses are fed into a scope –
locked on to one or two pulse widths
superimposed 1’s and 0’s
ISI – Eye Diagram
Demonstrated by “eye pattern” analysis of impulse response
It indicates the performance of a transmission system
original generated signal → transmission system → received signal

## Slide 29
Different Eye Patterns
Signal + timing errors - eye closing
Signal only - various small individual random distortions (but likely OK)
- eye is “open”
Signal + noise - eye closing (amount depends on noise)

## Slide 30
Can reveal important information
best point for sampling
SNR at the sampling point
amount of jitter and distortion
time variation at zero crossing - jitter
ISI – Eye Diagram
http://www.edn.com/design/test-and-measurement/4389368/Eye-Diagram-Basics-Reading-and-applying-eye-diagrams

## Slide 31
Multipath
an undesirable effect – reflections of radio waves hitting various objects in the environment
unavoidable
http://www.st-andrews.ac.uk/~www_pa/Scots_Guide/RadCom/part19/page3.html
i.e. interference between a symbol and its own reflection … another form of ISI

## Slide 33
Bandwidth

## Slide 34
Frequencies, Bandwidth – fundamental freqs
frequency
∼80Hz
∼2KHz
Bandwidth = ∼2kHz

## Slide 35
Frequencies, Bandwidth – add the harmonics
frequency
∼80Hz
Bandwidth = ∼20kHz

## Slide 36
freq
~20kHz
Bandwidth – Analogue Signals
Bandwidth = 20KHz
Baseband signals – the range of frequencies of the original signal
… unmodulated, not frequency shifted
~20Hz

## Slide 37
freq
40kHz
Sampled Bandwidth – Analogue Signals
Telephone bandwidth = 4KHz
∴ ten calls can be stacked into a 40KHz bandwidth
40KHz communications channel

## Slide 38
Digital Signals, Bandwidth and Spectra
Does Analogue Bandwidth relate to Digital Bandwidth?
... it depends ... but not an accurate relationship
Digital Bandwidth: Data rate in bits/second
= bandwidth of the communications channel
e.g. 20kHz signal, sampled at 44.1kHz
  with 16b coding (= 65536 quantisation levels) = 44100 x 16b per second
  = 705600 b/s = 689kb/s
  … for stereo = 689 x2 = 1378kb/s = 1.378Mb/s
compress to mp3 @320kb/s; bandwidth = 320kb/s
compress this to mp3 (or aac) @128kb/s; bandwidth = 128kb/s
typical SD TV channel, avc =>3Mb/s
typical HD TV channel, avc = >8Mb/s
depends on no of bits, compression, etc
but consider the practical transmission channel
… the modulation level; channel S/N

## Slide 39
Noise

## Slide 40
Noise
IMPORTANCE
for audio or video:
  … noise is an obvious disturbance to the original noiseless signal
for data transfer
  … noise can obliterate data; can reduce data rates; require retransmissions, etc
Nature of noise
typically random – a stochastic process
Noise is manifested as a voltage
… alongside the voltage of the original signal
Various causes of noise
(see noise types …)
Need ways to measure and represent noise
signal / noise ratio
Useful noise (sometimes)
white and pink noise

## Slide 41
Noise
signal
noise
signal + noise

## Slide 42
Channel Noise
clean signal
channel noise
E/M interference
additive
noise affected signal

## Slide 44
Sensor Noise
any active circuit (and many passive circuits) including camera sensors will produce noise ...
+ =
+ =
photocell charge plus positive noise spike = brighter pixel
photocell charge plus negative noise spike = darker pixel
original image = pure grey tone
recorded image = noisy grey tone
At the instant of image capture:

## Slide 45
Movement of electrons in ONE direction gives rise to ELECTRIC current
... is really a movement of CHARGE
No field – haphazard movement
... net current flow is zero
Conductors (metals, e.g. Copper) – have loose bindings to their outer electrons
Conduction
-
-
-
electrons progress through conducting medium attracted towards positive electrode of the electric field.
they may be attracted to a nearby positive ion, or may continue drifting towards the anode

## Slide 46
Conductors
-
-
-
electron flow
current flow
CONDUCTORS
allow electrons to flow
electrons easily freed and move through lattice of atoms when electric field is applied
e.g. – gold, copper, tin, carbon
INSULATORS
restrict movement of electrons
electrons firmly bound to atom

## Slide 47
Semiconductors
Operate as both/either conductors or insulators under controlled circumstances
… i.e. within a circuit
Applications
diodes, transistors – CPUs (millions of transistors), sensors
Some semiconductors are intrinsic
... but usually doped to assist the semiconductor action
Semiconductor materials
Germanium (Ge), Silicon (Si)
Have impurities (doping) added to their crystal lattice structures to make n-type or p-type semiconductors

## Slide 48
Semiconductor – Silicon atom
(positive charge)
(neutral charge)
(negative charge)

## Slide 49
Semiconductor – Silicon atom
Covalent bonds – share atoms to bond and join atoms …
… into a lattice structure

## Slide 50
Semiconductors (simplified 2D view of the lattice)
for n-type
“Donor” impurities
  Antimony
  Arsenic
  Phosphorus
introduces “free” electrons
Sb
Si
Si
Si
Si
donor impurity introduces free electrons
Antimony (Sb) impurity
B
Si
Si
Si
Si
donor impurity creates a hole
Boron (B) impurity
for p-type
“Acceptor” impurities
  Boron
  Aluminium
  Gallium
introduces “holes” – room for free electrons

## Slide 51
P-N Junctions
p-type silicon
n-type silicon
current readily flows
current doesn’t readily flow

Transistors
here – Bipolar junction
  top – NPN transistor
  bottom – PNP transistor
other types – FET (field effect)
Semiconductor Diode

## Slide 52
P-N Junctions
p-type silicon
n-type silicon
current readily flows
current doesn’t readily flow

Semiconductor Diode

## Slide 53
SHOT NOISE
Random noise
due to electron flow – i.e. discrete events
  … rather than a smooth flow
also photons in an optical transmission
significant problem with low signal levels
generally across all frequencies
current flow
Noise - Causes
THERMAL NOISE (JOHNSON–NYQUIST NOISE)
thermal effects agitating the electrons in a circuit
increases with temperature
  i.e. kinetic energy of molecules of the crystal lattice of semiconductor
time
noise voltage
noise voltage
frequency

## Slide 54
Noise - Causes
BURST NOISE; IMPULSE NOISE (“popcorn noise”)
noise spikes in the lower audio range
different distinct levels of noise
in audio circuits amplified into speakers, sounds like popcorn popping
occurs in semiconductors
due to imperfections in the semiconductor material
FLICKER NOISE
recombination / reforming of electron holes in a semiconductor structure
occurs in low frequecy range
  dropping off towards higher freqs with a 1/f characteristic (like Pink Noise)
noise voltage
freq
noise voltage ∝
Random white noise (e.g. shot noise) (in time and freq)
Impulse (popcorn) noise
time

## Slide 55
Noise – Other Causes
Several other causes of noise:
nearby interference sources
contact noise - oxidation on contacts
avalanche noise - caused at a semiconductor junction
partition noise - electrons flowing between a number of electrodes
grain noise – e.g. granularity of media – e.g. tape coatings, etc
etc

## Slide 56
White Noise
Flat power-spectral density
i.e. noise power is the same across the frequency spectrum
(theoretically from 0Hz to ∞ Hz
practically – over a specified frequency range
1000 10,000
freq (Hz)
0
-5
-10
-15
-20
-25
-30
-35
-40
intensity (dB)

## Slide 57
Pink Noise
Spectral Density is inversely proportional to frequency
i.e. intensity ∝
actually drops 3dB / octave
(again) theoretically 0Hz to ∞ Hz
1000 10,000
freq (Hz)
0
-5
-10
-15
-20
-25
-30
-35
-40
intensity (dB)

## Slide 58
Noise – White, Pink
Depending on frequency spectrum, i.e. the amplitude of the noise voltages across the freq range
WHITE NOISE
has an increased intensity of 3dB for each octave increase
because each octave is twice the frequency range of the previous octave
100…200……400……………….800…………………………………..1.6KHz….
freq (Hz)
1….....…2…………………..3…………………………………………4 …. octaves
PINK NOISE
power density drops 3dB intensity per octave
therefore amount of power is the same in octave ranges:
e.g. power in range 100 – 200 Hz
= power in range 1KHz – 2 KHz
therefore is useful for audio measurements

## Slide 59
Frequency and Time Domains
This response (from the previous slide) is of intensity over the frequency range … i.e. observed in the the frequency domain
This is a snapshot in time of the frequency domain
signal amplitude
time
Observing the noise-producing circuit over a period of time, we see only the changes in signal amplitude (i.e. intensity)

## Slide 60
Noise is Probabalistic
i.e. – (below) - can’t be certain that intensity is at any specific value at any specific frequency
… or that noise voltage amplitude = any specific value at any specific time
time
signal amplitude

## Slide 61
Noise is Probabalistic; Measuring Noise
As noise is random, it’s mean value will be (usually) zero
∴ use mean square values for measurements of the dissipated noise power
The effective noise power of a source is measured in root mean square (RMS)

## Slide 62
Measuring Noise: Signal to Noise Ratio (SNR)
Comparison of
the power of the required signal
against the power of the (usually) unwanted noise
measured in decibels (dB)
SNR (dB) =
signal
noise

## Slide 63
photon strikes the diode
excites an electron
creating a free electron and a (positively charged electron hole)
current is produced - photocurrent
Photoelectric effect

## Slide 64
Dynamic Range – Camera Sensor, Signal to Noise
signal: the light which hits the camera sensor
noise is unavoidable
can be small relative to the signal
  appears to be nonexistent
noise low ratio = much noise high ratios = very little visible noise
signal strength
constant noise level
image signal
Signal to noise ratio (SNR)
compare relative amounts of signal and noise
used for any electronic system
http://www.cambridgeincolour.com/
light level

## Slide 65
Dynamic Range – Camera Sensor, Photosites
Black level – at low level, is limited by the signal required to overcome the sensor noise.
White is limited by the highest level of charge accommodated in the photosite
... Depends on the capacity of the photosite. A lower capacity element may accommodate less light before it is saturated
… smaller sensors usually have lower capacities
… compact cameras, smaller sensors
Camera sensors – each photosite accumulates charge in response to the incident light
Figures below – accumulation of charge is like filling buckets with balls (or water ... whatever ...); actually electrons
Contrast ratio is the ratio between lowest level and highest level
lower ISO levels usually have bigger dynamic ranges, since there is less noise at low ISO black levels
Camera dynamic range usually measured in f-stops
e.g. contrast ratio of 1024 ≡ 210,
i.e. 10 stops

## Slide 66
(state
Dynamic Range – Camera Sensor, Photosites
Dynamic Range = Full Well Capacity
Camera Noise
= 20 log10 Full Well Capacity (stated as number of electrons)
Camera Noise (stated as number of electrons)
… … stated in decibels (dB)
Dynamic range improves if the full-well capacity is higher
… and the camera noise is lower
Parameters that affect the dynamic range:
Pixel size (Full-well capacity)
Temperature (Dark noise)
Readout rate (Readout noise)

## Slide 67
Noise Factor, Fn
The noise factor of a system is
the ratio of output noise power (Pno)
to input noise power (Pni):
Ideally Fn = 1
(because noise out would = noise in)
Noise sources are subject to temperature (thermal noise)
∴ needs to be measured at a standard temperature = T0 = 20ºC; = 293K
Fn
specifies how much additional noise the device will contribute to the noise already from the source.
Fn =
Fn =

## Slide 68
Noise Figure, NF
Noise Figure NF is the Noise Factor in dB
NF = 10 Log10 Fn
Noise Factor Fn:
Fn =
But – SNR is measured in dB
∴ NF = SNRin – SNRout

## Slide 69
Signal Distortion
Frequency Distortion
certain frequencies are boost or cut unevenly across the audio spectrum
stated in equipment specifications as the components frequency response
Phase Distortion
given frequency from a complex waveform takes longer to pass through a signal chain than others: i.e. a phase shift in the individual frequencies
(amplitudes may be amplified equally over the entire frequency band, but the composite waveform has been varied)
Total Harmonic Distortion (THD)
most commonly known form of distortion
directly related to the percentage of harmonics generated by the components in the signal chain
Measured using Fourier Analysis
Intermodulation (IM) Distortion
modulation of combinations of spurious frequencies
the combination of resulting frequencies are equivalent to the sum and/or difference of integral multiples of the individual frequencies of a complex waveform
Transient Intermodulation (TIM)
solid-state amplifiers use negative feedback in order to improve frequency response and reduction of harmonic distortion
occurs during high-frequency music passages

## Slide 70
Signal Distortion
Perfect Amplifier
?

## Slide 71
Signal Distortion
Unintended distortion
component and board layout
connecting cables
component interiors
  capacitance in transistors
capacitance to earth (of casing)
… causes filtering effects

## Slide 72
Signal Distortion
Uneven frequency response
gives phase differences across the signal bandwidth
Lower freqs: OK
in
out
Circuit
different frequencies have different phase responses

## Slide 73
Signal Distortion
Transient response – circuit can’t react immediately to changes in signal
in
out
circuit produces rounding of edges due to limted frequency response (due to filtering, as previous)
… or circuit over-runs rise and falls in transients, causing “ringing” effects
or …

## Slide 74
in
out
Signal Distortion
out
out
Successive forms of compression
clipping the waveform
causes high freq harmonics
(ref Fourier – many high freq harmonics required to turn a sine wave to square wave)
e.g. caused by power supply “sag”

## Slide 75
Signal Distortion
in
when an amplifier gain is set too high
  by mis-calculation or design for a specific effect
the amplifier is trying to amplify the signal beyond the range of the supply voltage
(simplified case):
  e.g. an amplifier gain = 100 with a 0.5V input, but the power supply is 40V
out
limit of undistorted amplification
the signal is amplified and limited to the the power supply values

## Slide 76
Intermodulation Distortion (IM)
from ESP - http://sound.westhost.com
Occurance: two different frequencies are being amplified simultaneously
one of frequency much lower than the other
high frequency signal modulated by the low frequency
different from the signals simply adding (as they are supposed to)
effect (musically speaking) is that the sound is muddied
Individual instruments become difficult to separate; their harmonics blend into a 'wall of sound'

## Slide 77
Intermodulation Distortion (IM)
Signal includes components that are
  the sum of the two frequencies and
  the difference between the two frequencies
usually a fraction of a percent of the original signal
over 1% IM is noticeable
over 3% is annoying
from ESP - http://sound.westhost.com

## Slide 78
Harmonic Distortion
The production of harmonic frequencies by an electronic system when A signal is applied at the input
when an input signal goes through nonlinear electronic circuitry, the output signal will include some harmonic distortion (or unwanted frequencies)
the frequency of each unwanted frequency is a multiple
  (x1, x2, x3, etc.) of the centre frequency of the input signal
Odd And Even-order Distortion
if the frequencies of the distortion are 2, 4, 6, etc., times the centre frequency, it's even-order harmonics
if the frequencies of the distortion are 3, 5, 7, etc., times the centre frequency, it's odd-order harmonics

## Slide 79
Total Harmonic Distortion
The ratio of the powers of:
sum of the power of all the harmonic components
the fundamental (required) signal
:
Usually expressed as a %
i.e. ∑ power of all harmonics
power of fundamental freq
= THD%

## Slide 80
http://members.aol.com/sbench102/thd.html
Total Harmonic Distortion
compare these even harmonic distortions

## Slide 81
Total Harmonic Distortion
Odd harmonic distortions
compare the lower two:
this has higher THD in the 2nd and 3rd harmonics
… this has lower THD in the 2nd and 3rd harmonics

## Slide 83
From Analogue to Digital

## Slide 84
Analogue vs Digital Signals
Analogue
offers an infinite range from 0 to V volts
at any point the signal voltage should be exactly a specific voltage
but there are many points in the chain where this specific voltage may be corrupted and subject to distortion (as previous slide)
Range of signal voltage:
Digital
offers a choice of only two values
  Logical “0” = 0 volts
  Logical “1” = V volts
(simplisticly...) a decision point between 0 and V volts
  above this = “1”
  below this = “0”
we can be (almost) certain that the signal is in either one state or the other
allows the signal to suffer much distotion before it is mis-read
0 volts
V volts

## Slide 85
0 volts
V volts
Distortion Affecting Digital Signals
Data: “1”........ “0”......... “1”.......... “1”.......... “1” ......... “0” .......... “1” ........... “0” .......
“1” = V volts ±y volts
“0” = W volts ±z volts
Specified Tolerances for Signals
Tolerance on pulse shapes and timings
(e.g. in relation to a CLOCK)
rise time
fall time

## Slide 86
Data: “1”........ “0”......... “1”........ “1”......... “1” ........ “0” ........ “1” ......... “0” .......
Time:
Digital Signal Timing - Clocking
Transmitting and receiving ends must agree on times at which data is read – the CLOCK frequencies
Clocking information must also be inferred in recorded media (CDs, etc)

## Slide 87
Go Digital!
Digital Signals are either “1” or “0”
Can add codings e.g. for error detection / correction
if 1’s and 0’s can represent the analogue voltage, the produced / reproduced signal can be much more robust and faithful
Aim: to keep the process digital as much as possible
Signal
Generation
Mixing
Production
Mastering
Master
Signal
Reproduction
Mass Produced Units
Digital domain
Analogue domain
Analogue domain

## Slide 88
Signal
Generation
Mixing
Production
Mastering
Master
Signal
Reproduction
Mass Produced Units
Digital domain
Analogue domain
Analogue domain
digital signals
digital mixing and mastering
digital reproduction format
digital players
The Digital Chain of Production / Reproduction

## Slide 89
Audio
Signal
Sampling
ADC
Digital
Data
DSP
Transmission
Process / Integrate with other services
Storage
DAC
Audio
Signal
Analogue Domain
Digital Domain
Digital
Data
DSP
DSP = Digital Signal Processing
ADC, DAC, Analogue and Digital Domains
Analogue signal in
Analogue signal out

## Slide 90
Additional slides
Binary Systems
Sound, SPL and the logarithmic relationship
Sound measurement
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 91
e.g. the number 2549
is – 2 x Thousand ... 5 x Hundred ... 4 x Ten ... 9 x one
i.e. 2 x 1000 + 5 x 100 + 4 x 10 + 9 x 1 = 2549
The composition of the decimal system in a more complex way:
Units are 100 = 1
Tens are 101 = 10
Hundreds are 102 = 10 x 10
Thousands are 103 = 10 x 10 x 10
… and so on
So 2549 is actually:
(2 x 103) + (5 x 102) + (4 x 101) + (9 x 100)
= 2000 + 500 + 40 + 9 = 2549
Counting in Base 10
(anything)0 = 1

## Slide 92
Counting Bases
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39…
Counting to the base 10:
Counting to the base 7:
0
1
2
3
4
5
6
10
11
12
13
14
15
16
20
21
22
23
24
25
26
30
31
32
33
34
35
36
… this is the decimal system
40
41
42
43
44
45
46
50
51
52
53
54
55
56
60
61
62
63
64
65
66
100
101
102
103
104
105
106
least significant digit, i.e. units have least value compared to tens and hundreds

## Slide 93
Counting Bases – The Binary System
Binary System = counting to the base 2
0
1
10
11
100
101
110
111
binary digits
bits
1000
1001
1010
1011

## Slide 94
Counting Bases – The Binary System
Binary System = counting to the base 2
0
1
10
11
100
101
110
111
binary digits
bits
1000
1001
1010
1011
least significant bit … “LSB”
most significant bit … “MSB”

## Slide 95
The Binary System
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
... it’s all about spotting the patterns ...

## Slide 96
The Binary System
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Filling in the “leading bits”
e.g.
Binary 10 = decimal 2
… filling in the leading bits …
  10 becomes 0010
  … or even 00000010
it’s still = decimal 2, but probably less confusing if we have a digital system based on 4 or eight bits
Digital systems can have 8, 16, 32 or 64 bits (e.g. computer buses)

## Slide 97
The Binary System
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
least significant bit … LSB
most significant bit … MSB
This is using four bits to count
= “four bit binary”
translating decimal numbers to binary
(here, from 0 to 15) is
“binary coded decimal” ... BCD
For three bits there are 8 combinations
... from 0 to 7
For four bits there are 16 combinations
... from 0 to 15
... and so on

## Slide 98
The Binary System
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
LSB
consider the frequency of change for each column – notice the pattern

## Slide 99
The Binary System
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
The frequency of the second column is half the LSB column

## Slide 100
The Binary System
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
The frequency of the third column is half the second

## Slide 101
The Binary System
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 102
The Binary System
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
now consider each of these binary pulses being transmitted as signals on a system
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 103
The Binary System
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
we can repeat the four LSB columns .. but if we add a new MSB column (red) we can double the counting capacity
columns are the same

## Slide 104
The Binary System
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
32
33
34
35
36
37
38
39
40
41
42
43
44
45
46
47
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
Now add another column of “10”

## Slide 105
The Binary System
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
10
32
33
34
35
36
37
38
39
40
41
42
43
44
45
46
47
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
48
49
50
51
52
53
54
55
56
57
58
59
60
61
62
63
64
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
11
11
11
11
11
11
11
11
11
11
11
11
11
11
11
11
1000000

## Slide 106
The Binary System ... The Powers Of 2
Let’s review binary counting from the point of view of the powers of 2:
20 = 1
21 = 2
22 = 4
23 = 8
now assign these values to each of the columns ...
MSB ... ... LSB
23 22 21 20
=8 =4 =2 =1
0 0 0 0 = 0 .... .... .... .... .... .... = 0
0 0 0 1 = 1 x 20 .... .... .... .... .... .... = 1
0 0 1 0 = 1 x 21 .... .... .... .... .... .... = 2
0 0 1 1 = 1 x 20 + 1 x 21 = 1 + 2 = 3
0 1 0 0 = 1 x 22 = 4 .... .... .... .... = 4
0 1 0 1 = 1 x 22 + 1 x 20 = 4 + 1 .... = 5

## Slide 107
The Binary System ... Milestones
Specific patterns that are fairly recognisable, or lodge in the memory after lots of use (!)
0000 = 0
0010 = 2
0100 = 4
1000 = 8
10000 = 16
100000 = 32
11 = 3
111 = 7
1111 = 15
11111 = 31
1010 = 10

## Slide 108
Hexadecimal
Four bit binary has the capacity to count from 0 to 15
(i.e. 16 combinations)
5 bit binary ... 0 to 31 .... 32 combinations
6 bit binary ... 0 to 63 .... 64 combinations
7 bit binary ... 0 to 127 .... 128 combinations
8 bit binary ... 0 to 255 ... 256 combinations
In hexadecimal
For four bit (0-15) alpha-numeric characters are used to count beyond decimal 9:
8
9
10
11
12
13
14
15
1000
1001
1010
1011
1100
1101
1110
1111
=
=
=
=
=
=
=
=
0
1
2
3
4
5
6
7
0000
0001
0010
0011
0100
0101
0110
0111
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
A hexadecimal number is preceded with the hash character “#”
e.g. hex C is written as #C

## Slide 109
8
9
10
11
12
13
14
15
1000
1001
1010
1011
1100
1101
1110
1111
=
=
=
=
=
=
=
=
0
1
2
3
4
5
6
7
0000
0001
0010
0011
0100
0101
0110
0111
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
#0
#1
#2
#3
#4
#5
#6
#7
#8
#9
#A
#B
#C
#D
#E
#F
Hexadecimal
0011 1011 = #3B = decimal 59
0111 1111 = #7F = decimal 127
0100 0101 = #45 = decimal 69
1010 1101 = #AD = decimal 173
Note even if a hex number is only numric characters, the decimal equivalent will be different

## Slide 112
Linear / Logarithmic Relationship
Linear relationship
Logarithmic relationship
(Depending on what’s being measured, can be this orientation …
On a linear scale
(ii) On a log scale

## Slide 113
Sound Intensity: The Ear’s Response
The human ear can detect a large range of intensities
Sound measurements are made relative to a
standard threshold of hearing intensity, I0
where I0 = 10-12 W/m2
Measured as the ratio of:
intensity I : threshold of hearing intensity I0 ; i.e. =
Usual context is the sound intensity at the listener’s location
... and relative to the standard threshold of hearing (I0)
Wm-2
i.e. I(dB) = 10log10
Power
Area
Intensity =
Decibels:
a ratio of one quantity compared to another
Acoustics:
sound
Electronics, signals:
power
voltage

## Slide 114
Logarithms
bn = a … e.g. 103 = 1000
logb(a) = n i.e. log10(1000) = 3
example (ii) since 100.301=2
so log102 = 0.301
Used for calculations, e.g. multiplication:
log (m x n) = log(m) + log(n)
log (m / n) = log(m) – log(n)
Example: 2 x 3 = 6
… can be calculated from: log10 (2x3) = log102 + log103
= 0.301 + 0.477
= 0.778
this is the log, so we need to antilog: antilog100.778 = 6
Usual bases are log10 or loge
n =
the power to which you raise b (the base) …
to get a

## Slide 115
0 1 2 3 4 5 6 7 8 9 10
3
2
1
-1
-2
-3
Logarithms
passes through x=1
- since anything to
the power of 0 = 1
y = log10x
x
y
log102= 0.301
log1010= 1.00
log100.5= -0.301
log100.1= -1
log100.01= -2
log100.001= -3
etc
log10100= 2.00
log101000= 3.00
y = log10x

## Slide 116
Logarithms
linear scale
log scale
decade
e.g.1 to 10
decade
e.g.10 to 100
decade
e.g.100 to 1000
decade
e.g.1000 to 10000
decade
e.g. 0.1 to 1.0

## Slide 117
Decibels
For measurement of power:
Where a0 is a specified reference level
This can usually (conveniently) set to =1, so therefore can be ignored
10 times ... because we want decibels
a dB
“just noticable difference”
=1dB
is the ratio of sound a
compared to
the reference level a0

## Slide 118
0dB = no gain, and no loss
if p is 10db greater than q … then p is ten times the power of q
if p is 3dB greater than q … then p is twice the power of q
(in electronics a power gain of x2 = 3dB;
  however, a voltage gain of x2 is 6dB)
Decibels in Practice
Vin
Vout
x100
x10
Cascading Circuits: multiply the gain = add the decibels
20db
Gain = 100 x 10 = 1000
In decibels this is
20dB + 10dB = 30dB
10db

## Slide 119
Example:
The intensity I measured is 10,000 times the threshold
 the ratio of the intensity I to the threshold intensity I0 is 104
the power of ten is 4, and the intensity is 40 dB:
Decibels
log1010,000= 4

## Slide 120
Decibels
decibels:
10log10x … … … x
i.e.
one hundred times = 20dB
ten times = 10dB
if we start with “1”
a tenth is = -10dB
a hundredth = -20dB
etc …
…
…

## Slide 121
Decibels:
For Audio Power
(or other power)
http://www.phys.unsw.edu.au/jw/dB.html
Original sound intensity
TWICE the Power
= +3dB
10x the Power
= +3dB
HALF the Power
= -3dB
SAME POWER
= 0dB

## Slide 122
Decibels – What they sound like
Go here (University of New South Wales) for flash version
http://www.animations.physics.unsw.edu.au/jw/dB.htm

## Slide 123
A,B, and C Contours
Relative Response, dB
Frequency, Hz
20 50 100 200 500 1000 2000 5000 10000 20000
10
0
-10
-20
-30
-40
-50
A
A
B
B & C
C
A-contour - approximates the ear at low sound levels
eliminates inaudible low frequencies; widely used
B-contour - approximates the ear for medium loud sounds; rarely used
C-contour - approximates the ear at very high sound levels
used for traffic noise surveys in noisy areas
Applied to tools to assimilate the human ear
To measure sound loudness, as distinct from an objective intensity measurement, the sensitivity of the ear must be factored in
dBA
dBB
dBC

## Slide 124
The Phon
related to dB by the psychophysically measured frequency response of the ear
At 1 kHz, readings in phons and dB are, defined as equal
The phon scale is then determined for all other frequencies based on subjective listening tests with volunteers
volunteers were asked to adjust the loudness of a signal at a given frequency until they judged its loudness to equal that of a 1 kHz signal
Fletcher-Munson curves - converts dB to phons
depends on sound level (it becomes flatter at high sound levels)

## Slide 125
ELECTRIC POWER, dBm or dBmW
dB (1mW) – power measurement relative to 1 milliwatt.
denoted as X dbm
dBW
dB(1W) – similar to dBm, except the reference level is 1 Watt
0 dBW = +30dBm;
−30 dBW = 0 dBm;
Xdbw = Xdbm − 30
Decibels, Power – Absolute Measurements
30 …
because 30dB is 1000x
and 1W = 1000mW

## Slide 126
Decibels, Voltage – Absolute Measurements
dBu
0.775V as reference , i.e. dB(0.775 VRMS)
voltage relative to 0.775 volts
(diagram, right) the relationship between dBu (the voltage source) and dBm (the power dissipated as heat by the 600 Ω resistor)
      (historical reasons) - the voltage level which delivers 1 mW of power in a 600 ohm resistor (standard reference impedance in telephone audio circuits)
originally dBv, it was changed to dBu to avoid confusion with dBV
dBV
dB(1VRMS)
voltage relative to 1 volt (regardless of impedance)
= 0.775 VRMS

## Slide 127
Most common nominal levels:
Consumer equipment is -10 dBV
Professional equipment is 4 dBu
  Convention - nominal levels always written with sign symbol 4 dBu is +4dBu
In absolute terms
a signal at -10 dBV ≡ a sine wave, peak amplitude of ∼ 0.447 volts
a signal at +4 dBu ≡ sine wave, peak amplitude ∼ 1.737 volts
Line Level

## Slide 129
Moving Coil Meter

## Slide 130
LEDs Circuits
R1 limits current
allows LED to light
protects LED by restricting current through it
restricts amount of current drawn from the power supply to conserve power
www.personeel.glr.nl/koster/elektro/led.htm
Conventionally, the longer connector is the anode (+ve)
Cathode
Anode
Voltage drop
Silicon diodes (all Si diodes, not just LEDs) have a voltage drop of 0.7Volts
e.g. - if power supply = 5V, 4.3V will be dropped across R1
R1

## Slide 131
...pins...
LEDs Circuits
Arrays of LEDs
each LED individually operated
e.g. by logic circuits
to produce simple displays
  bars
  seven segment
  etc
http://www.highwaygold.co.uk/science/technology/electronics/components/optoelectronics/led/

## Slide 132
Dynamic Range: The difference between the highest and lowest acceptable levels.
Arrange for:
  the loudest peaks to be below the maximum level which the system can handle
  and for the quietest signals to be kept well above the noise floor
Meters – mostly for avoiding overloads and maximising signal-to-noise ratio
level meters on recorders and consoles mainly intended as an aid to balancing sound levels
Simply matching peak meter levels between different sources is not consistent
Dynamic range

## Slide 133
RTA & Level-History Metering
Real-Time Spectrum Analyser (RTA)
programme level varies in different parts of the frequency spectrum
many different measuring standards for RTAs (like programme level meters):
http://www.mackie.com/Products/d8b_v3/PlugIns/acuma/acuma.html
Acuma Labs RTA-31
Goldwave - spectrum analysis
meter ballistics
numbers and widths of the separate measuring bands,
meter for history of programme levels

## Slide 134
simplest of meter designs
display an approximation to the RMS voltage level of electrical signals
  (ok for pure sine, but not for complex waves)
will usually read slightly lower than the true RMS value
but still useful and practical
inherently cheap - no complex peak-sensing driver circuitry involved
VU meters on different equipment react differently
VU (Volume Unit) Meter

## Slide 135
Measures 'average' levels:
a sustained sound reads much higher than a brief percussive one
Even when both sounds have the same maximum voltage level:
reading is dependent on
  amplitude
  duration of peaks in the signal
standard VU response and fallback times exaggerate this effect ~300 mS each
∴ transients and percussive sounds barely register at all
… and can cause unexpected overloads
Supposed to be sensitive to both the positive and negative half-cycles
many budget units are sensitive only to one half of the waveform
VU (Volume Unit) Meter

## Slide 136
More precise and expensive than VU
Designed not to catch the fastest transient peaks
show transients which are sustained for a defined time
termed 'quasi-peak' meters
'Type I' meters
integration time of 5mS
'Type II' meters
Integration time ~10mS
∴ levels of transients usually exceed the PPM reading by between 4dB to 6dB
encourages overall programme levels to be driven slightly higher ∴ better S/N
assumes that overloading the briefest transients will be inaudible
effectively a peak-hold condition
PPM (Peak Programme) Meters
some bar-graph level displays are available with a VU response shown as a solid bar plus floating dot above it which registers the PPM level

## Slide 137
Headroom
the ability of the sound system to accommodate loud program peaks
e.g. two sound systems that both operate at the same nominal level
… the system with the greater headroom will be able to handle louder peaks before distorting or breaking

## Slide 138
Headroom Requirements
PA in loud factory environment
needs very high nominal sound level (say 110dB) to overcome machinery but needs only ~6dB headroom
Rock band PA ~10dB headroom
Symphony orchestra concert
probably > 20dB headroom because
average level of the orchestra may be low say 90 dB
but on peaks may momentarily exceed 120dB SPL
∴ needs 30 dB of headroom
… if the sound system is capable of only 20dB of headroom, the peaks will be distorted
change with the nature of the program material and the purpose for which the sound system is operated

## Slide 139
Meter Scales – Comparative Between Meters
Different audio metering scales developed by different industries in different countries
each optimises the display for a specific set of applications
VU: zero point at +4dBu*
Comparison of standards

## Slide 140
e.g. stereo or multi-channel systems
each meter's dynamic response must match to within a tenth of a second and their amplitude responses should be within 0.3dB of each other in the critical areas of the meter range
In order to calibrate VU and PPM meters, it's best to use a mid-frequency sine tone (typically 1kHz), as these signals are the most accurately read by meters which are not truly peak-reading
Multiple Meters Used Together

## Slide 141
Level meters display information about signal voltages
rather than their perceived loudness
meters are only an aid to judging the acoustic balance of audio material
Specialist metering systems required for [perceived] loudness of a programme
taking into account the characteristics of human perception
also - broadcasting organisations are now transmitting hundreds of channels via satellite, cable and the internet
impossible to monitor all of them acoustically
Also - growing use of sophisticated multi-band compressors
possible to create audio material which appears completely normal on quasi-peak meters yet sounds extremely loud
causes problems at programme junctions
Metering And Loudness

## Slide 142
Metering And Loudness
Post-production houses monitor and regulate the true perceived loudness of films using loudness meters
common meter - Dorroughs
Thames Television and the ITC ...
  - formulated a specification for displaying the relative loudness perception of typical audio programme material
Perception of loudness depends on -
level of a signal
frequency bandwidth
wider the bandwidth, the louder a signal seems to be
(even if its peak level remains constant)

## Slide 143
Human ear - most sensitive around 2-4kHz
signals in this frequency band will sound much louder than low- or high-frequency signals of similar peak level
e.g. band-limited 1/3-octave noise signals at 100Hz and 10kHz can be almost 15dB higher in level than noise centred on 4kHz …
  ...yet all will be perceived as sounding equally loud!
Metering And Loudness
0 1 2 3 4 5 6 7 8 9 10 freq, kHz →
dB
0
-5
-10
-15

## Slide 144
Revision - Analogue - Digital Conversion
Metering for Digital Systems
1111
1110
1101
1100
1011
1010
1001
1000 0111
0110
0101
0100
0011
0010
0001
0000

## Slide 145
Digital systems - transient overloads are clearly audible
∴ neither VU nor PPM metering is suitable
Digital equipment use true peak-reading meters
derived from the digital data stream
  ... not analogue level-sensing electronics
∴ can be extremely accurate.
Analogue meters all have a nominal alignment point — the zero reference
have a notional headroom above
signal peaks are routinely allowed into the first 8dB or so of this headroom
peaks of +12dBu will usually start to cause distortion
becomes more noticeable with increasing level ...
  until clipping occurs, usually above +18dBu
Metering for Digital Systems

## Slide 146
No headroom above the maximum quantisation level
∴ notional headroom created
by choosing a 'zero' point well below this
Digital meters scaled such that maximum quantisation level is denoted as 0dBFS (full scale)
so the alignment level is always a negative value below this point.
Europe Standard (by European Broadcasting Union)
0dBu = -18dBFS
∴ signal peaking at the top of the EBU-standard PPM scale
(therefore with true peaks at around +16dBu)
remains a little below the digital full scale value
American SMPTE
0dBu at -20dBFS instead...
Digital Systems

## Slide 147
Problem: post-production and mastering situations
programme levels have been carefully controlled
these standard alignments typically cause most mixes to peak only below -10dBFS
Consequently, strong arguments for adopting a different alignment strategy in these circumstances
  e.g. align 0dBu to -12dBFS for mastering work
  however, there is as yet no standard calibration specifically for post-production applications.
Digital Systems

## Slide 148
Original recorded (analogue) signal
Converted signal (digital, but shown here as the analogue)
1100010010010000100010101000100010
“Over” Indicators
Digitised signal, using full quantisation range
Digital processing requires increasing the amplitude, but this excedes the quantisation range
required amplified signal
maximum available signal
The problem:

## Slide 149
Signal exceeds the maximum quantisation level
when the analogue input is greater than the available quantisation range
when some signal-processing operation results in a sample value larger than the maximum quantisation level
“Over” Indicators
However - often less meaningful when metering an already-digitised audio without the benefit of the original source as a reference
Only way in which most digital meters can detect overloads in the audio data stream is by watching for consecutive samples with the maximum quantisation value
Commonly, four consecutive maximum-value samples are interpreted as an overload
… but some meters include an option for the user to specify this number.
However, four maximum quantisation values in a row does not necessarily imply an overload:
  peak-level low-frequency signal could easily create four maximum-value samples quite legitimately
  high-frequency signal could be severely distorted with just a couple of peak-value samples

## Slide 153
Picture Line-up Generation Equipment - PLUGE
Generates test patterns
greyscale - adjust the black level and contrast
various PLUGE patterns,
most common - vertical bars of super-black, normal black, and near-black and two rectangles of mid-gray and white
included in the SMPTE colour bars
NTSC, PAL, and SECAM
first vertical bar (left) = black
  not seen against the background
second vertical bar = only just visible as dark grey
third vertical bar = lighter gray and clearly visible
white box = comfortable level of true white
  80Cd/m2 with a suitable light meter
no colour in PLUGE display
For monitor set up, see (for example):
https://documentation.apple.com/en/finalcutpro/usermanual/index.html#chapter=78%26section=9%26tasks=true
See also
100% bars
75% bars - NTSC

## Slide 154
Diamond Display
Top diamond: Pb against Y
Bottom diamond: Pr against Y
Tested on test equipment – e.g. Tektronix waveform monitor (below)
Anything outside the diamonds is outside of the gamut (NTSC, or other suitable colour space)