## Slide 1
Broadcast Technology UG1
4: Modulation, Multiplexing
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
Modulation,
AM, FM, Phase,
(QAM ... later on …)

## Slide 3
Signals - baseband
time
voltage
20kHz
frequency
voltage
TIME DOMAIN
FREQUENCY DOMAIN

## Slide 4
Carrier Waves
Receiver
Receiver
Receiver
Transmitter
carrier
frequency a
“tuned” to frequency a
tuned to frequency b
tuned to frequency c

## Slide 5
Receiver
Receiver
Receiver
Transmitter
“tuned” to frequency a
tuned to frequency b
tuned to frequency c
carrier
frequency a
carrier
frequency b
carrier
frequency c
Carrier Waves

## Slide 6
Modulation
Sports
News
Music
Receiver
Receiver
Receiver
Transmitter
Sports
News
Music
“tuned” to frequency a
tuned to frequency b
tuned to frequency c
modulated carrier
frequency a
modulated carrier
frequency b
modulated carrier
frequency c
carrier wave
program signal
Modulation

## Slide 7
Modulation
To convey a Baseband signal on a Carrier signal
Necessary to allow a multitude of baseband signals to simultaneously exist
Carrier - sinusoidal
y = sin x
Wavelength = 
= 1 cycle
Frequency ...
f = cycles/second
= Hertz, Hz

## Slide 8
Signals
time
voltage
20kHz
voltage
TIME DOMAIN
FREQUENCY DOMAIN
frequency

## Slide 9
Signals – transmitting more than one signal on a channel - multiplexing
20kHz
20kHz
voltage
time
voltage
frequency

## Slide 10
20kHz
20kHz
20kHz
voltage
frequency
Signals – transmitting more than one signal on a channel - multiplexing

## Slide 11
20kHz
20kHz
20kHz
voltage
frequency
Signals – multiplexing
Each channel needs a separate carrier
fc1
e.g. 200kHz
fc2
e.g. 222kHz
fc3
e.g. 244kHz
Includes 2kHz guardband

## Slide 12
y = sin x
Carrier - sinusoidal
Carrier parameters can change to convey the baseband signal:
  Amplitude
  ... Amplitude Modulation - AM
  Frequency
  … Frequency Modulation
  - FM
  Phase
  … Phase Modulation
  (PM and many other types)
Modulation

## Slide 13
Analogue Modulation – AM and FM

## Slide 14
Amplitude Modulation - AM
Carrier Wave
Audio Signal
Amplitude Modulated Carrier
Transmitted AM signal
+


## Slide 15
Audio
Programme
Carrier Wave Generator
Transmitter
Modulator






Amplitude Modulation

## Slide 16
Receiver
Demodulator


Audio Stage


Amplitude Demodulation
Receiver - antenna feeds a circuit tuned (i.e. sympathetic to the frequency of the desired carrier wave). The modulated carrier wave is retrieved
The demodulator – “tunes in” to the same frequency as the carrier, so retrieves the required baseband signal

## Slide 17
Receiver
Demodulator


Audio Stage


Amplitude Demodulation

## Slide 18
Noise interference hits
transmitted wave
… and alters the amplitude of the carrier
demodulated wave contains noisy spikes
AM Prone to Noise Interference

## Slide 19
Modulation Index
The ratio of the depth of modulation
carrier voltage
= Vc
carrier
modulating signal
modulated carrier
signal voltage = Vs
Modulation Index = m =

## Slide 20
Modulation Index
Here, modulating signal Vs is half the magnitude of carrier voltage Vc
i.e. Carrier Voltage = Vc
… and Vs = 0.5 x Vc
∴ m = Vs / Vc
= 0.5v / v
= 0.5 (or 50%)
Here, the modulating signal Vs is the same magnitude as the carrier Vc;
i.e. Vs = Vc
∴ m = Vs / Vc = 1 (or 100%)
note - the modulated wave reduces to zero

## Slide 21
Modulation Index
Here the modulation index is 0.25
giving a fairly shallow modulated carrier wave
signal strength is low compared to noise (S/N ratio)
Here the modulation index is 1.5
- giving an over modulated carrier

## Slide 22
Amplitude Modulation
Carrier Wave
Audio Signal
Amplitude Modulated Carrier
Transmitted AM signal
+

Carrier Signal = vc = Vc sinωct;
ωc=2πfc where fc= carrier freq
Modulating Signal = vs = Vs sinωst;
ωs=2πfs ; where fs = modulation freq
So the voltage of the carrier varies between
(Vc + Vm) and (Vc - Vm)
Modulation Index = m =Vs / Vc; so Vs = m Vc
vc = (Vc + Vssinωst) sinωct
= Vc sinωct + Vssinωst . sinωct
since
sinωst . sinωct = ½ [cos(ωc – ωs)t - cos(ωc + ωs)t]
then
vc = (Vc sin ωct) + ½ mVc cos(ωc – ωs)t - ½ mVc cos(ωc + ωs)t

## Slide 23
Amplitude Modulation
vc = (Vc sin ωct) + ½ mVc cos(ωc – ωs)t - ½ mVc cos(ωc + ωs)t
Carrier + USB - LSB
fc
fc + freq range of signal
fc - freq range of signal
Power
LSB =
Lower Side Band
USB =
Upper Side Band

## Slide 24
AM Frequency Spectrum - Sidebands
AM process produces a spectrum containing the carrier and two sidebands of frequencies related to the modulating signal
e.g.:
e.g. modulating signal is between 100Hz and 8KHz,
and carrier freq = 600KHz (=600,000Hz)
Then - USB extends up from [600,000 + 100]Hz to [600,000 + 8,000]Hz
= 600.1KHz up to 608KHz
LSB extends down from [600,000 – 100]Hz to [600,000 – 8,000]Hz
= 599.9KHz down to 592KHz
fc
fc + freq range of signal
fc - freq range of signal
Power
LSB =
Lower Side Band
USB =
Upper Side Band

## Slide 25
AM Frequency Spectrum - Sidebands
Carrier frequency
fc = 5KHz
Signal frequency, fm = 500Hz
Sideband at fc-fm = 5KHz-500Hz = 4.5KHz
Sideband at fc+fm = 5KHz+500Hz = 5.5KHz

## Slide 26
Frequency Modulation
Unmodulated
Carrier Wave
Audio Signal
Frequency Modulated Wave
i.e. carrier freq increases with audio signal amplitude

## Slide 27
Received signal
S(t)
Zero Crossing Detection
Fully rectified signal
Pulse Generator
Low Pass Filter
Regenerator Threshold
Regenerated baseband
signal
Sm(t)
Limited and filtered
signal
FM Demodulation

## Slide 28
Frequency Modulation – Modulation Index
Often denoted as β
indicates how much the frequency of the carrier will deviate in relation to the frequency of the modulating signal
i.e.
β = = the change of frequency / frequency of the carrier
e.g. β=5 means the frequency of the modulated carrier will deviate
by 5x the modulating signal
e.g. if freq range of the signal is 20Hz to 15KHz (i.e. typical FM spec)
then the frequency of the carrier will deviate by 100Hz up to 75KHz

## Slide 29
Transmitted FM signal
Noise-hit FM signal
... however - frequency of signal is still intact:
Since we are only interested in the frequency of the carrier, the original audio signal can still be recovered
Amplitude of signal is corrupted...
Frequency Modulation - Immunity to noise

## Slide 30
Spectrum of an Analogue PAL TV Transmission

## Slide 31
SSB produced by filtering one of the sidebands, usually the lower (LSB)
Carrier is also often reduced or removed entirely (suppressed)
= single sideband suppressed carrier (SSBSC)
No information is lost in the process
Radio frequency transmission is now concentrated in a single sideband
∴ effective power output is greater than in normal AM
(since the carrier and redundant sideband account for well over half of the power output of an AM transmitter)
Requires special reception to demodulate
Sidebands – Single, Vestigial

## Slide 32
sideband that has been only partly cut off or suppressed
to reduce the large bandwidth of the original video signal
also be used in digital transmission, such as the ATSC standardized 8-VSB
by the RF and IF filters
Vestigial Sideband (VSB)
For video - SSB would be desirable
... but the video signal has significant low frequency content, plus square sync pulses
... so some of the lower sideband is retained
VSB - full upper sideband of bandwidth transmitted = 4MHz
... but only 1.25MHz of the lower sideband is transmitted, plus the carrier
effectively makes the system AM at low modulation frequencies and SSB at high modulation frequencies
absence of the lower sideband components at high frequencies must be compensated for, and this is done by the RF and IF filters

## Slide 33
Sub Carriers
sub carrier is 848kHz below main carrier
The subcarrier is modulated with a signal, the resulting signal is then modulated onto main carrier. (i.e. two levels of modulation)
(This example is actually for contactless payment systems, but the principle is common for subcarrier modulation)
sub carrier is 848kHz above main carrier

## Slide 34
Vision Carrier
1.25MHz
(AM / VSB)
Colour Sub-Carrier
(suppressed)
5.68MHz
Chroma coding (QAM)
Sound Centre Freq
6.75MHz
(FM)
7.0MHz
PAL Signal Spectrum
freq
Full Sideband
Vestigial Sideband

## Slide 35
Broadcast Channels Frequency Spacing
475MHz
850MHz
7Mhz TV Channel
8Mhz Spacing
Ch21
Ch68
48 channels

## Slide 36
http://www.ukfree.tv/txdetail.php?a=SK113003

## Slide 37
Multiplexing:
FDM, TDM
Statistical
Multiplexing: combination of signals to transmit on a common bearer / channel

## Slide 38
  Each signal is modulated onto a different frequency (subcarrier )
  Multiplexing - Frequency Division Multiplexing (FDM)
“baseband”
signals
i.e. unmodulated original signal
f1 f2

## Slide 39
  Multiple signals are interleaved (in bits or blocks) over time
  Multiplexing - Time Division Multiplexing (TDM)
Data streams divided into frames
Frames divided into time slots
Each user is allocated one time slot
Time slots contain data with guard period if needed for synchronisation
1
3
4
2

## Slide 40
10110011
01001001
10010001
010100101
010100101
10010001
01001001
010100101
010100101
01001001
010100101
Time Division Multiplex
4kHz voice sampled at 8kHz (fs) into 8 bits binary
e.g. for UK / European E1 Multiplexes:
30 channels of speech into 32 channel frame “Multiplex”
32 channels x 8b x 8kHz = 2.048Mbs-1
  (includes 1 channel signalling and 1 channel synchronisation)
TS1 TS2 TS3 TS4 TS5 TS6 TS7 TS8 ………………………………………………………………….
Analogue – Digital: Samples are dropped into allocated timeslot for each frame
TS6 previous frame
TS6 this frame
TS6 next frame

## Slide 41
Statistical Multiplexer
Input buffer
Multiplexing - Statistical Multiplexing
Input buffer
Input buffer
Input buffer
Output buffer
Input buffer
Source A
Source B
Source C
Source D
Source E
Incoming ports: Data blocks arrive asynchronously from variable-rate sources
Input buffers smooth fluctuation in input data rates
Headers containing addresses and other information are added to the data blocks – to form packets
Packets are then fed to the output buffer
Outgoing Port:
Packets are placed on the outgoing channel

## Slide 42
Multiplexing - Statistical Multiplexing
e.g. DVB multiplex:
End
Flag
Address
Field
Control
Field
Information
Payload
Error
Control
Start
Flag
Packet format: Control, management and content assigned into fields

## Slide 43
Dynamic capacity allocation
Variable Bit Rate – VBR
one channel capacity reallocated to meet immediate service needs of other channels
Statistical Multiplexing
http://igorfuna.com/dvb-t/slovenia/multiplex-a-usage-chart
allow additional elementary bit streams to be added at the input of the multiplexer
... or allow elementary bit streams to be multiplexed at a second stage

## Slide 44
WDM – Wave Division Multiplexing
A number of multiplexes (each of many channels) are carried on one fibre
Each multiplex is a string of data
  each on it’s own wavelength
Uses single mode fibre
Sources
Receivers
Fibre Optic

## Slide 45
Modulation for
Digital Data

## Slide 46
Modulation for Digital Data
objective:
We need to transmit a digital file of 00010101100110101000101010100101100110101…
can’t transmit “neat” digital 1’s and 0’s from a transmitter
  (or receive them at a receiver)
transmission technologies operate only on analogue signals
  we also need to retain the carrier frequency concept to allow for many stations
so carry 1’s and 0’s on analogue signals:
1 0 1 1 0 0 1
1 0 1 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1
… often at hundreds of Mbits/s



## Slide 47
7.0MHz
e.g: Analogue TV … to Digital TV
frequency
Analogue TV Signal Spectrum
Frequency spectrum (range) for Analogue TV broadcast:
  video signal (luminance + colour)
  audio signal

## Slide 48
Broadcast Channels Frequency Spacing
475MHz
850MHz
7Mhz TV Channel
8Mhz Spacing
Ch21
Ch68
48 channels
UHF band

## Slide 49
UHF TV in the Electromagnetic Spectrum

## Slide 50
http://www.ukfree.tv/txdetail.php?a=SK113003

## Slide 51
475MHz
850MHz
Ch21
Ch68
48 channels

## Slide 52
1 0 1 1 0 0 1
t
Digital Data
… is modulated
on to a
Analogue
Carrier
180 180 0 180 0 180
Phase Coherent
90 270 270 90 90 270
Differential
Digital Data on Analogue Carrier e.g. Phase Shift Keying (PSK)
Binary PSK (there’s various formats):

## Slide 53
The Transmitted Signal
Shown here – 8 QAM
i.e. eight digital codes can be transmitted:
  000, 001, 010, 011, 100, 101, 110, 111
So transmit the signal 000110001111:
…break it into the groups of codes available
000 110 001 111

## Slide 54
Digital
Data
Carrier Wave Generator
Transmitter
Modulator






Digital Transmission
Receiver

Data retrieval, etc
Receiver tunes into carrier, detects phase changes, retrieves data

## Slide 55
Inter-Symbol Interference for Modulated Data
Causes
multipath interference, including atmospherics
channel gain variations
signal spreading over a transmission line
jitter and other timing issues

## Slide 56
Inter-Symbol Interference for Modulated Data
+ =
+ =
Path difference – results in phase difference

## Slide 57
Symbol n
Symbol n+1
Symbol n+2
Symbol n+3
Symbol n+4
Symbol n+5
Symbol n
Symbol n+1
Symbol n+2
Symbol n+3
Symbol n+4
Symbol n+5
Path 1
Path 2
Path 1+2
echo delay time
intersymbol interference
Inter-Symbol Interference for Modulated Data

## Slide 59
Advanced: QAM (later in the Course)

## Slide 60
0°…… 90°……180°..…270°…360°
The Carrier for Digital – Still a Sinusoidal Wave
Carrier wave
e.g. for Digital Terriestrial TV = 475 – 850 MHz
… for Bluetooth = 2.4GHz
… for Wifi = 2.4GHz and 5GHz
… for DSL broadband – many frequencies (OFDM)

## Slide 61
90° phase change (advanced)
270° phase change
(advanced)
Phase Changes In A Sinusoidal Wave
0°…… 90°……180°..…270°…360°
Changes in phase (and amplitude) of a carrier can be used to denote digital code information
e.g. +90° = “1”; +270 ° = “0”
(but it gets more sophisticated than that!)

## Slide 62
90° phase change
Phase Changes In A Sinusoidal Wave
0°…… 90°……180°..…270°…360°
Signal was to be transmitted here …
But it has been moved forward (advanced) by 90°
90°

## Slide 63
90°
0°
180°
270°
90° phase advance
270° phase advance
Constellation Diagrams
A graphical representation of digital codes corresponding to amplitude and phase-change in the carrier signal
e.g. a signal with 90° and 270° phase changes:

## Slide 64
Amplitude Changes – Constellation Diagram
0°………………90°…………….180°……………..270°…………….360°
90°
0°
180°
270°
i.e. red wave increases to twice the amplitude of green, but is still in phase at change
… an additional way to convey digital coded information

## Slide 65
Phase and Amplitude Changes
0°………………90°…………….180°……………..270°…………….360°
90°
0°
180°
270°
i.e. red wave is half the green amplitude, and has advanced by 90°

## Slide 66
1
Decision Thresholds
0°
180°
0
Constellation Diagrams
Two phase changes - 90° & 270°
allows intelligence – i.e. binary information – to be defined in these carrier changes
two changes in state – allows two coded bits: 1 & 0
270
90°

## Slide 67
0
1
Decision Thresholds
0°
180°
Constellation Diagrams
11
10
01
00
90°
0°
270°
180°
Two phase changes - 90° & 270°
i.e. two changes in state, allows
two coded bits: 1 & 0
Four phase changes - 45°, 135 °, 225 °, 315 °
i.e. four changes in state, allows two coded bits per symbol:
00, 01, 10, 11
Problem: The receiver has to detect smaller phase changes
270
90°

## Slide 68
11
10
01
00
90
0
270
180
If the phase change falls within this range, it represents a signal “01”
i.e. a fairly wide decision threshold
Constellation Diagrams

## Slide 69
QAM – Quadrature Amplitude Modulation
90
0
270
180
16-QAM
16 decision points
4 coded bits per symbol
Used in Cable TV, IPTV, Satellite TV, WiFi
... most digital transmisions

## Slide 70
16-QAM
90
0
270
180
Decision
Thresholds
Vector:
Length = Amplitude
Angle = Phase
16-QAM
16 decision points
4 coded bits per symbol
0000
0001
0010
0011
0100
0101
0110
0111
For example
Decision
Thresholds
Phase change can fall within this (small) range

## Slide 71
270
Decision
Thresholds
90
0
180
64-QAM
64 decision points
6 coded bits per symbol
64-QAM
More digital bits - more information transmitted
More fragile signal (I.e. than 16QAM)-
will suffer in a poor transmission
results in more messages retransmitted
Decision thresholds
e.g. a phase/ amplitude shift represented by this point = (say…) “100101”

## Slide 72
256-QAM
256-QAM
256 decision points
8 coded bits per symbol
e.g. a phase/ amplitude shift represented by this point = (say…) “10010111”
Decision
Thresholds
90
0
180

## Slide 73
16-QAM Potential Errors
... due to phase and amplitude variations caused by transmission vaguaries
Left – ideal reception of signal
Above – more practical reception

## Slide 74
The Transmitted Signal
Shown here – 8 QAM
i.e. eight digital codes can be transmitted:
  000, 001, 010, 011, 100, 101, 110, 111
So transmit the signal 000110001111:
…break it into the groups of codes available
000 110 001 111