## Slide 1
Broadcast Technology UG1
1: Transmission Media
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
The Context …

## Slide 3
Information Transmission, Signal Encoding
Information
Source Coding
Channel Coding
Modulation
Interference
Phase Distortion
Attenuation
Demodulation
Channel Decoding
Information
Source Decoding
bit errors
Transmission Link
Source Information
coded data in as small space as possible (compressed, etc)
signal received – reverse processes
transmission is subject to noise interference
aim – to approach the Shannon Limit
Channel coding
appropriate error protection method
... depends on channel characteristics
modulation on to carrier
jeremy.foss@bcu.ac.uk
Crosstalk
Crosstalk
jitter
NOISE
NOISE
NOISE

## Slide 4
Video Packets
Audio Packets
Data Packets
TS Mux
Mux adaptation, scrambling
Error Correction
Block Code
Interleaving
(against long errors)
FEC
Convolutional
coding
Interleaving
(against burst errors)
Mapper
(IQ symbols)
Frame adaptation
symbols
Pilot, TPS signals
OFDM
Modulation
Guard interval insertion
DAC for Tx
DVB Transmission Playout System
Antenna,
Cable,
Sat uplink
(Based on DVB-T, but –C, -S and –H are similar)
QPSK, QAM, etc
Blocks (1512 – 6048 sy/block)
of symbols →
frames (68 blocks)
(4frames =superframe)
Transmission parameters
carriers, 2k – 32k (for T2
channel b/w =
1.7 to 10MHz
includes cyclic prefix
FEC – Outer …….
FEC – Inner
COMPRESSION

## Slide 5
Back to Basics

## Slide 6
Transmission
Media

## Slide 7
Types of Transmission Media
Multiplexing - FDM, TDM, Statistical
  * introduction only – will be covered in depth later on
Cables
  Twisted Pair
  Coaxial
Fibre Optic
  Wave Division Multiplexing
Radio
  Spectrum
  Transmitter
  EM Wave, Radio Waves
  Propagation through lower and upper atmosphere
  Broadcast Transmitter Technologies (valves)
Transmission Media

## Slide 8
“Guided”: The waves are guided along a physical path
“Unguided”: The medium transmits the waves but does not guide them
Types of Transmission Media
Direct Link:
  The signal is propagated directly from transmitter to receiver (perhaps through amplifiers/repeaters)
Point-to-Point:
  A guided medium that provides a direct link between two and only two devices
Multipoint:
  A guided medium that is shared by more than two devices
Types of Transmission Connection
ref – Prof. David Bernstein, James Madison University

## Slide 9
Twisted Pair Cable
Two insulated copper wires that are twisted together (which results in cancellation of induced interference; cancellation of radiated interference, hence reduces radiation)
The individual pairs can be shielded (STP) or unshielded (UTP)
The cable can also be shielded (S/STP)
Categories (CAT ...)
  1 - primarily for voice
  2 - 4Mbps
  3 - 16MHz bandwidth; 10Mb/s
  4 - 20MHz bandwidth; 16Mb/s
  5 - 100MHz bandwidth; 100Mb/s (4 pairs/cable)
  - 400MHz bandwidth; 1Gb/s (4 pairs/cable)
  - 600MHz bandwidth (1GHz for Augmented); 10Gb/s
  - 1.2GHz bandwidth
Common Uses:
  Voice Telephony, various Digital Subscriber Line (xDSL), LANs
CAT 7 – Screen Shielded Twisted Pair (SSTP)

## Slide 10
Untwisted cable
Twisted cable
Magnetic field
Induced noise current
Noise generated by magnetic fields from the environment.
noise current is the result of that magnetic field
straight cable - all noise current flows same direction
twisted cable – in alternate twists noise current is the opposite from the current in other twists
Twisted Pair Cable

## Slide 11
Twisted Pair Cable
Advantages:
  High availability
  Low installation cost
Disadvantages:
  Usable frequency spectrum is small
  Limited data rates
  Limited range
  High suceptibility to electromagnetic and radio frequency interference
ref – Prof. David Bernstein, James Madison University

## Slide 12
In balanced pair operation -
Differential mode transmission -
differential signals; receiver detects the difference between the two
noise signals tend to couple to both wires equally
∴ noise produces a common signal in each conductor
- which is cancelled at the receiver
(not effective when the noise source is close to the signal wires; closer wire will couple with the noise more strongly)
Twisted Pair Cable
Twist rate
more twists the better (usually)
http://www.extron.com/company/article.aspx?id=utptechnology

## Slide 13
Twisted Pair Cable
UTP: Unshielded twisted pair
STP
Twist rate
more twists the better (usually)
STP: Shielded twisted pair
UTP

## Slide 14
Twisted Pair Cable
Telecommunication cables pairs in the same cable adjacent for many miles
... one pair can induce crosstalk in another
each half twist the wire nearest to the noise-source is exchanged
also reduces electromagnetic radiation from the cable

## Slide 15
10BASE-T
transmission at 10 Mb/s on unshielded twisted-pair cabling
defines various aspects of running Ethernet on this cabling.
100BASE-T
transmission at 100 Mb/s on unshielded twisted-pair cabling
defines various aspects of running baseband Ethernet on this cabling
1000BASE-T (gigabit Ethernet) transmission at 1000 Mb/s on unshielded twisted-pair cabling
defines various aspects of running baseband Ethernet on this cabling
IEEE Cable Standards for Ethernet on Twisted Pair

## Slide 16
Frequency dependent attenuation and dispersion
… Intersymbol Interference (ISI)
Coupling between wires in same and adjacent binders
… crosstalk - near-end cross-talk = NEXT
- far-end cross-talk = FEXT
Bridged taps and gauge transitions
… reflections : pulse distortion (ISI)
Impulsive noise : high bursts of short duration (10 ms - 1 ms)
Signal Issues on Twisted Pairs at High Frequencies
Impedance mismatch between hybrid and line impedance
… reflections (echo)
RFI interference: AM broadcast & amateur radio
… ingress & egress
All these require a highly adaptive transceiver (at each end)

## Slide 17
Coaxial Cable
A (thick) copper wire surrounded by an insulator and an outer conductor
Common Types:
  RG-6 - 1.00mm core, 75 Ω
  RG-59 - 0.81mm core, 75 Ω
  RG-58 - 0.90mm core, 50 Ω
  RG-8 - 2.17mm core, 50 Ω
Common Uses:
  Applications for RF signals
  Cable TV (Old: RG-59; New: RG-6)
  Ethernet (RG-58: 10Base2; RG-8: 10Base5)
  connecting radio transmitter feeds
Advantages:
  High capacity (370-1000 times more than twisted pair)
  Low susceptibility to noise and crosstalk (because of shielding)
Disadvantages:
  Noise on the return path
  High installation cost

## Slide 18
Coaxial Cable
dimensions of the cable are controlled to give a precise, constant conductor spacing
needed to function efficiently as a radio frequency transmission line
electric and magnetic fields are confined to the dielectric with little leakage outside the shield
electric and magnetic fields outside the cable are largely kept from causing interference to signals inside the cable
design of cable to control the electrical transmission properties ...
compare to standard shielded cable

## Slide 19
Coaxial Cable
All cables have electrical properties - they are not just short-circuits between equipment
Electrical properties of any cable pair:
R: resistance along the cable
L: signals cause inductance along the length of the cable
G: conductance - a certain amount of leakage, similar to a high resistance between the conductors
C: capacitance between the two conductors
Coax cable is designed to control these parameters

## Slide 20
Coaxial Cable
All cables have electrical properties - they are not just short-circuits between equipment
All cables are effectively a (mathematically) complex circuit of distributed impedance sections

## Slide 21
Coaxial Cable
Double shielded coax
Coax female socket Coax male plug

## Slide 22
Coaxial Cable
Splitting signals
simple 2-into-1 can cause impedance imbalance
splitters should normally terminate each cable and combine in an impedance-balanced circuit, especially at high RF feeds

## Slide 23
Fibre Optic Cable
A thin glass core surrounded by cladding that reflects light into the core
surrounded by a protective plastic buffer/jacket
Common Uses:
  Cable TV
  Voice Telephony
  Ethernet
9 – 62.5mμ

## Slide 24
Fibre for local distribution
MicroCore Blown Fibre Cable – for air-blown installation (using existing ducts, e.g. replacing existing cable plant)
Fibre Optic Cable

## Slide 25
Fibre Optic Cable
Common Wavelengths (in the infrared):
  850nm (i.e., 0.85 μm )
  1300nm (i.e., 1.30 μm )
  1550nm (i.e., 1.55 μm )
Advantages:
  Low cost
  High capacity
  Thin
  Low interference/degradation
Disadvantages:
  Has a minimum radius for bending
  Each fiber is one-way
  High cost of interfaces

## Slide 26
Wavelengths of light used for signal carriers
may be a number of colours - WDM
Fibre
Light Signal
Fibre Optic Cable
Light is laser LED;
  laser light is a single frequency
  ... (i.e. a single wavelength)
Reflections: Internal reflection of the glass fibre
Signal degrades due to impurities in the glass

## Slide 27
Electrical to Light Conversion
(O/E)
Light to Electrical Conversion
(O/E)
Fibre Optic Cable
Transparent glass or plastic fibres
allow light to be guided from one end to the other with minimal loss

## Slide 28
Total Internal Reflection
Light passing from one medium (m1) to another (m2) with lower index of refraction (ri) bends away from the normal line
At the critical angle, defined by sin ( θ ) = n1 . n2, the refracted light will not go into the second medium but will travel along the border
Fibre Optic Cable

## Slide 29
Three types of fibre optic cable commonly used:
Multimode - MMF
many rays (modes)
core = 62.5 microns
  (some 50 microns)
LED and laser sources 850, 1300nm
LANs
graded index ~2GHz b/w
step index is rare
Single mode - SMF
single ray (mode)
core = 9 microns
telephony, CATV
laser @ 1300, 1550 nm
b/w ~ 100THz
Fibre Optic Cable

## Slide 30
Step-Index Multimode Fiber
large core
some rays direct - others zigzag
  arrive separately ∴ pulse spreads out
  leave space … prevent overlapping
    limits data rate
for short(er) distances, <2km, LANs, SANs,
  data centers etc
Graded-Index Multimode Fiber
refractive index reduces from the centre
  centre: higher index
    rays travel more slowly than those further out
    rays curve helically
edge rays – zig-zag
edge rays and central rays travel (more) equal distances
∴ pulse suffers less dispersion
  Typically use LEDs as source 850-1310 nm
lower cost
higher loss
higher loss
Fibre Optical Multimode, Indexes

## Slide 31
small diameter core: 9μm
allows only one mode of light to propagate
  number of light reflections created as the light passes through the core decreases
  lowers attenuation
  signal can travel further
  high precision packaging
typically used in long distance >60km; WAN, MAN
  higher bandwidth runs by Telcos, CATV companies
  Typically use lasers as source
Fibre Optics - Singlemode

## Slide 32
Summary of Modes and dispersion
Fibre Optics
Most fibres 125um outside diameter
MMF
larger core: 50 or 62.5um
wavelengths: 850 and 1300 nm
SMF
smaller core ~9um
Plastic Optical Fibre (POF)
large core ~1mm
usually step index
short, low speed
PCS, HCS
PCS plastic clad silica
HCS hard clad silica
smaller glass core ~200um
thin plastic cladding

## Slide 33
Fibre Optics – Chromatic Dispersion

## Slide 34
CATV
Most CATV applications
both single mode and multimode signals
within different areas of the network:
Headend –to- fibre nodes: Single Mode fibre
then converted to multimode for remaining outward distribution
CATV Fibre Optics

## Slide 35
WDM – Wave Division Multiplexing
A number of multiplexes (each of many channels) are carried on one fibre
Each multiplex is a string of data, each on its own wavelength
Uses single mode fibre
Sources
Receivers
Fibre Optic

## Slide 36
Fibre Networks

## Slide 37
network infrastructure - mixture of cabling, switches and repeaters
no data = no light: ‘dark’ .. not in use
Originally - When Networks Planned / Built:
usually overestimate cabling required, so many fibres dark, for future expansion
Plus, now - Dark Fibre often leased from network providers and operators
client create / operate their own privately-operated optical fibre network
.. rather than just leasing bandwidth
Could be dark fibre rings, point to point or point-to-multipoint configurations
clients aim for high performance, a high security, superfast
better signal strength
more immune to interference than fibre on traditional networks
DWDM (Dense Wavelength Division Multiplexing)
key in the development of Dark Fibre
multiple data signals are transmitted simultaneously, different wavelengths
higher capacity
Dark Fibre

## Slide 38
HF and VF Bands:
  Tend to be absorbed by the Earth
  Can be bounced off of the ionosphere (called sky wave propogation)
VLF, LF and MF Bands:
  Range of about 1000km
  Penetrate buildings
  Omnidirectional
Electromagnetic
Spectrum;
Radio – LF to VHF
higher freqs = shorter wavelength
nm=nanometres
= 10-9 meters
Audio wavelengths (not EM) – shown for comparison
μm=micrometres
= 10-6 meters
(a millionth)
Angstrom Unit =
= 10-8 meters

## Slide 39
Properties:
  Travel in a nearly straight line
  Can be narrowly focused (by a parabolic antenna)
  High signal to noise ratio
  Little interference
  Low penetration
      Do not pass through buildings
      At 4GHz and above, the waves are very short and can be absorbed by water (e.g., rain)
      At 60GHz the waves can be absorbed by oxygen
Range:
  2GHz-6GHz: 70km
  18GHz-45GHz: 1.6-8km
Radio - Microwave
Audio wavelengths (not EM) – shown for comparison
μm=micrometres
= 10-6 meters
(a millionth)
Angstrom Unit =
= 10-8 meters
nm=nanometres
= 10-9 meters

## Slide 40
BAND Freqs, MHz Typical usage
LW 0.14 - 0.28 BBC Radio 4 LW (0.198MHz)
MW 0.58 - 1.6 Medium Wave Radio Stations
HF 3 - 26 special broadcast services, popular for Pirate radio
CB 26 - 28 CB
Low VHF 29.7 - 47 Military, Model aircraft, hospital
Band I 47 - 68 old TN band; now alarms, cordless phones, car alarms
Low Band 68 - 87.5 Military, emergency services, private business radio
FM, Band II 87.5 - 108 FM radio broadcast
Air Band 108 - 137 Aero comms, navigation
Mid Band 137 - 165 Military, police
Marine Band 156 - 163 Marine, ports, navigation, distress
High Band 165 - 174 Medical, telemetry, theatres
Band III 174 - 230 special applications, eg via JFMG freq allocation
NATO Band 230 - 400 NATO, space shuttle
UHF1 & 2 400 - 470 Navigation, repeaters, telemetry
TV, Bands IV & V 470 - 854 TV broadcasting, PAL, SECAM
GSM & mobile 854 - 960 GSM mobile, aero, navigation, astronomy
Amateur 23cm 1.2GHz Amateur use
Microwaves 1 - 300GHz Communications links
Ku TV Band 10.7-12.75GHz Comms, satellite support
Visible Spectrum
Radio and TV Frequency Band Allocations

## Slide 41
TV/Radio Broadcast Transmitter
sound
video
CARRIER
MODLATOR
OUTPUT POWER STAGE
ANTENNA
electromagnetic energy from output signal is propagated from the antenna
may be unidirectional, or focussed in particular direction by antenna design
Output stage
small transmitters – may be solid state
large transmitters – valves more efficient

## Slide 42
NEC DTU-52 Transmitter equipment, Winter Hill, UK, for Arquiva, transmission provider for UK terrestrial TV

## Slide 43
(left) http://learn.uci.edu/oo/getOCWPage.php?course=OC0811004&lesson=005&topic=002&page=21
Electromagnetic Wave
alternating electrical current produces an electric and magnetic field that are also alternating
the wave of the electric field and the wave of the magnetic field are propagated perpendicularly to the direction of propagation and to each other

## Slide 44
Electromagnetic Wave

## Slide 45
Transmitter - generates radio-frequency energy
energy travels through a transmission line to an antenna
antenna converts the energy into radio waves
radio waves radiate into space from the antenna at the speed of light
radio waves travel through the atmosphere or space until they are either reflected by an object or absorbed
Radio Waves - Basic Antenna
Receiving antenna
in the path of the radio waves
absorbs part of the waves and converts them to energy
energy travels through transmission line
fed to a receiver
Transmitter Station
Receiver Station
Transmission line
Transmitter
Antenna
Receiver
Antenna
Transmission line

## Slide 46
Basic Antenna
Wet foliage can cause problems in reception
… especially for higher frequencies
Transmitter Station
Receiver Station
Transmission line
Transmitter
Antenna
Receiver
Antenna in “shadow” of tree (especially when wet)
Transmission line

## Slide 47
Radio Transmission and Reception
Electric and magnetic fields generated by a dipole antenna
Radiating electrical field from transmitter
Induced electric and magnetic fields in receiver
Note charge and current directions

## Slide 48
Antenna Power Gain
combination of directivity and electrical efficiency
Transmitting antenna - how well the antenna converts input power into radio waves headed in a specified direction
Receiving antenna - how well the antenna converts radio waves arriving from a specified direction into electrical power
Radio Transmission and Reception
Antenna / transmission polarisation

## Slide 49
Radio Wave Propagation
For reception, antenna length at least λ/4
Low freq (e.g. AM services)
earth ground has strong influence
  induce current in ground
  attenuated by absorbtion in earth
  attenuation increases with increase in freq
  maximum range depends on …
    transmitted power, frequency (< few MHz)
Higher Frequencies – VHF, UHF
Waves can be refracted off Troposphere
(lowest of atmospheric layers)
refraction due to atmospheric rerfractive indeces
(so not a guaranteed performance due to changing weather)
… see later …
Surface Waves

## Slide 50
Ground waves
propagate along the earth surface, close to the ground
  (never reach the ionosphere)
typically travel 150Km in daytime
higher freqs are subject to a high attenuation
  … travel less than 15 km (at 30 MHz)
mainly for low frequencies below 1.8 MHz (MW, LW and VLF)
Radio Wave Propagation
Space waves / Line of Sight
directly from antenna to another without reflection on the ground
also assisted by waves bending near the ground (curved path on earth surface)
Sky wave propagation:
  next slide ...

## Slide 51
Troposphere
where all weather takes place; rising and falling packets of air
air pressure at the top of the troposphere is only 10% of that at sea level (0.1 atmospheres)
Radio Wave Propagation
Stratosphere
air flow is mostly horizontal
thin ozone layer in the upper stratosphere
  high concentration of ozone
  warm: absorbs UV radiation from the Sun
Ionosphere
(generally) ionized by solar radiation (∴ aurora)
Ionosphere
Stratosphere
Troposphere
Mesosphere
~85km – 1000km
~45km – 85km
~12km – 45km
to ~12km

## Slide 52
Transmitter antennae
increasing
frequency
Ionosphere layers
signals can “bounce” off the ionosphere and reach further round the earth
Refraction
bending of waves passing through different media (air or ionosphere)
produces variation in the velocity of waves
Ionospheric scatter
  Ionosphere – ~80Km – 600Km+ above the earth
Radio Wave Propagation

## Slide 53
Radio Wave Propagation - Localised Issues
Diffraction
location is out of sight of transmitter (e.g. - behind a hill)
  can receive transmissions (but reduced)
(although HF will more likely reach due to refraction or reflection in the upper atmosphere)

## Slide 54
Radio Wave Propagation
Reflection
similar to light
for long wavelengths (80m+)
small obstacles (cars, trees) have little effect
  objects small compared to the wavelength, can't reflect the energy
  long waves are reflected by the ground ... but also penetrate
short wavelengths - V/UHF waves (2m - 70cm)
very sensitive to small obstacles
metal objects can be used as reflectors
Reflections
e.g. wi-fi in metal framed buildings
radio waves reflect and interact
could cause stronger or weaker reception

## Slide 55
Years ago - tetrode and pentode valves mainly used on V.H.F. and U.H.F.
Over years, broadcast on higher frequencies - dimensions of the electrodes decreased in order to reduce their effect on the tuned circuits
∴ reduction in power
Magnetron developed,
then klystron
Now – more efficient Inductive Output Tubes (IOT) or Klystrdes (right)
capable of producing power output up to about 30 kW continuous and 7 MW pulsed and gains of 20 - 23 dB at frequencies up to about a GHz
Broadcast Output Power Stages
http://www.thevalvepage.com/valvetek/uhfvalve/uhfvalve.htm
http://steveblank.com/category/secret-history-of-silicon-valley/page/2/
http://www.lbl.gov/MicroWorlds/ALSTool/ALS_Components/RFSystem/
http://www.theonlineengineer.org/TheOLEBLOG/how-iots-work-a-tutorial-2/
http://www.theonlineengineer.org/TheOLEBLOG/radio-waves-a-tutorial/
http://www.youtube.com/watch?feature=player_embedded&v=ecxKfZ3ATwg

## Slide 56
Broadcast Headend Transmitter
IOTs – High power devices
Need special management for cooling
Air Conditioned environment
Water-cooled circuits
Safety features

## Slide 57
https://www.youtube.com/watch?v=fx0asm1kvRw
How IOTs Work

## Slide 59
The Signal Path

## Slide 60
ACQUISITION
LOGGING
INGEST
MEDIA
STORE
DELIVERY
PRODUCTION
SCHEDULE
CREATION
ARCHIVE
AUTOMATION
& PLAYOUT
EPG
CREATION
CODING
&
MULTIPLEX
INTERNET
Streaming
Encoding
iPlayer
Website
CDN
Live Feeds
Studios
OBs
Low end /
Domestic
Camcorders /
DSLRs
News
Camcorders
Hi-End
Camcorders
Digital
Cinema
Cameras +
Recorders
Multi-
Camera
Studio / OB
Other
Material
Data
Input
Data
Input
Data Store
Database
Edit
Grading
Graphics
Effects
Audio
Dubbing
Broadcast and Production Workflow (BBC Schematic)
(review from week 8)
Media
Metadata
Both
Transmission

## Slide 61
Production Contribution Distribution Consumption
Contribution and Distribution

## Slide 62
Media Distribution
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End
Distribution Network
Satellite
Cable
Telco Broadband
Terrestrial TV
Web (OTT)
Mobile

## Slide 63
Media Distribution ... ... Satellite
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End

## Slide 64
Media Distribution - Digital Terrestrial (DTTV)
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
STB, etc
End Users
Video Head-End

## Slide 65
Media Distribution – Cable
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Cable Network
Video Head-End
Access Network

## Slide 66
Media Distribution – IPTV - Telco Broadband, OTT/Web
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
Video Head-End
Access Network
Telco Broadband

## Slide 67
Media Distribution – IPTV - Telco Broadband, OTT/Web
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
Video Head-End
Access Network
Telco Broadband
OTT
OTT
WEB-BASED VIDEO PROVIDER