## Slide 1
Broadcast Workflow
Jerry Foss
jeremy.foss@bcu.ac.uk

## Slide 2
Effective workflow
ensure that critical business processes can be tracked and optimised over time
auditing, logging
to seamlessly orchestrate the interactions between enterprise resources
storage
transcoding
network
etc
... and groups of people
Workflow

## Slide 3
PLANNING
up to the point of shooting
conventions and practices to be adopted at the start of the process
RUSHES MANAGEMENT
capture and handling of content, on location or in a studio
up to the point of rushes archive and management.
POST-PRODUCTION
from the ‘ingest’ of material into the edit
through to the completion of the master
DELIVERY
production of masters for delivery to broadcasters, clients or audiences
DPP technical and metadata standards for file-based delivery of completed programmes.
Production to Delivery

## Slide 4
Contribution
Dedicated links
Satellite
IP -based: low-res, high -res
If not networked, then probably …
Tape
Disk
SSD
Mobile, handheld devices
Metadata
Other Sources
Archive
News Agencies
Stock footage
Internet
Distribution
Terrestrial
Satellite
Cable
Web: Live & VOD
Mobile
Metadata
Sources, Technologies and Architectures
Production
Editing
Colour grading
Subtitles
Metadata
Metadata Input
Archiving
Asset Management
(Predelivery – EPG .. etc)
Delivery
  Metadata
User Content
Security, Asset Management

## Slide 5
Typical Essences, Wrappers, Metadata, etc
METADATA
Structural Metadata SMPTE 377M
MPEG-7
EBU-Core
Descriptive Metadata Scheme - 1 (S380M)
Custom Metadata Scheme Via XML
AS11 1.1/DPP
SMPTE 434 dictionaries
WRAPPERS
AS11 1.1 / DPP
XAVC
Cinema DNG
AVC-Ultra
AVC-LonGOP (RDD 26:2014)
AVC Proxy (RDD 25:2014)
IMF
MXF …
  OPAtom and OP1a
  OP1b; OP1C; Op2a-c; OP3a-c
ESSENCES - Audio, Video
MPEG-2
H.264 .. AVC-Intra
Pro Res
SHQ / NDI
JPEG 2000
DNxHD (VC-3)
DNxRI (HR) (VC-3)
DVCAM
DVCPRO 25 / 50 … HD
AVI-DV
MPEG - 1
MPEG - 2 long GOP and I frame SD and HD
MPEG PS, TS
MPEG - 4
AES3
  (S302M, S331M PCM, Dolby-E)
AIFF
Wave / BWF
AAC
Codecs –
Acquisition
Mezzanine
Distribution

## Slide 6
Workflow – From Traditional to Next Gen TV
Recent Developments in the Media Industry (and specifically TV)
Main technologues
  UHD / 4K … 8K
  HDR
  video compression
  storage
  bandwidth
New services
  Digital Media / Multi Platform
  Multi-screen
  Interaction and personalisation
    Multi-sourced inputs in real time
    Multiple potential outcomes of programme
    Ingest of social media for playout
      Requirement for information and metadata
    ... to describe all constituent actors and objects in the programme
    ... their position and movement
    ... their relevance to the end user
    ... integration of content with other events and media
    ... Advertising and placement integrated in to the content
    ... 360º video
    ... VR / TV
    ... assisted TV, accessibility

## Slide 7
Contribution and
Distribution

## Slide 8
Contribution and Distribution

## Slide 9
http://www.cisco.com/c/en/us/solutions/service-provider/distribution/index.html#
Production Contribution Distribution Consumption
Contribution and Distribution

## Slide 10
Contribution (distinct from Distribution) - Transport of media content
- video, audio, metadata, and ancillary data - between professional users
  ingest
  capture and production activities
Key aspects for contribution
Picture quality
Latency
  prime importance for contribution
  end to end delay - encoding and decoding process
  less important for distribution
    distribution emphasis: maximizing picture within the available bit rate
Synchronisation →
Encryption →
http://cable.doit.wisc.edu/SMPTE/01-Compression%20for%20IPTV/Trow.TP.01-14-2008.pdf
Contribution and Distribution

## Slide 11
Synchronisation
close audio / video sync needed in production environment
  tolerances -
    -5 to +15ms = “lip-sync”
    relaxed in contribution applications ~ -5 to +30ms)
c.f. Distribution applications
    tolerances significantly relaxed
    lip-sync acceptable -40 to +60ms limits
Encryption
contribution
  - limited number of encryption standards
distribution
  - wide array of encryption and entitlement schemes being commonly used
Contribution Quality

## Slide 12
According to DVB Commercial Module:
Quantified as equivalent to uncompressed or very mildly compressed source material
  assumed that the material is full frame rate
  usually 4:2:2 chroma-subsampling sampling
Compare to:
Broadcast Quality
  equivalent to Satellite, Terrestrial and Cable broadcast
  full frame rate but at a quality not assumed appropriate for contribution applications
Good Quality
  commercially acceptable quality
  not considered acceptable for contribution except as a last resort
  or for fast response news applications
  not necessarily full frame rate
Acceptable Quality
  commercially acceptable for low data rate applications
Mobile Phone Quality
  equivalent to CIF and QCIF resolutions (phones, etc)
  (but more HD phones now)
Contribution Quality
CIF - Common Intermediate Format - resolution of 352 × 288
QCIF - Quarter CIF

## Slide 13
ACQUISITION
LOGGING
INGEST
MEDIA
STORE
DELIVERY
PRODUCTION
SCHEDULE
CREATION
ARCHIVE
AUTOMATION
& PLAYOUT
EPG
CREATION
CODING
&
MULTIPLEX
INTERNET
Streaming
Encoding
iPlayer
Website
CDN
Live Feeds
Studios
OBs
Low end /
Domestic
Camcorders /
DSLRs
News
Camcorders
Hi-End
Camcorders
Digital
Cinema
Cameras +
Recorders
Multi-
Camera
Studio / OB
Other
Material
Data
Input
Data
Input
Data Store
Database
Edit
Grading
Graphics
Effects
Audio
Dubbing
Broadcast and Production Workflow (BBC Schematic)
Media
Metadata
Both
Transmission

## Slide 14
ACQUISITION
LOGGING
INGEST
MEDIA
STORE
DELIVERY
PRODUCTION
SCHEDULE
CREATION
ARCHIVE
AUTOMATION
& PLAYOUT
EPG
CREATION
CODING
&
MULTIPLEX
INTERNET
Streaming
Encoding
iPlayer
Website
CDN
Live Feeds
Studios
OBs
Low end /
Domestic
Camcorders /
DSLRs
News
Camcorders
Hi-End
Camcorders
Digital
Cinema
Cameras +
Recorders
Multi-
Camera
Studio / OB
Other
Material
Data
Input
Data
Input
Data Store
Database
Edit
Grading
Graphics
Effects
Audio
Dubbing
Broadcast and Production Workflow (BBC Schematic)
Media
Metadata
Both
Transmission
Implementation ...
“IP Studio”, maybe ...
  … from SDI / Traditional Workflow Suites
  … to Commodity COTS
NMOS ( FIMS ?)
??? ROI, Integration, Interoperability,
Flexibility, Scale Investment, future proof, standards, skills ..

## Slide 15
Overview of
many / some of
Workflow Processes

## Slide 16
http://www.snellgroup.com/documents/brochures/automation-and-media-management/Momentum.pdf
Workflow Processes
Typical – there are many variations ...
... and automated:

## Slide 17
MEDIA ASSET MANAGEMENT
BPM: Business Process Management (“Workflow Engine”)
Database

## Slide 18
Preferred approach - file-folder structure
accessible via a standard network protocol (rather than a proprietary interface between the storage and the asset management system)
Typical MAM File System Approach
File 1: DISK H1 … written today
File 2: LTO L3
File 3: DISK H4 … being copied to LTO L2
File 4: LTO L2
File 5: DISK H3 … written last hour
File 1: LTO L7
File 2: LTO L5
File 3: DISK H2
File 4: LTO L1 being copied back to disk (due to recent read attempt)
+ access to other cloud storages (own, third party)

## Slide 19
General specifications |  |  |  | 
Tape type | Raw capacity (compressed capacity @ 2.5:1) | Max Uncompressed Speed MB/s (note bytes) | WORM | Released
LTO-1 | 100 GB | 20 | No | 2000
LTO-2 | 200 GB | 40 | No | 2003
LTO-3 | 400 GB | 80 | Yes | 2005
LTO-4 | 800 GB | 120 | Yes | 2007
LTO-5 | 1.5 TB | 140 | Yes | 2010
LTO-6 | 2.5 TB 6.25 TB | 160 | Yes | 2012
LTO-7 | 6.4 TB 16 TB | 315 | Yes | 2015
LTO-8 | 12.0 TB 30 TB | 472 (upto 900Mb/s) | Yes | Now
LTO-9 | 26 TB 65.2 TB | 708 | Planned | TBA
LTO-10 | 48 TB 120 TB | 1100 | Planned | TBA
Linear Tape Open – to LTO 10
Note comparative native / compressed capacities
(2014 … )
Sony Tape @ 148Gb/in2
… 185TB per cartridge

## Slide 20
Tiered Archival Storage
http://perpetualstorage.com/need-right-data-right-place/ [as at 2013]
(i.e. sustainable)
Tiered storage utilizing tape
reducing power
cooling
space
media and administration costs
efficient access via LTFS indexing
infrastructure cost reduction
The Economics of Tiered Archival Storage

## Slide 21
Cloud Archival
Storage of an organization’s
media assets:
original content
EDLs
finished masters
copies
versions
releases, etc
Cloud-based storage being used for
ingest and content collection
playout from the cloud
processing in a virtual environment
.. so what is the need (and issues) for storage in the cloud ?
Cloud concerns
storage alternatives
tier-based migration
automated management
Storage alternatives
Backup or archive
On-prem or in co-lo
Private, hybrid or public cloud

## Slide 22
MXF – Material eXchange Format
wrapper
interchange of finished / almost finished audiovisual material
+ metadata
AAF – Advanced Authoring Format
wrapper – essence + metadata
post-production stages

## Slide 23
Advanced Authoring Format (AAF)
digital nonlinear post production and authoring
“Super-EDL”
supports essence + associated metadata
  provide cross-platform interchange
    of metadata or program content
  track history of program content
    from source elements through final production
  content to be described as a media object

## Slide 24
MXF – Material eXchange Format
e.g. clip composed from a pair of recordings
  MXF file has -
    2 File Packages and
    1 Material Package (instructs decoder how to play the packages)
Material Packages
desired output timeline
File Packages
represent the
source material

## Slide 25
AS-02 – typically in TV broadcast
VERSIONING

## Slide 26
IMF - Interoperable Master Format
High Quality Multi Version Masters for Studio Applications
Typically in the Film Industry
Versioning - IMF

## Slide 27
https://www.smpte.org/PDA_On-demand/IMF (1h 09m)
IMF - Interoperable Master Format

## Slide 28
IP Workflows
SMPTE 2022, 2110

## Slide 29
Why IP is replacing SDI*
Universal connectivity (broadcast and other industries)
Lower budgets, higher quality requirements
Production companies scaling:
  IP allows best production talent remains in a central location
  Receive camera feeds from remote locations
Democratise the industry
  single producer can have many camera inputs from anywhere in the world
  * although SDI is still in development
IP Workflows

## Slide 30
https://www.smpte.org/sites/default/files/section-files/GVExpo2018%20SMPTE%2004%20-%20Scalable%20Facilities%20with%20ST%202110%20-%20Mailhot.pdf
In SDI Routing, all routing in the SDI crosspoint frame
The Control System tells the crosspointwhat to switch where
The Crosspoint Router switches everything internally
Receivers just receive all data sent to them
In IP Routing, the Receiver is involved …
Control System tells the Receiver:
  What Multicast Group & Port# to switch to (Main and Protect)
  Technical Metadata of the new stream
  The Receiver is responsible for how it switches/transitions to it
  The Receiver asks the network for the new signal
  The network provides the new signal through packet forwarding logic
How is IP Television Routing Different from SDI ?

## Slide 31
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
Traditional Broadcast and Media Routing

## Slide 32
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
IP World of Broadcast and Media Routing

## Slide 33
SMPTE ST 2022-6 (Multiplexed Streams)
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017

## Slide 34
Slide from Phil Myers, Snell Advanced Media, SMPTE presentation, BCU. 2017
SMPTE ST 2110 – Essence Streams

## Slide 35
Workflow
.. next …

## Slide 36
Metadata …
Semantics and Workflow

## Slide 37
Service Based Workflow - SOA / FIMS / Microservices
MJDrouin, VSF
Having split workflow into services …
Can outsource it and grow utilisation of third part sevices
… into the cloud ..
Could be another operational model for MXF?
Broadcaster flexibility in whether / or not to invest in infrastructure
Microservices

## Slide 38
Service Based Workflow ... cloud based
MJDrouin, VSF

## Slide 39
Bundled (Audio, Video, Metadata together)
Audio/Video/Metadata/Sync travel coherently
Requires extra work to “unpack” separate essences
SMPTE ST 2022-6 - IP Packetisation of SDI Raster
One IP Address
Video
+ Audio
+ Metadata

## Slide 40
Essence Based (Audio, Video, Metadata separate)
Suited for Studio/Production workflows
Individual essence kept in sync using PTP timing
No blanking!
ST 2110 – Essence-Based Approach
IP Address #1
Video
IP Address #2
Audio
IP Address #3
Metadata
IP Packetisation of Active Video
IP Packetisation of Audio Channels
IP Packetisation of ANC Data
IETF RFC 4175
AES-67
IETF ANC291

## Slide 41
https://youtu.be/K3dn5gQYyw4
The business case for delivery and control standards in program workflows - Bruce Devlin, 2014
A historical perspective leading to Digital Delivery, but a highly relevant argument of various interoperable developments across the industry
(at 11m15 there’s a section on FIMS: FIMS is becoming less relevant, but the underlying issue is still important – note my comments in class)