## Slide 1
Broadcast Technology UG1
9: DVB, Compression Intro, TS, PS
Jerry Foss
jeremy.foss@bcu.ac.uk
DVB, COMPRESSION INTRO, TS, PS:
DVB
MPEG compression (Intro)
PS,TS, Streaming
IP Workflows

## Slide 2
MPEG Systems
Multiplexes
Program Streams
Transport Streams
Statistical Multiplexing
DVB
Streaming
HTTP
ABR, DASH
SDI and IP
SMPTE 2022, 2110
Networks
TDM
Circuit Switching
Packet Switching
Layers of Networks
Telephone, Internet, WWW
This Session:

## Slide 3
From Circuits …
… to Packets

## Slide 4
Traditional PSTN - Digitisation of the Network
Local Exchange
Trunk / Transit
Exchanges
Digital Network
Traditional 4KHz channels
... digitized to 8bit 64kb/s channels
10110011
10110011

## Slide 5
Time Division Multiplex
4kHz voice
sampled at 8kHz
into 8 bits binary
10110011
01010010
10010001
time
time
amplitude
amplitude

## Slide 6
01010010
01001001
10010001
010100101
010100101
10010001
01001001
010100101
010100101
01001001
010100101
Time Division Multiplex
30 channels of speech into a time-divided-multiplex
TS1 TS2 TS3 TS4 TS5 TS6 TS7 TS8 ………………………………………………………………….
Analogue – Digital: Samples are dropped into allocated timeslot for each frame
TS6 previous frame
TS6 this frame
TS6 next frame
Many phone calls at the same time allocated to other slots in the multiplex

## Slide 7
Circuit Switching in a Network
http://www.highteck.net/EN/Basic/Internetworking.html
... a waste of resources when there is no data to transmit
economy of circuits ✘
resilience / survivability -
latency ✓

## Slide 8
http://www.highteck.net/EN/Basic/Internetworking.html
Packet Switching in a Network
economy of circuits ✓
resilience / survivability ✓
latency ✘

## Slide 9
Packet Switching
01001001
010100101
010100101
10010001
010100101
01001001
010100101
01001001
010100101
digitised voice
digital data
digital media
01001001
010100101
010100101
10010001
010100101
01001001
010100101
01001001
010100101
internet network link
all traffic – voice, video, data is split into packets
packets are dropped into a bitstream as/when available
  … “statistically multiplexed”
  … the bitstream may not always have enough capacity for all the traffic competing for access
address field - packets routed through network
House / business ethernet (or wireless) LAN

## Slide 10
Flag
Address
Control
Information Field (Payload)
CRC
Flag
start of frame
end of frame
Message in Packets
00010100010101000101101010001001011100010010001100100001000110010011000100100111000111001001

## Slide 11
Layers of Networks
The Carrier Network
Ethernet (Data Link)
Internet
  (+ The Web)
Protocols
Routing

## Slide 12
Telecomm Network
Local Exchanges
Main Switching Centres
Subscribers
Internet Protocol – IP - to carry data, voice and media over telephone networks

## Slide 13
Telephone Network – Internet Overlay
ISP equipment (Internet Service Provider)
ISP
Many ISP’s:
calls routed across telephone network to ISPs’ servers

## Slide 14
Telephone Network
Internet
Layers of Networks
Internet
US, mid ’60’s ARPANET; DOD Universities
data (voice, video, data) is sent in packets
packets are routed around the network individually
“survivable network”
World Wide Web
Services – from servers to clients – data, media, voice
Telephone Network - BT
Internet
World Wide Web
Services – from servers to clients – data, media, voice
Telephone Network – France Telecom
other Telephone Networks … etc

## Slide 15
MPEG Systems
MPEG family
Overviews
MPEG-1, MPEG-2, MPEG-2 Audio, MPEG4
Audio Compression
Compression Usability, Latency
Encoding Architecture
Perceptual Coding: Psychoacoustic Models
Transform Domain Methods, Decoding
Coding, Bit Allocation, Frames
AAC - Advanced Audio Coding
MPEG-4 AAC, Low Delay Coder, Error Resilience,
AAC compared to mp3
Other Formats
Variable Bit Rate

## Slide 16
MPEG
Motion Picture Experts Group
MPEG 1
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), 4, 5,
MPEG 2
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), …
MPEG 3 - originally for HDTV - abandoned
MPEG 4
audio and video coding - parts 1 - 22
MPEG 7
metadata, description
MPEG 21
framework for multimedia content delivery
XML-based; to communicate machine-readable license information
open framework for multimedia applications
"Rights Expression Language"

## Slide 17
Audio and video coding
Parts
1 - Synchronization and multiplexing of video and audio
- transport stream
2 - Compression codec for non-interlaced video signals
3 - Compression codec for perceptual coding of audio signals
- three layers of audio coding options (mp, mp2, mp3)
4 - Procedures for testing conformance
5 - Reference software
video CD format - quality ~ VCR
originally 1.5M bit/second data rates and 352x240 resolution
later up to 4M bit/second
the most compatible format in the MPEG family
only progressive scan video (... so need for MPEG-2)
MPEG-1

## Slide 18
(1994) Audio and video coding
for broadcast - DVB (satellite, cable, DTT, etc), also DVD (with mofifications)
9 Parts, including -
1 - Transport Streams - TS
  to carry digital video and audio in (unreliable) broadcast applications
  Program streams carry audio and/or video data + time stamp data
2 - Video
  similar to MPEG-1
  support for interlaced video
  optimised > 3 Mbit/s; not for low bit-rates (less than 1 Mbit/s)
  backwards compatible to MPEG1
  enhancements - used (to date) in most HDTV transmission systems
3 - Audio
  layers 1, 2, 3
4, 5 - as MPEG-1
7 - Enhanced audio
MPEG-2

## Slide 19
Part 3
new audio encoding (see later...)
low bitrate encoding with halved sampling rate
  MPEG-1 Layer 1/2/3 LSF - low sampling frequency
multichannel encoding with up to 5.1 channels
... backwards compatible -
MPEG-1 audio decoders can decode stereo from MPEG-2 multi-chan audio
MPEG-2 AAC - Part 7
make better use of available bandwidth
  non-backwards-compatible
MPEG-2 Audio

## Slide 20
Requirement:
To transmit Audio and Video compressed data in:
(i) reliable channels – studio, DVD, reliable media (PS)
(ii) transmission in hostile environments (TS)
Allow interchange between these two formats
Video
Audio
Video
Audio
Data
MPEG-2 Transport Mux
Transport Stream, TS
Program Stream, PS
MPEG-2
Systems Processor
MPEG-2
Systems Processor
MPEG-2
Compressors
MPEG Systems
Decoder
Decoder
Decoder

## Slide 21
Transport Stream Multiplex
A
D
V
SI
etc
A
D
V
SI
etc
A
D
V
SI
etc
A
D
V
SI
etc
Multiplex
A
V
V
V
V
D
SI
V
V
Adaption Field
Payload
Packet Header
188 Bytes
4 Bytes
Transport Steam: Composed of A number of Program Streams (and their Elementary Streams)
when MPEG-2 content is to be distributed / networked, Transport streams are the structure
they are a multiplex of PESs
i.e. carry a number of programmes
MPEG-2Transport Stream
Transport Stream Multiplex consists entirely of short, fixed length transport packets
SI = Service Information
FEC

## Slide 22
Time stamping system
to ensure that related elementary streams are replayed in synchronism at a decoder
Tables of service information
network parameters, programmes within the multiplex and the nature of the various elementary streams
Conditional Access
Allow control of scrambling of one or more elementary streams (but CA not specified by MPEG)
Private Data
i.e. not spec’d by MPEG - include network management data, teletext, etc
MPEG-2
Multiplexer
Elementary Streams
Elementary Streams
Elementary Streams
Elementary Streams
Service Information
Synchronisation
Conditional Access
Channel Adapter
& Modulation
Data rate
No constraints, but must at least equal the total of the combined data rates of the contributing elementary streams
Fixed or variable data rate; may contain fixed or variable data rate elementary streams
Not specified:
error protection, modulation technique, physical layer technologies
Output - a contiguous stream of 8-bit-wide data bytes
e.g. a Freeview Multiplex of ~ 6 TV channels and some radio channels
Private Data
Transport Stream Multiplex

## Slide 23
Video Presentation Units: Raw video coding at discrete time intervals
MPEG-2 Packets and Multiplexes
audio and video data can be exchanged between TS and PS at PES level
Audio
Encoder
Video
Encoder
Packetiser
Packetiser
TS Multiplexer
PS Multiplexer
Transport Stream
(TS)
Program Stream
(PS)
Access Units (AU)
Audio Elementary Stream
Access Units (AU)
Video Elementary Stream
Audio PES
Video PES
Scope of MPEG-2 Systems Standard
Clock
Audio Presentation Units: 24mS of Raw uncompressed audio

## Slide 24
Video Elementary Stream
Compressed
I-Picture
~100KB
Video Presentation Unit
625 lines
4:2:2
=830KB
Picture 830KB
Picture 830KB
Picture 830KB
Picture 830KB
Compressed
B-Picture
~ 12KB
Compressed
B-Picture
~ 12KB
Access Units
Video Elementary Stream - figures for SD video and compression of approx 5Mb/s
Compressed
P-Picture
~ 33KB
Uncompressed Digital Video Stream
Compression: Raw → DCT → I, P, B

## Slide 25
Elementary Stream - ES - sub-divided – packetised
⇒"Packetized Elementary Stream“ = PES
  fixed-size chunks without regard for access unit boundaries
Packetizing
PS: Many packets Form PS Packs
TS: TS packets, 188B

## Slide 26
MPEG-2 – PES ⇒ PS Packs and TS Packets
PS
Pack
Pack
Pack
Program end code
........................
Pack
Header
PES
Pack
PES
PES
PES
...................
PES
PES
Header
PES payload
TS
Header
TS payload
TS
Header
TS payload
TS Packet
PID =m
TS Packet
PID = k
TS Packet
PID = m
TS Packet
PID = h
TS Packet
PID = k
.................................
188 bytes
188 bytes
188 bytes
188 bytes
188 bytes
TS
Packet
TS
Pack

## Slide 27
MPEG-2 - Packet Multiplexing, Video, Audio, Data Streams
PS
Pack
Pack
Pack
Program end code
........................
Pack
Header
PES
Pack
PES
PES
PES
...................
PES
PES
Header
PES payload
TS
Header
TS payload
TS
Header
TS payload
TS Packet
PID =m
TS Packet
PID = k
TS Packet
PID = m
TS Packet
PID = h
TS Packet
PID = k
.................................
188 bytes
188 bytes
188 bytes
188 bytes
188 bytes
TS
Packet
TS
Packets multiplexed
efficient and flexible
allows for conversion PS ↔ TS
Transport Stream – TS
for channels with likely errors
short fixed-length: 188B
PES packets – long variable length
  Sub-divided
  carried as payload of TS packets
Program Steam - PS
for transmission and storage in error-free channels
PES - long variable-length packets
... into variable length packs
    multiple PES packets
... of nearly equal length
(video and audio)

## Slide 29
DVB - Digital Video Broadcasting
Standards
Satellite DVB-S, DVB-S2, SH
Cable DVB-C, DVB-C2
DTT DVB-T, DVB-T2
DTT for handhelds DVB-H, DVB-H2
IPTV DVB-IPTV
DASH DVB-DASH
DVB-3DTV - Frame Compatible Plano-Stereoscopic 3DTV
DVB-C2 - 2nd Generation Cable Transmission
DVB-CID - Carrier Identification for Satellite Transmission
DVB-CPCM - Content Protection and Copy Management
DVB-FF - DVB File Format
DVB-GEM - Globally Executable MHP
DVB-GSE - Generic Stream Encapsulation
DVB-H - Broadcasting to Handheld Devices
DVB-IPDC - Internet Protocol Datacasting
DVB-IPTV - Internet Protocol Television
DVB-MHP - Open Middleware for Interactive TV
DVB-PCF - Portable Content Format
DVB-RCS2 - Return Channel Satellite
DVB-RCT - Return Channel Terrestrial (03/2001)
DVB-S2 - 2nd Generation Satellite Broadcasting
DVB-SH - Satellite Services to Handheld Devices
DVB-T - Digital Terrestrial Television
DVB-T2 - 2nd Generation Terrestrial Broadcasting
DVB - Emergency Warning System
DVB Project - An Introduction
Hierarchical Modulation in DVB-T (03/2000)
plus many others (inc addenda, etc) …
Industry Organisation
Standardisation Process –
Joint Technical Committee (JTC) of:
ETSI - European Telecommunications Standards Institute
CENELEC - European Committee for Electrotechnical Standardization CENELEC
EBU - European Broadcasting Union
Note standards refer to other standards and patents, e.g. MPEG
http://www.dvb.org/standards/factsheets

## Slide 30
Digital Terrestrial TV (DTT)
Advanced Television Systems Committee - ATSC-8VSB
Modulation: 8VSB: 8-level Vestigial Sideband
American Continent
MPEG2-TS
Digital Video Broadcast, Terrestrial Television - DVB-T
Europe; also DVB-S for Satellite, DVB-C for Cable; DVB-H for handhelds
MPEG2 format; also
Integrated Services Digital Broadcasting, Television - ISDB-T
Japan; also ISDB-S for Satellite, ISDB-C for CableTV
MPEG2 format
Modulation: PSK, COFDM/PSK/QAM

## Slide 31
DVB Specifies …
Specifies - essentially a layer one protocol for transport with Data Link (Transport Streams, GSE, etc)
Including -
Input Interface
usually Transport Streams - i.e. TV
Generic Stream Encapsulation – e.g. IP
Modes
Variable Coding and Modulation
Adaptive Coding and Modulation
FEC
e.g. DVB-T2: LDCP, BCH ½. 3/5. 2/3. ¾. 4/5. 5/6
Modulation
e.g. DVB-T2: OFDM
Modulation Schemes
Q/8/16/32PSK, QAM
e.g. DVB-C2: 16-4096QAM
Guard Interval
e.g. DVB-T2: 1/4, 19/256, 1/8, 19/128, 1/16, 1/32, 1/128 (fractions of a symbol)
Interleaving
Bit- Time- and Frequency-Interleaving

## Slide 32
Transport Stream Multiplex
Transmission:
Terrestrial
Cable
Satellite
Broadband
Program Streams

## Slide 33
MPEG
Motion Picture Experts Group
MPEG 1
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), 4, 5,
MPEG 2
audio and video coding - parts 1, 2, 3 (layers 1, 2, 3), …
MPEG 3 - originally for HDTV - abandoned
MPEG 4
audio and video coding - parts 1 - 22
MPEG 7
metadata, description
MPEG 21
framework for multimedia content delivery
XML-based; to communicate machine-readable license information
open framework for multimedia applications
"Rights Expression Language"

## Slide 34
Compression
- Introduction

## Slide 35: Why Compress Video
Size of uncompressed 1080p HDTV
  1920 * 1080 ≈ 2 Mpixels per frame
For RGB this is 6MB per frame
  Thus 1 second of video needs
  25 *6MB = 150MB
  Data rate of 150 *8 = 1200 Mbps = 1.2 Gbps
  One hour of video needs 3600*150 MB
= 540,000 MB = 540 GB

## Slide 36: Why Compress Audio?
CD quality = 2* 44.1 *16 Kbps ≈ 1.4 Mbps
  About 1/850 of HDTV video
1 hour of audio needs 3600* 1.4 /8 = 630 MB
  100 tracks take about 360 minutes ≈ 4 GB

## Slide 37: Compression – Information Theory
IF …
image is all the same colour
  very easy to compress - just replace with colour value and codeword to indicate
every pixel is a random number between 0 & 255 and not correlated in any way with other pixels
  it is impossible to compress
In between -
look for patterns only for lossless compression
additionally psychovisual characteristics for lossy compression

## Slide 38: Compressed and Uncompressed Images
raster
image
display
processing
time
display
compressed
image
processing
time

## Slide 39: Lossless Compression (of Images)
Three standard techniques that take advantage of regular and repeating data
  Run Length Encoding (RLE)
  Huffman Compression
  Differential (or Predictive) Coding
ironically in their pure form they are most suited to compression of bitmap representations of computer generated images

## Slide 40: Lossless Compression
RLE replaces repeating bytes with number and kind:
  e.g.777555555 becomes 3765
  compression ratio 9:4 =2.25
In most applications RLE files are further compressed using Huffman which scans the whole file to discover the most frequently occurring bytes. These bytes are then translated to bit form, for example using only 1 bit for the most frequently occurring byte , 2 bits for the next most frequently occurring and so on

## Slide 41
Bit Rate Reduction Principles
Main process of bit-rate reduction:
Remove lower priority information from the signal at encoder
  ... according to what we perceive in the image
Coding - including information about the bit-rate reduction
  ... codec at time of image capture
Decode - to assemble and play the compressed file
  ... codec at time of viewing image

## Slide 42
Audio Compression (Introduction)

## Slide 43
Audio Compression
Audio Compression
Compression Usability, Latency
Encoding Architecture
Perceptual Coding: Psychoacoustic Models
Transform Domain Methods, Decoding
Coding, Bit Allocation, Frames
AAC - Advanced Audio Coding
MPEG-4 AAC, Low Delay Coder, Error Resilience,
Variable Bit Rate

## Slide 44
The Physiology of Hearing
Ossicles
Auditory Nerve
Cochlea
Tympanic Membrane
Auditory Canal
acts as a closed tube resonator
enhances sounds in the range 2-5 KHz
Pinna
presents larger area to received sound energy
“collects” sound – like a preamplifier
Stirrup
low + high frequencies

## Slide 45
High frequency sounds
The Physiology of Hearing – The Cochlea
schematic view - unroll the cochlea - distribution of sensitive hair cells
nerve endings
hair cells
incoming sounds
Lower frequencies

## Slide 46
http://www.hitl.washington.edu/publications/hollander/2.html
low + high frequencies
The Physiology of Hearing – The Cochlea

## Slide 47
Two signals within a critical band - closely related in frequency
stimulate the same area of the membrane in the cochlea
these two sounds added together don’t give twice the loudness
Two signals - frequencies separated
stimulate the different areas of the membrane in the cochlea
not competing for the same nerve endings
give an appreciable increase of perceived intensity
The Physiology of Hearing
freq
freq
freq
critical band
critical band
critical bands

## Slide 48
Threshold of Hearing, Masking Threshold

## Slide 49
MPEG Psychoacoustic Models
MPEG standard defines two models:
Psychoacoustic Model 1:
  simpler, less computationally expensive
  serious compromises in what it assumes a listener cannot hear
Psychoacoustic Model 2:
  More features
    more complex coding (assuming increased processor bandwidth)
  Layer III (.mp3)

## Slide 50
Video Compression (Introduction)

## Slide 51
The Eye
The Eye
The Eye

## Slide 52
Receptors
… Rods and Cones
http://www.cellsignallingbiology.org/csb/010/csb010fig10_rod_and_cone_structure.htm

## Slide 53
Psychovisual – how we perceive images
Light sensitivity in the eye
Rods - light intensity - not colour
~125 million across the retina
characteristics of high speed black & white film
Cones - colour - responsive in three wavebands
6 or 7 million cones
characteristics of low-speed colour film
RODS and CONES
(retina)
... Chroma Sub-sampling

## Slide 54
Images Captured on a Camera
Image captured on red blue and green – responsive photo-sites
each pixel is represented by R, B, G
each pixel has its own value of light intensity
Original captured image at camera sensor:

## Slide 55
RGB to Y,Cb,Cr
RGB pixel format … … … is converted to … … … Y,Cb,Cr
where
Y = luminance (light intensity)
Cb, Cr = colour information
Weighted RGB converted to Y Cb, Cr
0.2989*R + 0.5870*G + 0.1140*B
Cr
Cb
Y
During the encoding stage ...

## Slide 56
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma

## Slide 57
RGB to Y,Cb,Cr – each pixel
Weighted RGB luminance:
approx 29% Red + 59% Green + 11% Blue
similarly,
Cr = R – Y
= -
Cb = B – Y
i.e. 8 bits of Cb (0-255)
value of Cb:
value of original Blue
minus
value of luma
= -
e.g.
= 210 - 90
Overall luminance
i.e. greyscale, monochrome
of this pixel
= Y, ... i.e. the luma
1111000
11010010
01011010

## Slide 58
Y,Cb,Cr – for image of x x y pixels in “4:4:4”
x pixels
y pixels

## Slide 59
Y,Cb,Cr – Chroma Sub-sampled to “4:1:1”
x pixels
y pixels
Reason: To greatly reduce the amount of data
Rationale: The eye’s resolution of luminance is greater than for colour

## Slide 60
YCbCr
Colour Space: Y = Luminence Information; Cr, Cb = Chrominance Information
Derived from RGB (gamma corrected)
Y is dominant information; RGB colour info derived from Y, Cr, Cb relationships
  (simplified): Cb = B-Y ; Cr = R-Y
Cr
Cb
Y
Original image
Y,Cb,Cr

## Slide 61
Cr
Cb
Y
Cr
Cb
Y
RGB to Y,Cr,Cb
i.e. there are now three mappings of the original RGB image:
Y: Luminance intensity
Cb: Intensity of the values of
[B minus Y]
Cr: Intensity of the values of
[R minus Y]

## Slide 62
Reception / Decoding
Decoding, reverse process ...
  from Chroma sub-sampled to full RGB
note – interpolating lost information
∴ detail is lost in the process
Perceptual (e.g. MPEG, etc ) encoding + decoding is also part of this process and loses a lot more detail
... more later in the module
encoding process
decoding process

## Slide 63
MPEG –
Coding For
Moving Images
Intraframe and Interframe Compression

## Slide 64
Video Sequence
Group Of Pictures (GOP)
GOPs – Groups Of Pictures
Group of Pictures (GOP)
Header + series of one of more pictures
3 types of pictures: I, P, B
Provides a regular structure of video content
  recurring pattern of pictures
  allow easy access to the video stream
For TV the GOP is 12 pictures ( 0.5 s of a projected at 24 frames / s movie
For NTSC 30 fps, uses 15 pictures

## Slide 65
Basic Principles for Moving Elements in Images
Blocks Identical or nearly-identical in following frames
Blocks with nearly* identical characteristics are replicated; spatial displacement is coded with a motion vector
*we’ll deal with the “nearly” part shortly …

## Slide 66
Difference Coding
Amount of information in the difference between the two frames is a lot less than in Frame 2
motion in the scene will increase the differences
analyse motion
  … where each block moved since previous frame
  encode motion as vector -
    x- and y- direction vectors
  encode differences for the moved block like a jpg,
  i.e. DCT, quantization, RLE (zig-zag), Huffman
  (… but this jpeg is very simple to encode due to little changed information in the image)
see - http://www.cs.ucl.ac.uk/teaching/GZ05/08-h261.pdf

## Slide 67
Codecs –
Current, Emerging: Tensions in the Market

## Slide 68
Codecs – Current, Emerging, Tensions in the Market
New formats - AV1, VVC, EVC, and NDI
Rising video consumption
more immersive higher resolution TV
major new family of video compression standards from
  MPEG + ITU-T Study Group 16’s VCEG
  (Video Coding Experts Group)
Undermining of MPEG HEVC by some of its own patent holders
  ⇨ traditional codecs versus potentially disruptive alternatives
Cost for distributing video is a major factor
  - especially in IP nets (the quality is compressed)

## Slide 69
Codecs – Current, Emerging, Tensions in the Market
Current market
AVC/H.264 codec
  old, popular, widespread decoder support, well-functioning licensing situation
HEVC - adoption low in streaming …
HEVC Advance (licensing admin)
licensing cost issues
slow take-up in key market segments
⇨ Rival codecs - better performance / royalty free / or both
Patent holders had technology accepted before declaring rights and costs in the patent pools
  further fragmented by HEVC IP holders

## Slide 70
Codecs – Current, Emerging, Tensions in the Market
The “Tax on distribution”
MPEG LA - charges per decoding units capped at U$25m a year
HEVC Advance caps annual unit charge at U$40m
  demands royalties for streaming, capped at U$5m a year
other HEVC IP owners - Nokia and Technicolor late to join a pool or announce royalty policy
HEVC royalties significantly more expensive than H.264

## Slide 71
Codecs – Current, Emerging, Tensions in the Market
Emerging … AV1
Royalty-free (but not yet contested in court … )
Based on VP9
  Alliance for Open Media (AOMedia) (BBC R&D is a member)
Few well-conducted comparisons between AV1 <> HEVC
  HEVC supporters say HEVC is 30% better than AV1
  AV1 supporters say AV1 is 40% better than HEVC
  (see later in these slides …)
AV1 - significantly more complex encoder to achieve performance
  ... so not good for real time

## Slide 72
Codecs – Current, Emerging, Tensions in the Market
Joint Video Exploration Team (JVET) – VVC
Versatile Video Coding (VVC)
MPEG – collaborate with ISO and ITU-VCEG (Video Coding Experts Group):
formed JVET
  new suite of video coding technologies
  basing its work on HEVC
BBC R&D (Marta Mrak):
  “HEVC and AV1 are similar; VCC 30% better”
UHD bitrates similar to current HDTV; storage: 2x as much

## Slide 73
Bitmovin - AV1 will be standard for future content - hi res, VR and AR
Others say - new codec needed
data demands of 5G - ultra-high bandwidth low latency streaming - VR, 8K - need a new codec - AV1 is not designed for that
Codecs – Current, Emerging, Tensions in the Market

## Slide 74
Codecs – Current, Emerging, Tensions in the Market
EVC - Essential Video Coding
MPEG-5
Extensible from Royalty free basic profiles
to
licensed more complex profiles
also …
NewTek
NDI – Royalty Free s/w standard for video device intercommunication
ND1- Codec - Low latency, ~4:1 UHD

## Slide 75
Streaming
HTTP, HLS
  MPEG-DASH
RTP/RTSP

## Slide 76
The original solution for streaming
  ... overtaken by RTP/RTSP based for large IPTV deployments
  ... more recently back in favour
used generic HTTP servers (often based on Apache or Windows Server)
HTTP Streaming
Early days
Limited bandwidth available
    “Download and play”
        no lookahead seeking or random access
      Multiple viewers – server bandwidth issues
Apple introduce progressive download

## Slide 77
HTTP server/client – stateless
  HTTP-streaming: retrieves consecutive short chunks on as-needed basis
      little waste (the video is delivered as it is watched)
          server efficiently serves more streams
      Random seeking
        (viewer selects – player retrieves the appropriate chunks)
    firewall friendly
    can utilise HTTP caching mechanisms
    less expensive to implement (no streaming server required)
      scale more cheaply and effectively to serve available users
Streaming Media Protocols – HTTP addresses RTMP Issues
RTMP/RTSP/HTTP – state of the market
little impetus for RTMP/RTSP sites to change –still widely used
new installations - overwhelming view – HTTP
in fact most video content is delivered via plain old HTTP progressive download

## Slide 78
Client
Server
http GET
http GET
Segment timing:
10 seconds = reasonable balance for most broadcast content
Shorter segments
= more frequent refreshes of the index file
.. unnecessary network overhead for the client
Longer segments
= latency and initial startup time
Media Formats
e.g. video: H.264 / VP9,
  audio: .aac / Opus, etc
  video + audio file segments unwrapped
  … but certain applications –
  can be wrapped in MPEG-TS (DVB)
Audio segment
Video segment
etc
HTTP Streaming

## Slide 79
HTTP Live Streaming - HLS
Apple (part of QuickTime and iOS)
HLS v5 announced in Sept16
support for Fragmented MP4

## Slide 80
MPEG-DASH
Dynamic Adaptive Streaming over HTTP
http://www.streamingmedia.com/Articles/ReadArticle.aspx?ArticleID=79041
Background
(commercial) audio/video was typically transported over RTP/UDP
  (but streaming proprietary solutions based HTTP/TCP)
HTTP streaming - good - provided that the increased latency is acceptable
Benefits:
Firewall and NAT traversal (c.f. services based on RTP/UDP)
Widely deployed network caches (CDNs)
  Deployment of CDN caches can be kept simple
Complexity (adaptation) moved to client
Servers are agnostic to delivered content
network resources / configuration may vary over time

## Slide 81
MPEG-DASH
DASH client obtains the MPD …
MPD (Media Presentation Description) –
XML document
  delivered using HTTP or other transport
describes media data available at the servers
allows clients to select the data
defines segments available
can either be
  initialization segments - initialization data for decoding
  media segments
segment format based on MPEG2-TS
  Using ISO base Media File Format (ISOBMFF - general structure for time-based media
  (however, segments based on other formats can be specified)