## Slide 1
Broadcast Technology UG1
9: DVB, Compression Intro, TS, PS
Jerry Foss
jeremy.foss@bcu.ac.uk
DVB, COMPRESSION INTRO, TS, PS:
DVB
MPEG compression
PS,TS

## Slide 2
Media Distribution
The TV Headend
DVB - Digital Video Broadcasting
Transport Stream Multiplex
Distribution Network Archiectures
Satellite
Digital Terrestrial (DTTV)
Cable
HTTP Streaming: MPEG-DASH
Higher Definition
Content Delivery Networks
Media Distribution Platforms

## Slide 3
http://www.cisco.com/c/en/us/solutions/service-provider/distribution/index.html#
Production Contribution Distribution Consumption
Contribution and Distribution

## Slide 4
Media Distribution
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End
Distribution Network
Satellite
Cable
Telco Broadband
Terrestrial TV
Web (OTT)
Mobile

## Slide 5
Media Distribution ... ... Satellite
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Access Equipment
STB, etc
End Users
Video Head-End

## Slide 6
Media Distribution - Digital Terrestrial (DTTV)
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
STB, etc
End Users
Video Head-End

## Slide 7
Media Distribution – Cable
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Cable Network
Video Head-End
Access Network

## Slide 8
Media Distribution – IPTV - Telco Broadband, OTT/Web
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
VOD and
Various
Functions
(Servers, etc)
Video Head-End
Access Network
Telco Broadband

## Slide 9
Media Distribution – IPTV - Telco Broadband, OTT/Web
VOD and
Various
Functions
(Servers, etc)
Access to
WWW
Telephone N/W
Ingest of Media
Network Managed and Operated by Network Provider / Operator
- Routing, Switching, etc
Network Access Equipment
STB, etc
End Users
Network Core
Video Head-End
Access Network
Telco Broadband
OTT
OTT
WEB-BASED VIDEO PROVIDER

## Slide 10
Media Distribution
Broadcast
  but what is “broadcast?”
  … vs On Demand
  (what are “video servers”? – or any other server)
  digital cinema distribution
Streaming:
  DVB – Cable, Satellite, DTTV
  IP-based – IPTV (Telco broadband, OTT)
    http
      MPEG → DASH (dynamic adaptive streaming on http)
      HLS (http live streaming, Apple implemented)
    rtp protocol

## Slide 11
VOD and
Various
Functions
(Servers, etc)
Network Access Equipment
STB, etc
End Users
Video Head-End
Off air
Content
Local
Content
Encoding /
Transcoding
Conditional
Access
EPG
Additional Services
Prepare for
Transmission
modulation, etc
Transmission
Network
cable
satellite
Telco IPTV
Web
Customer
Home
Modem
Set Top Box
  inc CA
TV
Multiplexing
Middleware
Advertisment Inserts
Authentication
DHCP
The Headend (Cable, Satellite, Web, Telco ... )

## Slide 12
DVB - Digital Video Broadcasting
Standards
Satellite DVB-S, DVB-S2, SH
Cable DVB-C, DVB-C2
DTT DVB-T, DVB-T2
DTT for handhelds DVB-H, DVB-H2
DVB-3DTV - Frame Compatible Plano-Stereoscopic 3DTV
DVB-C2 - 2nd Generation Cable Transmission
DVB-CID - Carrier Identification for Satellite Transmission
DVB-CPCM - Content Protection and Copy Management
DVB-FF - DVB File Format
DVB-GEM - Globally Executable MHP
DVB-GSE - Generic Stream Encapsulation
DVB-H - Broadcasting to Handheld Devices
DVB-IPDC - Internet Protocol Datacasting
DVB-IPTV - Internet Protocol Television
DVB-MHP - Open Middleware for Interactive TV
DVB-PCF - Portable Content Format
DVB-RCS2 - Return Channel Satellite
DVB-RCT - Return Channel Terrestrial (03/2001)
DVB-S2 - 2nd Generation Satellite Broadcasting
DVB-SH - Satellite Services to Handheld Devices
DVB-T - Digital Terrestrial Television
DVB-T2 - 2nd Generation Terrestrial Broadcasting
DVB - Emergency Warning System
DVB Project - An Introduction
Hierarchical Modulation in DVB-T (03/2000)
plus many others (inc addenda, etc) …
Industry Organisation
Standardisation Process –
Joint Technical Committee (JTC) of:
ETSI - European Telecommunications Standards Institute
CENELEC - European Committee for Electrotechnical Standardization CENELEC
EBU - European Broadcasting Union
Note standards refer to other standards and patents, e.g. MPEG
http://www.dvb.org/standards/factsheets

## Slide 13
Transport Stream Multiplex
Transmission:
Terrestrial
Cable
Satellite
Broadband
Program Streams

## Slide 14
Ch3
Ch2
Ch1
Transport Stream Multiplex
A
D
V
SI
etc
A
D
V
SI
etc
A
D
V
SI
etc
Multiplex
A
Ch1
V
Ch1
V
Ch3
V
Ch4
V
Ch3
D
Ch2
SI
Ch1
V
Ch1
V
Ch4
SI = Service Information
Several TV channels as video packet streams … H.264/AVC or H.265/HEVC
10010010001001010101110010011001010100010100000.....
Multiplexer
Multiplex

## Slide 15
Distribution Network Architectures

## Slide 16
Digital Terrestrial
TV
(DTTV,
e.g.
Freeview)

## Slide 17
Digital Terrestrial TV (DTTV, e.g. Freeview)
475MHz
850MHz
Ch21
Ch68
48 channels
UHF Band IV, V
7Mhz Channel
contains a number of DVB-T TV channels

## Slide 18
Freeview – Sutton Coldfield Transmissions (9 Multiplexes altogether)
http://www.ukfree.tv/txdetail.php?a=SK113003

## Slide 19
Digital Terrestrial TV (DTTV, e.g. Freeview)
475MHz
850MHz
    – a transport stream modulated on many carriers
Ch21
Ch68
48 channels
UHF Band IV, V
7Mhz Channel
contains a number of DVB-T TV channels

## Slide 20
Multiplexing the Channels
freq
Data is modulated on to each of several carriers
Total data to be transmitted
00100010010101011110010010001001010101110010011001010100010100000.........
Each of these is one carrier with data modulated on to it in Quadrature Amplitude Modulation
(QAM – a mix of amplitude and phase modulation)
All these carriers are separate signals and are all modulated on to one main carrier
A
Ch1
V
Ch1
V
Ch3
V
Ch4
V
Ch3
D
Ch2
SI
Ch1
V
Ch1
V
Ch4

## Slide 21
Satellite Distribution
image from
http://upload.wikimedia.org/wikipedia/en/8/80/Sat_contribution_fig.jpg
Video Headend

## Slide 22
Satellite TV
DBS - Direct Broadcast Satellite; Broadcasting Satellite Service
One-way broadcast
From a communications satellite to an end user
Uplink: large dish 9-12m dia
Receiver - Small round or oval dish antenna < 20" diameter.
Compressed digital signal in the Ku band
  (11-15GHz)
http://www.supersatelliteselection.com/how-satellite-tv-works.html
Reception affected by
  rain
  solar activity

## Slide 23
Geostationary Orbit
appears as a fixed position to an earth-based observer
revolves around the earth at a constant speed once per day over the equator
ground based antennae - no need for expensive tracking equipment
36,000 km
= 22,250 miles
Some satellite data …
SES Astra satellites located at 28.2° east (Astra 2A/2B/2C/2D)
Eutelsat's Eurobird 1 satellite at 28.5°E
receiver dish parameters

## Slide 24
March 2014

## Slide 25
Satellite Transponders
24 x 36MHz channels in 6GHz band
24 x 36MHz transmission channels in 11GHz band
Each Transponder is a separate transceiver or repeater
Each transmission channel is a multiplex of several digital TV channels
(note – bigger transmission channels than DTT
∴ many more TV channels in each multiplex)
http://www.dream.com.ph/howdreamworks/hwd_schematic.asp

## Slide 26
Cable TV

## Slide 27
Hybrid networks:
fibre's reliability and bandwidth benefits
lower cost than a pure fibre network
utilising existing copper plant
HFC network - hybrid fibre-coax network
Combine both optical-fibre and coaxial cable lines.
TAP
TAP
TAP
Fibre Trunk
Coax Trunk
Router
Drop
Branch
Headend
Cable TV
Coaxial cable
- from the optical-fibre feeders to each subscriber's home.
Optical fibre
- from the cable head-end to neighbourhoods of 500 to 2,000 subscribers.
Notes: -----------------------------------------
>> CMTS

## Slide 28
DOCSIS - Data Over Cable Service Interface Specification
The Standard for the interface between the CMTS and the Cable Modem
Developed and licensed by CableLabs
Specifies modulation schemes and protocol
for exchanging signals over cable
to carry MPEG and IP
Interface
DOCSIS
Data
Cable TV – Data and TV to the user

## Slide 29
UPSTREAM
to network
DOWNSTREAM
to user
sub-channels
freq
signal
Cable TV – Data and TV to the user

## Slide 30
Telecomms Service Providers (Telco)
Broadband Access

## Slide 31
Telephony
UPSTREAM
DOWNSTREAM
xDSL (ADSL, XDSL)
sub-channels
freq
signal

## Slide 32
WWW
Middleware
VOD Server
Broadcast
Video Head-End
PSTN
Public Service Telephone Network
IP Router
Network
DSLAM
Digital Subscriber’s Line Access Module
Customer Premises
Telco Broadband (IPTV)
Notes: IP services
>>>> - SSw
>>>> - www
>>>> - Walled Garden
>>>> - video headend
>>>> Network
- (MSAN)
IP Router
- ASX4000, BXR 48000
>>>> B-RAS
migrate to edge - to MSAN
[more later]
---------------------
Second Mile - Ethernet

## Slide 33
Walled Garden
WWW
Middleware
VOD Server
Broadcast
Video Head-End
PSTN access
IP Router
Network
DSLAM
Customer Premises
bRAS
VDSL
Ethernet
Fibre
Street
Cabinet

## Slide 34
HTTP Streaming: MPEG-DASH
Content exists on the server in two parts:
  Media Presentation Description (MPD)
    content presentation types, its various alternatives, their URL addresses, etc
  Segments - contain the content bitstreams
    in the form of chunks, in single or multiple files.
Streaming content
from HTTP server
to a DASH client
content stored on HTTP server; delivered using HTTP

## Slide 35
How Much Access Bandwidth? (up to recently ...)
Video (biggest payload)
assume MPEG4 / WM9, say
2x SD streams = 2 x [0.5 ... 1Mbs]
+ 2 x HDTV streams = 2 x [3 … 6Mbs]
= … … … … … … … ~ 10 … 15Mbs
Data
assume RT (or better) download video … ~ 2 … 3 Mbs
Voice
(negligible) ~ …
Total … … … … … … … … < 20Mbs
Contentious figures!
But quite likely
however - UHD, HDR, Frame Rates…
Notes: How much access bandwidth?
- 100Mbs common in far east
- 1Gbs in HK
- (what do they do with it?)
... instantaneous transfer of entire contents of HD
... data back up
====================
Value Model - Players - Introduce some scenarios
-----------------------------------------
Media Industry Models

## Slide 36
Content Delivery Networks

## Slide 37
CDN - to optimize content delivery
infrastructure solutions to network service providers who deploy their own dedicated digital media delivery
asset tracking
network performance
  real-time load
  statistics reporting
Internet - end-to-end
  core network is simple - only forwards data packets
  intelligence is at edges
Content Networking
1 – central server
2 – cache (edge server/cache)
3 – end users

## Slide 38
system of caches containing copies of data
data is distributed at various points in a network
maximizes the bandwidth required to access the data from clients throughout the network
Content Networking
1 – central server
2 – cache (edge server/cache)
3 – end users

## Slide 39
The Cloud
Storage
Processing
Software as a Service (SaaS)
Platform as a Service (PaaS)
Not really a cloud (!)
a facility of servers and processors
may be private owned
may be third party owned
resources rented out
  service level agreements
e.g.
media workflow facilities
video headends
etc …

## Slide 40
Cloud Computing, Amazon Instances
Instance | EC2 Compute Units | Memory (GB) | Instance Storage (GB) | Platform | I/O Performance | Hourly Price
Small | 1 (1 Virtual Core x 1 Compute Unit) | 1.7 | 160 | 32-bit | Moderate | $0.10
Large | 4 (2 Virtual Core x 2 Compute Unit) | 7.5 | 850 | 64-bit | High | $0.40
X-Large | 8 (4 Virtual Core x 2 Compute Unit) | 15 | 1690 | 64-bit | High | $0.80
High-CPU Medium | 5 (2 Virtual Core x 2.5 Compute Unit) | 1.7 | 350 | 32-bit | Moderate | $0.20
High-CPU XL | 20 (8 Virtual Core x 2.5 Compute Unit) | 7 | 1690 | 64-bit | High | $0.80
http://gevaperry.typepad.com/main/2009/03/figuring-out-the-roi-of-infrastructureasaservice.html
(more information at - http://aws.amazon.com/ec2/instance-types )